| CHANGE REQUEST |
| --- |
| Meeting ID:* | PRO34 |
| Source:* | Chonggang Wang, Convida, Wang.Chonggang@ConvidaWireless.Com Dale Seed, Convida, Seed.Dale@ConvidaWireless.Com Bob Flynn, Convida, Flynn.Bob@ConvidaWireless.com |
| Date:* | 2018-03-15 |
| Reason for Change/s:* | Stage-3 protocol details for <crossResourceSubscription> resources and its RESTful operations, which have been defined in TS-0001 V3.7.0 clauses 9.6.58, 9.6.59, 10.2.10.22, 10.2.10.23, 10.2.10.24, 10.2.10.25, 10.2.10.26, and 10.2.10.27. |
| CR against: Release* | Release-3 |
| CR against: WI* | Active <Work Item number> MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004 V3.3.0 |
| Clauses * |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | <TS/TR number>, <Version Number>, and <Description on which aspect should be reflected in this TS/TR> |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

R01 – fix header

R02 – clarifies procedures for <subscription> CREATE/UPDATE related to associatedCrossResourceSub

Removed text related to create/update ACP resources as they are no longer needed.

R03 – moved to PRO 34

R04 – Drafting session changes

Cross-resource subscription as a new feature has been adopted in TS-0001 (V3.7.0), which is supported by the following new attributes, resources, and operations included in TS-0001.

- New attribute associatedCrossResourceSub is introduced to <subscription> resource in clause 9.6.8.

- New  resource <crossResourceSubscription> is described in clause 9.6.58.

  - <crossResourceSubscription> can be a child resource of <CSEBase>, <remoteCSE>, and <AE>

  - <crossResourceSubscription> has a virtual child resource subscriptionLinkDeletion

  - <crossResourceSubscription> has a few new attributes: several of them (i.e. regularResourcesAsTarget, subscriptionsAsTarget, timeWindowSize) will be supported using existing oneM2M simple data type or create new oneM2M simple data type;  one attribute (i.e. timeWindowType) will be supported using a enumeration type; one attribute (i.e. eventNotificationCriteriaSet) will be supported by definiting a new oneM2M complex data type.

  - <crossResourceSubscription> also re-uses a few attributes of <subscription> resource.

- New virtual resource subscriptionLinkDeletion is described in clause 9.6.59

- CRUD operations on <crossResourceSubscription> are described in clauses 10.2.10.22-10.2.10.25

- Cross-resource notification procedure is described in clause 10.2.10.26

- The virtual resource subscriptionLinkDeletion is used to remove a <subscription> resource from the subscriptionResourcesAsTarget attribute of a <crossResourceSubscription> resource. This is described in clause 10.2.10.27

Based on the above resources, attributes, and operations in TS-0001 (V3.7.0), the following changes/updates are proposed in this contribution for cross-resource subscription resource description and operations for TS-0004.

- “7.4.8 Resource Type <subscription>”  is updated since associatedCrossResourceSub is introduced as a new attribute of a <subscription> resource; also, when a <subscription> is deleted, it should be removed from the subscriptionResourcesAsTarget attribute of the associated <crossResourceSubscription> – Change 1.

- New clauses “7.4.X1 Resource Type <crossResourceSubscription>” and “7.4.X2 Resource Type subscriptionLinkDeletion” is added – Change 2, Change 3.

### -----------------------Start of change 1-------------------------------------------

### Resource Type <subscription>

#### 7.4.8.1	Introduction

The <subscription> resource contains subscription information for its subscribed-to resource. The subscription resource is a child of the subscribed to resource.

The detailed description can be found in clause 9.6.8 in TS-0001 [6].

Table 7.4.8.1-1: Data type definition of <subscription> resource

| Data Type ID | File Name | Note |
| --- | --- | --- |
| subscription | CDT-subscription-v3_3_0.xsd |  |

Table 7.4.8.1-2: Universal/Common Attributes of <subscription> resource

| Attribute Name | Request Optionality |
| --- | --- |
|  | Create | Update |
| @resourceName | O | NP |
| resourceType | NP | NP |
| resourceID | NP | NP |
| parentID | NP | NP |
| accessControlPolicyIDs | O | O |
| creationTime | NP | NP |
| expirationTime | O | O |
| lastModifiedTime | NP | NP |
| labels | O | O |
| creator | O | NP |
| dynamicAuthorizationConsultationIDs | O | O |

Table 7.4.8.1-3: Resource Specific Attributes of <subscription> resource

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | Create | Update |  |  |
| eventNotificationCriteria | O | O | m2m:eventNotificationCriteria | Default behaviour is notification on Update_of_Resource |
| expirationCounter | O | O | xs:positiveInteger | No default |
| notificationURI | M | O | list of xs:anyURI | No default |
| groupID | O | O | xs:anyURI | No default |
| notificationForwardingURI | O | O | xs:anyURI | No default |
| batchNotify | O | O | m2m:batchNotify | No default |
| rateLimit | O | O | m2m:rateLimit | No default |
| preSubscriptionNotify | O | NP | xs:positiveInteger | No default |
| pendingNotification | O | O | m2m:pendingNotification | No default |
| notificationStoragePriority | O | O | xs:positiveInteger | No default |
| latestNotify | O | O | xs:boolean | No default |
| notificationContentType | O | O | m2m:notificationContentType | Default value is set to ‘all attributes' |
| notificationEventCat | O | O | m2m:eventCat | No default |
| subscriberURI | O | NP | xs:anyURI | No default |
| associatedCrossResourceSub | O | O | m2m:resourceList | No default. This attribute shall only be modified by a <crossResourceSubscription> Hosting CSE. described in 7.4.X1 |

Table 7.4.8.1-4: Reference of child resources

| Child Resource Type | Child Resource Name | Multiplicity | Ref. to in Resource Type Definition |
| --- | --- | --- | --- |
| <schedule> | notificationSchedule | 0..1 | Clause 7.4.9 |
| <notificationTargetMgmtPolicyRef> | [variable] | 0..n | Clause 7.4.30 |
| <notificationTargetSelfReference> | ntsr | 1 | Clause 7.4.33 |

#### 7.4.8.2	<subscription> resource specific procedure on CRUD operations

##### Create

Originator:

No change from the generic procedures in clause 7.2.2.1.

Receiver:

The following are additional Hosting CSE procedures to the generic resource handling procedures (Figure 7.2.2.2-1 in clause 7.2.2.2). The additional procedures shall be inserted from Recv-6.2 to Recv-6.8 as below.

The resource handling procedure for the Hosting CSE which receives <subscription> CREATE request shall perform the following procedures in order:

- Recv-6.2

- Recv-6.3

- Check if the subscribed-to resource, addressed in To parameter in the Request, is subscribable. Subscribable resource types are defined in TS-0001 [6], they have <subscription> resource types as their child resources.

If it is not subscribable, the Hosting CSE shall return the Notify response primitive with a Response Status Code indicating "TARGET_NOT_SUBSCRIBABLE" error.

- Check if the Originator has privileges for retrieving the subscribed-to resource.

If the Originator does not have the privilege, the Hosting CSE shall return the response primitive with Response Status Code indicating "ORIGINATOR_HAS_NO_PRIVILEGE" error.

- If the notificationURI is not the Originator, the Hosting CSE should send a Notify request primitive to the notificationURI with verificationRequest parameter set as TRUE (See clause 7.5.1.2.2).

  - If the Hosting CSE cannot send the Notify request primitive, the Hosting CSE shall return the Notify response primitive with a Response Status Code indicating "SUBSCRIPTION_VERIFICATION_INITIATION_FAILED" error.

  - If the Hosting CSE sent the primitive, the Hosting CSE shall check if the Notify response primitive contains a Response Status Code indicating "SUBSCRIPTION_CREATOR_HAS_NO_PRIVILEGE" or "SUBSCRIPTION_HOST_HAS_NO_PRIVILEGE error. If so, the Hosting CSE shall return the Create response primitive with a Response Status Code indicating the same error from the Notify response primitive to the Originator.

- Recv-6.4

- Recv-6.5

If the Originator does not provide notificationContentType, the Hosting CSE shall set it as ‘all attributes'.

If the notificationURI is not the Originator, the Hosting CSE shall store Originator ID to creator attribute.

If the associatedCrossResourceSub is provided, check that the Hosting CSE ID value in the associatedCrossResourceSub is the same as the From parameter of the request.

- Recv-6.6

- Recv-6.7

- Recv-6.8

##### Retrieve

Originator:

No change from the generic procedures in clause 7.2.2.1.

Receiver:

No change from the generic procedures in clause 7.2.2.2.

##### Update

Originator:

No change from the generic procedures in clause 7.2.2.1.

Receiver:

The following are additional Hosting CSE procedures to the generic resource handling procedures in clause 7.2.2.2.

- Recv-6.5

If a new associatedCrossResourceSub is provided, check that the Hosting CSE ID value in the associatedCrossResourceSub is the same as the From parameter of the request.

If a <crossResourceSubscription> Hosting CSE ID is removed from associatedCrossResourceSub, the Hosting CSE shall send a Notify request for Subscription Deletion using the procedures in 7.5.1.2.4. to the <crossResourceSubscription> Hosting CSE.

##### Delete

Originator:

No change from the generic procedures in clause 7.2.2.1.

Receiver:

The following are changes to the receiver procedures described in  clause 7.2.2.2:

- Recv-6.5. The Hosting CSE shall send a Notify request for Subscription Deletion using the procedures in 7.5.1.2.4 to all <crossResourceSubscription> hosting CSEs indicated in associatedCrossResourceSub.

### -----------------------End of change 1-------------------------------------------

### -----------------------Start of change 2-------------------------------------------

### 7.4.X1 Resource Type <crossResourceSubscription>

#### 7.4.X1.1 Introduction

The <crossResourceSubscription> resource is used to support cross-resource subscription and cross-resource notification. A cross-resource subscription is made on multiple target resources. A cross-resource notification shall be generated if and only if expected events on all target resources occur within a designated time window. When notifications from all target resources occur within a specified time window the Hosting CSE shall issue a cross-resource notification.

The detailed description can be found in clause 9.6.58 in TS-0001 [6].

Table 7.4.X1.1-1: Data type definition of <crossResourceSubscription> resource

| Data Type ID | File Name | Note |
| --- | --- | --- |
| crossResourceSubscription | CDT-crossResourceSubscription-v3_x_0.xsd |  |

Table 7.4.X1.1-2: Universal/Common Attributes of <crossResourceSubscription> resource

| Attribute Name | Request Optionality |
| --- | --- |
|  | Create | Update |
| @resourceName | O | NP |
| resourceType | NP | NP |
| resourceID | NP | NP |
| parentID | NP | NP |
| accessControlPolicyIDs | O | O |
| creationTime | NP | NP |
| expirationTime | O | O |
| lastModifiedTime | NP | NP |
| labels | O | O |
| creator | M | NP |
| dynamicAuthorizationConsultationIDs | O | O |

Table 7.4.X1.1-3: Resource Specific Attributes of <crossResourceSubscription> resource

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | Create | Update |  |  |
| regularResourcesAsTarget | O | O | m2m:resourceList | No default. |
| subscriptionResourcesAsTarget | O | O | m2m:resourceList | No default |
| timeWindowType | M | O | m2m:timeWindowType | PERIODICWINDOW |
| timeWindowSize | M | O | m2m:absRelTimestamp | No default, but shall be a relative timestamp (i.e. a time duration) |
| eventNotificationCriteriaSet | O | O | m2m:eventNotificationCriteriaSet | Default behaviour is notification on Update_of_Resource |
| notificationEventCat | O | O | m2m:eventCat | No default |
| expirationCounter | O | O | xs:positiveInteger | No default |
| notificationURI | M | O | list of xs:anyURI | No default |
| subscriberURI | O | NP | m2m:ID | No default |

Table 7.4.X1.1-4: Reference of child resources

| Child Resource Type | Child Resource Name | Multiplicity | Ref. to in Resource Type Definition |
| --- | --- | --- | --- |
| <notificationTargetMgmtPolicyRef> | [variable] | 0..n | Clause 7.4.30 |
| <notificationTargetSelfReference> | ntsr | 1 | Clause 7.4.33 |
| <subscriptionLinkDeletion> | sld | 1 | Clause 7.4.X2 |

#### 7.4.X1.2	<crossResourceSubscription> resource specific procedure on CRUD operations

##### 7.4.X1.2.1  Create

Originator:

The following are changes to the Originator procedures described in  clause 7.2.2.1.

Orig-1.0  When composing a request primitive, the Originator shall include regularResourcesAsTarget and/or subscriptionResourcesAsTarget attributes in the resource respresentation of the <crossResourceSubscription> in the content of the primitive. If regularResourcesAsTarget attribute is included, eventNotificationCriteriaSet attribute shall be included. If eventNotificationCriteriaSet contains only one eventNotificationCriteria, this eventNotificationCriteria shall be applied to all regular resources included in regularResourcesAsTarget attribute; otherwise, eventNotificationCriteriaSet shall contain the same number of eventNotificationCriteria elements as the number of regular target resources contained in regularResourcesAsTarget and each eventNotificationCriteria element shall be sequentially applied to corresponding target resource as listed in the regularResourcesAsTarget.

Receiver:

The following are changes to the receiver procedures described in clause 7.2.2.2.

- Recv-6.5: The following steps are in addition to the generic Create procedures defined in clause 7.3.3.5.

  - The request shall be rejected with a “BAD_REQUEST” Response Status Code if at least one of regularResourcesAsTarget or subscriptionResourcesAsTarget attributes is not present in the request.

  - If regularResourcesAsTarget is included, the Hosting CSE shall send a CREATE <subscription> request message to each target resource indicated by regularResourcesAsTarget.

    - In the new CREATE <subscription> request, the receiver shall use the From of the current CREATE request. For this <subscription> to be created:

      - eventNotificationCriteria attribute shall use the corresponding entry included in eventNotificationCriteriaSet attribute of this <crossResourceSubscription> being created.

      - notificationURI attribute shall be set to the resource identifier of this <crossResourceSubscription> resource being created.

      - associatedCrossResourceSub attribute shall be set to the resource identifier of this <crossResourceSubscription> resource being created

      - notificationEventCat attribute shall be set to the same value in the <crossResourceSubscription> resource representation.

    - If any <subscription> for a target resource can not be successfully created, the receiver shall send an unsuccessful response with a “CROSS_RESOURCE_OPERATION_FAILURE” Response Status Code  to the Originator; the receiver shall also delete already created <subscription> resources at other target resources that were created based on the presence of regularResourcesAsTarget.

  - If subscriptionResourcesAsTarget is included, the Hosting CSE shall add the resource identifier of this <crossResourceSubscription> resource to the associatedCrossResourceSub attribute of each <subscription> resource indicated in subscriptionResourcesAsTarget by issuing an UPDATE request to the <subscription> resource host.

    - In the UPDATE request, the receiver shall use the From of the current CREATE request.

    - notificationURI attribute shall be updated to include the resource identifier of this <crossResourceSubscription> resource being created.

    - If any <subscription> for a target resource can not be successfully updated, the receiver shall send an unsuccessful response with a “CROSS_RESOURCE_OPERATION_FAILURE” Response Status Code   to the Originator; the Hosting CSE shall also remove itself from already successfully associated <subscription> resources using the procedures in 7.4.8.2.4 and also delete already created <subscription> resources at other target resources.

  - Once the <crossResourceSubscription> resource is created, the Hosting CSE shall start the time window if the timeWindowType=PERIODICWINDOW; otherwise timeWindowType=SLIDINGWINDOW, the Hosting CSE shall start the time window after the first notification is received from a Target Resource Hosting CSE.

##### 7.4.X1.2.2  Retrieve

Originator:

No change from the generic procedures in clause 7.2.2.1.

Receiver:

No change from the generic procedures in clause 7.2.2.2.

##### 7.4.X1.2.3  Update

Originator:

No change from the generic procedures in clause 7.2.2.1.

Receiver:

The following are changes to the receiver procedures described in clause 7.2.2.2.

- Recv-6.5: The following steps are in addition to the generic Update procedures defined in clause 7.3.3.7.

  - If regularResourcesAsTarget is updated, the Hosting CSE shall perform the following tasks.

    - If a target resource is deleted in the new regularResourcesAsTarget attribute value delete the associated <subscription> child resource using the procedure in 7.4.8.2.4.

    - if the updated regularResourcesAsTarget attribute value contains new target resources, the Hosting CSE shall send a CREATE <subscription> request message to each new target resource as described in 7.4.X1.2.1.

  - If subscriptionResourcesAsTarget is updated, the Hosting CSE shall perform the following tasks.

    - If a <subscription> resource is deleted in the new subscriptionResourcesAsTarget attribute value the Hosting CSE shall UPDATE the <subscription> resource using the procedure in 7.4.8.2.4 to remove this <crossResourceSubscription> from the <subscription> resource’s associatedCrossResourceSub attribute.

    - if the updated subscriptionResourcesAsTarget attribute value contains new a <subscription>resource, the Hosting CSE shall shall add the resource identifier of this <crossResourceSubscription> resource to the associatedCrossResourceSub attribute of each <subscription> resource indicated in subscriptionResourcesAsTarget as described in 7.4.X1.2.1.

  - If eventNotificationCriteriaSet is updated, the Hosting CSE shall update the eventNotificationCriteria of each previously created <subscription> child resource of the targets listed in the regularResourcesAsTarget attribute to reflect the received eventNotificationCriteria content using the procedures in 7.4.8.2.3.

  - If timeWindowSize or timeWindowType  is updated in the resource representation the the receiver shall restart the timer as described in 7.4.X1.2.1.

  - If any of the Update procedures are unsuccessful the receiver shall send an unsuccessful response with a “CROSS_RESOURCE_OPERATION_FAILURE” Response Status Code to the Originator; the receiver shall also restore all resources to the states they where in prior to this request.

##### 7.4.X1.2.4  Delete

Originator:

No change from the generic procedures in clause 7.2.2.1.

Receiver:

The following are changes to the receiver procedures described in  clause 7.2.2.2:

- Recv-6.5: The following steps are in addition to the generic Delete procedures defined in clause 7.3.3.5.

  - the Hosting CSE shall delete the previously created <subscription> child resource of each target resource indicated in the regularResourcesAsTarget attribute. The Receiver shall use the From of the current request for these messages.

  - the Hosting CSE shall UPDATE the <subscription> resource of each target resource indicated in the subscriptionResourcesAsTarget attribute using the procedure in 7.4.8.2.3 to remove the resource identifier of this <crossResourceSubscription> from the <subscription> resource’s associatedCrossResourceSub attribute. The Receiver shall use the From of the current request for these messages.

### -----------------------End of change 2-------------------------------------------

# Comments

TS-0001 needs update to make this a list.

Section for Create/Update(?) <crossResourceSubscription>

The create procedure above.

The create procedure above.

The create procedure above.