| CHANGE REQUEST |
| --- |
| Meeting:* | TP34.3 |
| Source:* | InterDigital |
| Date:* | 2018-04-24 |
| Contact:* | Bob Flynn (bob.flynn@interdigital.com) |
| Reason for Change/s:* | Clarification of text (refer to A-PRO-34.1-001) |
| CR against: Release* | Rel-3 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004-V3.7.0 |
| Clauses/Sub Clauses* | 7.5.1.2.4, 7.5.1.2.19 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

| A-PRO-34.1-001 | Bob will examine if clause 7.5.1.2.19 and 7.5.1.2.4 can be merged or the title for clause 7.5.1.2.19 should be changed. |
| --- | --- |

##### Notification for Subscription Deletion

Originator:

When the <subscription> resource is deleted and subscriberURI or associatedCrossResourceSub of the <subscription> resource is configured , the Originator shall send a Notify request primitive with a subscriptionDeletion element of the notification data object set as TRUE and subscriptionReference element set as the ID of the <subscription> resource to the entity indicated in subscriberURI or associatedCrossResourceSub.

##### Notification for subscription deletion

Whenever the subscribed to resources' modification triggers a notification for subscription deletion procedure as defined in clause 7.5.1.2.4 and the subscription relationship is established with <crossResourceSubscription> resource, the following procedure shall be performed.

- The <crossResourceSubscription> resource is deleted using the procedure defined in 7.4.58.2.4.

-----

The first section discusses when to “SEND” and subscription deletion notification.

The second section describes what a Reciever of that notification should do in the case that the Reciever is the HOST of a <crossResourceSubscription>. This would be properly captured as Reciever actions.

So I recommend deleting section 7.5.1.2.19 and putting equivalent text into 7.5.1.2.4

## ----------------------- Start of change 1 -----------------------

##### Notification for Subscription Deletion

Originator:

When the <subscription> resource is deleted and subscriberURI or associatedCrossResourceSub of the <subscription> resource is configured , the Originator shall send a Notify request primitive with a subscriptionDeletion element of the notification data object set as TRUE and subscriptionReference element set as the ID of the <subscription> resource to the entity indicated in subscriberURI or associatedCrossResourceSub.

Receiver:

When a subscription deletion notification is received by a Hosting CSE the <crossResourceSubscription> resource is deleted using the procedure defined in 7.4.58.2.4.

## ----------------------- End of change 1 -----------------------

## ----------------------- Start of change 2 -----------------------

## ----------------------- End of change 2 -----------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?

# Comments

PRO-2017-0241R05 proposed to add this subclause, but similar subclause already exits(clause 7.5.1.2.4). The contributor should check this.

PRO-2017-0241R05 proposed to add this subclause, but similar subclause already exits(clause 7.5.1.2.4). The contributor should check this.