| CHANGE REQUEST |
| --- |
| Meeting:* | TP34.3 |
| Source:* | InterDigital |
| Date:* | 2018-04-24 |
| Contact:* | Bob Flynn (bob.flynn@interdigital.com) |
| Reason for Change/s:* | Remove 3GPP interworking text (refer to A-PRO-34.1-003) |
| CR against: Release* | Rel-3 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004-V3.7.0 |
| Clauses/Sub Clauses* | Annex B, 5.2.1, |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

| A-PRO-34.1-004 | Raise a CR to address the <trafficPattern> resource referenced in Table B.2.1.2-1. |
| --- | --- |

All of the information captured in Annex B is captured in TS-00026 3GPP Interworking.

I suggest removing the entire Annex, leaving a note for reference.

Related note for minutes:

| TS-0004 | It only lists a normative Annex for device triggering for 3GPP. A similar Annex (like B.2 under B annex) should be included for 3GPP2. Note that in section 5.1.1 references to 3GPP2 device triggering to Annex B.1 which is not right. It should refer to Annex B.2 once it is added in the document. | Need an editorial CR to Section 5.1.1 & also into to Annex B. LS to 3GPP2? |
| --- | --- | --- |

## ----------------------- Start of change 1 -----------------------

(normative): 
3GPP MTC Interworking Device triggering

Refer to TS-0026 3GPP Interworking

## ----------------------- End of change 1 -----------------------

## ----------------------- Start of change 2 -----------------------

### Interfaces to the underlying networks

The CSEs access the network service functions provided by the underlying networks such as 3GPP, 3GPP2 and WLAN via Mcn reference point. Protocol bindings to the Mcn reference point are described in clause 9. The following services are provided by the underlying networks:

Device triggering

Location request (see Annex G)

Device Management (see clause 7.3.4)

## ----------------------- End of change 2 -----------------------

## ----------------------- Start of change 3 -----------------------

## ----------------------- End of change 3 -----------------------

## ----------------------- Start of change 4 -----------------------

## ----------------------- End of change 2 -----------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?

# Comments

PRO-2017-0322R02 proposed to delete <trafficPattern>. This Annex shall be updated. Action for Convida.