| CHANGE REQUEST |
| --- |
| Meeting:* | PRO 35 |
| Source:* | KT Corp. (TTA) |
| Date:* | 2018-05-22 |
| Contact:* | Francisco, Sang-Eon Kim, kim.sangeon@kt.com |
| Reason for Change/s:* | HTTP Method Mapping is not clear to implement. |
| CR against: Release* | Release1 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0009-V3..0.0 |
| Clauses/Sub Clauses* | 6.2.1 Method |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Problem

HTTP method maping is not clearly specified  in TS-0009 as followings

-------------------

### 6.2.1	Method

The HTTP 'Method' shall be derived from the Operation request primitive parameter of the request primitive.

Table 6.2.1-1: HTTP Method Mapping

| oneM2M Operation | HTTP Method |
| --- | --- |
| Create | POST |
| Retrieve | GET |
| Update | PUT (full update) or POST (partial update) |
| Delete | DELETE |
| Notify | POST |

At the Receiver, an HTTP request message with POST method shall be mapped to a oneM2M Create or Notify request primitive in accordance with the value of the Operation parameter.

----------------

- How can operation identify POST method at Receiver ?

- How can method identify Update operation at Originator ?

## Proposal

Update operation is mapped to PUT or POST. PUT method is for full Update and POST method is for partial Update.

The POST method is used for Create, partial Update, Notify operation of M2M message. A Receiver need to identify POST method for three kinds of operations.

To reduce complexity, Let’s consider PATCH method.

RFC 5789 “PATCH Method for HTTP” is suitable for partial Update operation.

When WG3 agree to introduce PATCH, POST method can easily identify wither Create or Notify operation at a Receiver.

Because ‘Resource Type’ parameter is mandatory for Create operation, but ‘Resource Type’ parameter is not present as specified at clause 7.1.1.1 in TS-0004.

A Originator should identify Update operation to either PUT or PATCH/POST by checking media type in Request message.

RFC 6902 “ JavaScript Object Notation (JSON) Patch” introduce to media type for partial update

JSON patch can be identified by te media type "application/json-patch+json"

RFC7351 “A Media Type for XML Patch Operations” is for XML patch media type.

“ "application/xml-patch+xml" is an XML document structure for expressing a sequence of operations to apply to a target XML document, suitable for use with the HTTP PATCH  method.”

Request primitive is specified at clause 7.1.1.1 in TS-0004-V1.2.1 as follows

-----------------

#### Request primitive format

Table 7.1.1.1-1 summarizes the primitive parameters of  the Request primitive, indicating their presence depending on the C, R, U, D or N operations. "M" indicates mandatory, "O" indicates optional, "NP" indicates not present.

Refer to clause 8.1.2 of the oneM2M TS-0001 [6] for additional information on the request primitive parameters.

Table 7.1.1.1-1: Request Primitive Parameters

| Primitive Parameter | CREATE | RETRIEVE | UPDATE | DELETE | NOTIFY |
| --- | --- | --- | --- | --- | --- |
| Operation | M | M | M | M | M |
| To | M | M | M | M | M |
| From | M | M | M | M | M |
| Request Identifier | M | M | M | M | M |
| Resource Type | M | NP | NP | NP | NP |
| Name | O | NP | NP | NP | NP |
| Content | M | O | M | NP | M |
| Originating Timestamp | O | O | O | O | O |
| Request Expiration Timestamp | O | O | O | O | O |
| Result Expiration Time | O | O | O | O | O |
| Operation Execution Time | O | O | O | O | O |
| Response Type | O | O | O | O | O |
| Result Persistence | O | O | O | O | NP |
| Result Content | O | O | O | O | NP |
| Event Category | O | O | O | O | O |
| Delivery Aggregation | O | O | O | O | O |
| Group Request Identifier | O | O | O | O | O |
| Filter Criteria | NP | O | O | O | NP |
| Discovery Result Type | NP | O | NP | NP | NP |

-----------------

R01;

TS-0026 V.0.8.1 introduces PATCH method for partial update through HTTP protocol.

However, TS-0009 can not support partial update at this time.

ARC-2018-0125 propose to discuss this issues.

If ARC/PRO reach consensus to introduce PATCH method, this contribution needs to re-open and discuss.

In the protocol aspect, it needs to be discussed scope of release partial update for either all release (Release 1, Release2 and Release 3) or Release 3 only.

Otherwise, ARC should change for full update i.e. PUT method

R02:

Revise clause 2.1	Normative references

### -----------------------Start of change 1-------------------------------------------

### 6.2.1	Method

The HTTP 'Method' shall be derived from the Operation request primitive parameter of the request primitive.

Table 6.2.1-1: HTTP Method Mapping

| oneM2M Operation | HTTP Method |
| --- | --- |
| Create | POST |
| Retrieve | GET |
| Update | PUT (full update) or PATCH (partial update) |
| Delete | DELETE |
| Notify | POST |

At the Receiver, an HTTP request message with POST method shall be mapped either to a Create or Notify Operation parameter. Discrimination between Create and Notify operations can be accomplished by inspection of the content-type header. The Resource Type parameter is present in the content-type header only when the HTTP POST request represents a Create request (see clause 6.4.3). The Resource Type parameter is not present in the content-type header when the HTTP POST request represents a Notify request.

An Originator which has Content parameter shall be mapped Create and Notify operation to POST method. A Receiver shall be checked Resource Type parameter. When the Resource Type parameter exists, POST method shall be mapped to Create operation. When the Resource Type parameter does not exists, POST method shall be mapped to Notify operation as specified at clause 7.1.1.1 in TS-0004.

An Originator which has Content parameter shall be mapped Update operation to PUT or PATCH method. An Originator shall be checked media types as specified at clause 6.7 in TS-0004. When a Request message has patch media type, Update operation shall be mapped to PATCH method for partial update. When a Request message does not have patch media type, Update operation shall be mapped to PUT method for full update.

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

## 2.1	Normative references

References are either specific (identified by date of publication and/or edition number or version number) or non-specific. For specific references, only the cited version applies. For non-specific references, the latest version of the reference document (including any amendments) applies.

The following referenced documents are necessary for the application of the present document.

[1]	IETF RFC 7230 "Hypertext Transfer Protocol (HTTP/1.1): Message Syntax and Routing", June 2014

[2]	oneM2M TS-0003: Security Solutions.

[3]	oneM2M TS-0004: "Service Layer Core Protocol Specification".

[4]	IETF RFC7235: “Hypertext Transfer Protocol (HTTP/1.1): Authentication”, June 2014.

[5]	IETF RFC6750: “The OAuth 2.0 Authorization Framework: Bearer Token Usage”, October 2012.

[6]	oneM2M TS-0011: Common Terminology.

[7]	oneM2M TS-0001: Functional Architecture.

[8]		IETF RFC 7232 "Hypertext Transfer Protocol (HTTP/1.1): “Conditional Requests", June 2014.

[9]	IETF RFC 3986: “Uniform Resource Identifier (URI): Generic Syntax”. January 2005

[10]	IETF RFC 7231: “HTTP/1.1 Semantics and Content”, June 2014[11] 	IETF RFC 5789, "PATCH Method for HTTP", March 2010

### -----------------------End of change 2---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?