| CHANGE REQUEST |
| --- |
| Meeting ID:* | PRO 35 |
| Source:* | Siddharth Trikha (strikha@cdot.in), Sachin Jain (sachin@cdot.in), Suman Sheoran (ssheoran@cdot.in), Anupama chopra(anupama@cdot.in) |
| Date:* | 2018-05-07 |
| Reason for Change/s:* | See the Introduction |
| CR against: Release* | Release 2 |
| CR against: WI* | Active <Work Item number> MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: PRO-2018-0149R01-CoAP STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0008 v2_6_0 |
| Clauses * | 6.3.2, 6.3.3 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) |  |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

In TS-0004 scetion 7.2.2.2, generic flow for handling request at receiver is shown in the diagram below

Figure 7.2.2.2-1: Generic procedure of Receiver

#### Create a success response (acknowledgement)

The Receiver CSE shall create a Response primitive. The Receiver CSE shall include the following parameters in the Response primitive.

Table 7.3.2.3-1: Response primitive parameter settings

| Parameter Name | Value |
| --- | --- |
| Response Status Code | "ACCEPTED" |
| Request Identifier | The value of the parameter Request Identifier in the associated non-blocking request. |
| Originating Timestamp | Timestamp when this message was built |
| Content | Reference to the <request> of the associated non-blocking request only if <request> resource is supported. |

That implies in case of Non-Blocking, Reference of <request> resource is always sent along with acknowledgement if <request> resource is supported. Then After successfully processing of request notification is sent to notificationURIs with the content of that notification as response of original request only if request mode is "nonBlockingRequestAsynch".

While In TS-0008, section 6.3.2 do not mention anything about reference of <request> resource as highlighted in text below:

### Non-Blocking Asynchronous case

If Response Type parameter is configured as "nonBlockingRequestAsynch" (non-blocking asynchronous case), the Originator (CoAP client) shall use the Confirmable Method for the resource to the Receiver (CoAP server). Originator shall provide a unique Token value in the request.

The Receiver shall provide an acknowledgment of receipt of the request using Acknowledgment message.

The Receiver, upon successful processing of the request, shall send an appropriate response in a separate Confirmable message with the Token value. The Originator shall acknowledge the Confirmable response.

First change proposes to piggy-back <request> resource reference in Non-Blocking Asynchronous on the Acknowledgement message.

Reason for change2:

Figure 6.3.0-1: Accessing resource cases

### 6.3.3	Non-Blocking Synchronous case

If Response Type parameter is configured as "nonBlockingRequestSynch" (non-blocking synchronous case), the Originator (CoAP client) shall use the Confirmable Method for the resource to the Receiver (CoAP server). Originator shall provide a unique Token value in the request.

The Receiver shall provide an acknowledgment of receipt of the request using Acknowledgment message. The response on the request may be piggy-backed in the Acknowledgement message if possible for the Receiver.

The Receiver, after validating the request and before processing it fully, shall send an appropriate response including a reference in a separate Confirmable message. The Originator shall acknowledge the Confirmable response.

The Originator can use the reference or the token to synchronously access or retrieve the resource. The Receiver, upon receipt of the request, shall respond with the current state of the resource.

NOTE:	If the Receiver is a Transit CSE, the Receiver acts as CoAP client and CoAP server.

In nonblockingSynch request, clarification is required in bullet 2 and 3 text. Firstly, in bullet 2 it’s written “response on the request” may be piggybacked, making it explicit that <request> resource reference needs to be returned in the Acknowledgement message rather than whole response. Secondly, in accordance to the second bullet correction, third point becomes optional i.e if only the <request> reference is not piggybacked, then it needs to be sent in a separate CON (Confirmable) message.

### -----------------------Start of change 1-------------------------------------------

### 6.3.2	Non-Blocking Asynchronous case

- If Response Type parameter is configured as "nonBlockingRequestAsynch" (non-blocking asynchronous case), the Originator (CoAP client) shall use the Confirmable Method for the resource to the Receiver (CoAP server). Originator shall provide a unique Token value in the request.

- The Receiver shall provide an acknowledgment of receipt of the request using Acknowledgment message piggybacking the <request> resource reference, if <request> resource is supported.

- The Receiver, upon successful processing of the request, shall send an appropriate response in a separate Confirmable message with the Token value. The Originator shall acknowledge the Confirmable response.

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

### 6.3.3	Non-Blocking Synchronous case

If Response Type parameter is configured as "nonBlockingRequestSynch" (non-blocking synchronous case), the Originator (CoAP client) shall use the Confirmable Method for the resource to the Receiver (CoAP server). Originator shall provide a unique Token value in the request.

The Receiver, after validating the request and before processing it fully, shall provide an acknowledgment of receipt of the request using Acknowledgment message. The  reference of <request> resource may be piggy-backed in the Acknowledgement message if possible for the Receiver else

the Receiver,  shall send an appropriate response including a reference of the <request> resource in a separate Confirmable message. The Originator shall acknowledge the Confirmable response.

The Originator can use the reference or the token to synchronously access or retrieve the resource. The Receiver, upon receipt of the request, shall respond with the current state of the resource.

NOTE:	If the Receiver is a Transit CSE, the Receiver acts as CoAP client and CoAP server.

### -----------------------End of change 2---------------------------------------------

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?

# Text boxes

Recv-1.0: “Check the validity of received request primitive”

Recv-2.0: Communication method?

Recv-6.0: Resource handling procedures

Recv-3.0: “Create <request> resource locally”

Recv-4.0: “Create a success Response”

Recv-5.0: “Send Response primitive”

nonBlockingRequestAsynch

nonBlockingRequestSynch

Recv-6.0: Resource handling procedures

Recv-7.0: “Update <request> resource”

Finish

Start

Recv-3.0: “Create <request> resource locally”

Recv-4.0: “Create a success Response”

Recv-5.0: “Send Response primitive”

Recv-6.0: Resource handling procedures

Recv-7.0: “Update <request> resource”

Recv-8.0: “Send Notification”

Recv-9.0: “Wait for Response primitive”

blockingRequest

Recv-10.0: “Send Response Primitive”