| MINUTES |
| --- |
| Meeting: | PRO 35 |
| Chair: | Peter Niblett, IBM Europe, peter_niblett@uk.ibm.com Nobuyuki Uchida, Qualcomm, nuchida@qti.qualcomm.com Hao Wu, ZTE, wu.hao18@zte.com.cn |
| Secretary: | Laurent Velez, ETSI |
| Meeting Date: | 2018-05-22/25 |
| Meeting Details: | Face to Face meeting in Sophia-Antipolis , France |
| Intended purpose of document: | Decision Discussion Information Other <specify> |
| Template Version:23 February 2015 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

1	Opening of the meeting

Peter Niblett chair of the PRO WG, opened the meeting and drew the participants’ attention to the oneM2M notice on the cover page of the agenda.

2	Review & Agreement of Agenda

| PRO-2018-0174 | Agenda PRO35 | PRO WG Chair |
| --- | --- | --- |

PRO-2018-0174 was NOTED

PRO-2018-0174R01 was NOTED

PRO-2018-0174R02 was NOTED

PRO-2018-0174R03 was AGREED

3	Review of Previous Minutes

| PRO-2018-0161 | Minutes_PRO34_4 | ETSI |
| --- | --- | --- |

PRO-2018-0161 was AGREED

4	Objectives for the Meeting

The chairman presented the objectives of the meeting.

- Complete the R3 contributions

- Essential corrections for R2

5	Action Item Status

| Number | Action | Responsible | Status |
| --- | --- | --- | --- |
| A-PRO-16.0-002 | Investigate MQTT Binding on Mcc’ | SeungMyeong & Peter | Peter to draft a CR to permit absolute identifiers to be used |
| A-PRO-24.2-001 | Provide more information on SPARQL errors | Bob Flynn | We need a volunteer to deal with this. MAS WG would also need to be involved. PRO30 Update – Bob expects to provide an update during PRO31 Bob Indicated he is waiting for Semantic Interop testing that will be held on 4-8 Dec 2017 in Korea. |
| A-PRO-26.0-001 | Register CoAP codes with IANA | Peter & Laurent | Email sent to Miguel |
| A-PRO-32.0-002 | Raise CR to clarify format of ChildResourceRef – structured or unstructured? | Bob | No conclusion yet. Bob volunteers to raise a CR. Bob has prepared contribution |
| A-PRO-33.0-001 | Raise CR to add procedure for networkCoordinated attribute | Bob | Bob has prepared contribution |
| A-PRO-34-001 | Raise a CR to clarify multicast group fanout procedure. | Echo |  |
| A-PRO-34.1-002 | Raise a CR containing three changes. (a) remove the new oneM2M simple data type (m2m:resourceList) from Table 6.3.3-1 (b) remove two complex data types (6.3.5.67 and 6.3.5.68 (c) change the data type for the regularResourcesAsTarget and subscriptionResourcesAsTarget attributes to m2m:listOfURIs. | Bob |  |
| A-PRO-34.1-004 | Raise a CR to address the <trafficPattern> resource referenced in Table B.2.1.2-1. | Bob |  |
| A-PRO-34.2-002 | Raise a new CR to address issue that Resource type definition for <crossResourceSubscription> in TS-0001 includes a mandatory notificationContentType attribute which is missing in TS-0004. | Bob | Bob to check about the status of the issue Addressed in ARC-2018-0152 |
| A-PRO-34.2-003 | TS-0008. Use of non-confirmable needs to be clarified. Is the receiver required to treat a non-confirmable request (other than multicast) as an error? | Bob | Question: Should we state that originators shall not use non-confirmable ? |
| A-PRO-34.2-004 | TS-0008 states that DTLS is forbidden for the multicast group fan out messages in B.1. | Wolfgang | This appears to be a contradiction with TS-0003. This should be discussed with SEC WG. Wolfgang has produced a discussion paper to be reviewed first at next SEC WG meeting at TP#35, before going to PRO. Wolfgang has prepared a contribution |
| A-PRO-34.2-005 | Need CR to describe behaviour when accessControlPolicyIDs attribute value does not point to a valid resource or is not reachable | Wolfgang | Agreement with SEC and ARC needed Wolfgang is waiting for a CR from SeungMyeong about the behavior related to default access control policy CR PRO-2018-0154 is now available. |

| TS | Issue | Volunteer |
| --- | --- | --- |
| TS-0004 | It only lists a normative Annex for device triggering for 3GPP. A similar Annex (like B.2 under B annex) should be included for 3GPP2. Note that in section 5.1.1 references to 3GPP2 device triggering to Annex B.1 which is not right. It should refer to Annex B.2 once it is added in the document. | Need an editorial CR to Section 5.1.1 & also into to Annex B. LS to 3GPP2? |
| TS-0009 | HTTP_AE_CSE_registration | Release 2 |

6	Contributions

6.0 	Baselines

Baselines available:

TS-0004 v1.13.0 (Core Protocol)

| PRO-2018-0107 | TS-0004 Service Layer Core Protocol V1.13.0 | TS-0004 Rapporteur | 2018-03-22 |
| --- | --- | --- | --- |

Agreed at PRO34.1

TS-0004 v2.17.0

| PRO-2018-0108 | TS-0004 Service Layer Core Protocol V2.17.0 | TS-0004 Rapporteur | 2018-03-26 |
| --- | --- | --- | --- |

Agreed at PRO34.1

TS-0004 3.7.0

| PRO-2018-0109R02 | TS-0004 Service Layer Core Protocol V3.7.0 | TS-0004 Rapporteur | 2018-04-26 |
| --- | --- | --- | --- |

Agreed at PRO34.2

TS-0004 XML Schemas

| PRO-2018-0119 | PRO34_changes_of_XML_schemas_to_align_with_TS-0004 | Qualcomm | 2018-04-11 |
| --- | --- | --- | --- |

Agreed by correspondence

TS-0008 v1.6.0 (CoAP Protocol Binding)

| PRO-2017-0048 | TS_0008 R1 baseline | Huawei | 2017-02-23 |
| --- | --- | --- | --- |

Stabilised at 1.6.0

TS-0008 v2.6.0 (CoAP Protocol Binding)

| PRO-2018-0051 | TS-0008 CoAP Protocol Binding V2.6.0 | CoAP Rapporteur | 2018-01-15 |
| --- | --- | --- | --- |

Agreed

TS-0008 v3.1.0 (CoAP Protocol Binding)

| PRO-2018-0118 | TS-0008 v3.1.0 baseline | CoAP Rapporteur | 2018-04-08 |
| --- | --- | --- | --- |

Agreed at PRO34.2

TS-0009 v1.10.0 (HTTP Protocol Binding)

| PRO-2017-0002 | TS-0009 draft baseline v1.10.0 | HTTP Rapporteur | 2017-01-16 |
| --- | --- | --- | --- |

Stabilised at v1.10.0

TS-0009 v2.13.0

| PRO-2018-0049 | Draft TS-0009 v.2.13.0 | HTTP Rapporteur | 2018-01-15 |
| --- | --- | --- | --- |

Agreed

TS-0009 v3.0.0 (HTTP Protocol Binding)

| PRO-2018-0070 | TS-0009 v3.0.0 baseline | HTTP Rapporteur | 2018-02-21 |
| --- | --- | --- | --- |

Agreed

TS-0010 v1.8.0 (MQTT Protocol Binding)

| PRO-2018-0110 | TS-0010 draft baseline v1.8.0 | MQTT Rapporteur | 2018-04-02 |
| --- | --- | --- | --- |

Agreed at PRO34.1

TS-0010 v2.8.0

| PRO-2018-0111 | TS-0010 draft baseline v2.8.0 | MQTT Rapporteur | 2018-04-02 |
| --- | --- | --- | --- |

Agreed at PRO34.1

TS-0020 v2.2.0 (WebSocket Protocol Binding)

| PRO-2018-0114R01 | TS-0020-WebSocket_Protocol_Binding-V2_2_0_draft | WS Rapporteur | 2018-04-04 |
| --- | --- | --- | --- |

Agreed at PRO34.1

6.1		Contributions on TS-0004: Protocol TS

| PRO-2018-0039 | virtual resource name reservation (rel-2) | KETI |
| --- | --- | --- |
| PRO-2018-0042R01 | virtual resource name reservation (rel-3) | KETI |

It has been decided to note these contributions with no further action.

PRO-2018-0039 was NOTED at PRO#32.2

PRO-2018-0042R01 was NOTED at PRO#32.2

| PRO-2017-0231R03 | TS-0004 BDT | Convida |
| --- | --- | --- |

Presented by Bob and Catalina on Tuesday session-1 PRO

This contribution provides Stage 3 changes needed for implementation of Background Data Transfer procedure and the introduction of the <backgroundDataTransfer> resource (see TS-0001 V3_8_0, sections 9.6.60 and 10.2.20).

Comment:

- Question to the audience: Do we need to get a Transaction child to the backgroundDataTransfer resource ?

- Change 3: in table 7.4.x.1-2,  creator attribute is in the table but not in TS-0001 and one attribute of TS-0001  is missing in TS-0004. Bob to check.

- desiredTimeWindow attribute is optional in oneM2M but mandatory in 3GPP . Is it intentional? It is decided to change the optionality to Mandatory for create operation.. Edited online. The actual value will be determined by the underlying network.

- transferSelectionGuidance attribute : added the text for Default value :“ if not provided the CSE will set this value based on local policy.”

- Update of the receiver procedure of the clause 7.4.x.2.1 Create, in order to bring more clairity.

Revision expected

PRO-2017-0231R03 was NOTED

PRO-2017-0231R05 presented by Bob on Friday session-3 PRO

PRO-2017-0231R05 was AGREED

| PRO-2017-0247R04 | TS-0004_Transaction_Management_R3 | Convida |
| --- | --- | --- |

Presented by Bob on Tuesday session-1 PRO

This contribution adds support for Transaction Management to TS-0004.  Transaction Management functionality is currently described in TS-0001 as a new Rel-3 feature.

A transaction is a set of oneM2M request primitives that must be performed as an atomic set. The entire set of requests either need to be executed successfully or none of them executed.

This has been presented in previous conference calls. This revision R04 takes in account the comments received.

Comment:

- It was noticed a typo in the xsd file name. Edited online to fix it.

PRO-2017-0247R04 was NOTED

PRO-2017-0247R05 was AGREED

| PRO-2018-0132 | TS-0004 consistencyStrategy multiplicity correction R2 | BOE |
| --- | --- | --- |

Presented by Albert on Wednesday session PRO

Update the Request Optionality of the consistencyStrategy attribute in <group> resource should be “M”.

PRO-2018-0132 was NOTED

| PRO-2018-0133R03 | fanOutPoint_Correction(R3) | C-DOT |
| --- | --- | --- |

Presented by Prateek on Friday session-3 PRO

This contribution proposes to fix an inconsistency between TS-0001 and TS-0004 on FanOutPoint.

Comment:

- Minor editorial made online

PRO-2018-0133R03 was NOTED

PRO-2018-0133R04 was AGREED

| PRO-2018-0134R02 | fanOutPoint_Correction(R2) | C-DOT |
| --- | --- | --- |

Presented by Prateek on Friday session-3 PRO

Mirror CR of PRO-2018-0133R03

PRO-2018-0134R02 was AGREED

| PRO-2018-0135R01 | check_supported_resource_type(R3) | C-DOT |
| --- | --- | --- |

Presented by Prateek on Wednesday session-1 PRO

TS-0004 clause 7.3.3 describes the common operations of Hosting CSE actions, out of which Check supported resource types shall be valid only for CREATE requests, as resource type is provided only in the CREATE requests by the originator.

Also for other types of requests (RETRIEVE, UPDATE or DELETE), this check seems to be invalid because to determine the resource type of the targeted resource CSE has to determine its existence first.

Comment:

- Some editorial for clarifying the text.

PRO-2018-0135R01 was NOTED

PRO-2018-0135R02 Presented by Prateek on Thursday session-2 PRO

PRO-2018-0135R02 was AGREED

| PRO-2018-0136R01 | check_supported_resource_type(R2) | C-DOT |
| --- | --- | --- |

Presented by Prateek on Wednesday session-1 PRO

Mirror CR of PRO-2018-0135R01

PRO-2018-0136R01 was NOTED

PRO-2018-01356R02 Presented by Prateek on Thursday session-2 PRO

PRO-2018-0136R02 was AGREED

| PRO-2018-0143 | Synchronous_non-blocking_mode_R3 | C-DOT |
| --- | --- | --- |

Presented on Wednesday session-3 PRO/MAS

Comment/Issue: Editorial changes made online.

PRO-2018-0143 NOTED

PRO-2018-0143R01 AGREED

| PRO-2018-0156R01 | CreateLocationPolicyImmediateResponse_R2 | C-DOT |
| --- | --- | --- |

Presented on Wednesday session-3 PRO/MAS

Comment/Issue: Same comment as PRO-2018-0155R01

PRO-2018-0156R01 NOTED

| PRO-2018-0155R01 | CreateLocationPolicyImmediateResponse_R3 | C-DOT |
| --- | --- | --- |

Presented on Wednesday session-3 PRO/MAS

PRO-2018-0155R01 NOTED

Presented on Thursday session-3 ARC/PRO/TST

The flow is new, it has not been copied from either TS-0001 or TS-0004.

C-DOT to work with Echo to align between OMA/3GPP/location

This was previously noted during PRO 35

PRO-2018-0155R01 was NOTED

| PRO-2018-0158R02 | StateTag_TimeSeriesInstance_R3 | C-DOT |
| --- | --- | --- |

Presented by Neeta on Wednesday session-4 PRO

The stateTag attribute has been added to <timeSeriesInstance> resource, CR number-ARC-2018-0141R04. So, this CR make all the changes require to add new attribute in TS-0004 as well as in XSD.

Comment:

- Need to be addressed in joint ARC/PRO

- Typo in the name of StateTag attribute

PRO-2018-0158R02 was NOTED

PRO-2018-0158R02 presented on Thursday session-4 ARC/PRO/TST

This was previously noted during PRO 35

Questions raised over the feature number

PRO-2018-0158R02 was NOTED

ARC-35-0004: SeungMyeong to review all resource types and their usage of state tags

| PRO-2018-0158R02 | StateTag_TimeSeriesInstance_R3 | C-DOT |
| --- | --- | --- |

This was previously noted during PRO 35

Questions raised over the feature number

PRO-2018-0158R02 was NOTED

ARC-35-0004: SeungMyeong to review all resource types and their usage of state tags

The contribution will be reviewed in future conference calls

PRO-2018-0158R02 was POSTPONED

| PRO-2018-0159R01 | StateTag_TimeSeriesInstance_R2 | C-DOT |
| --- | --- | --- |

Presented on Wednesday session-3 PRO/MAS

Comment/Issue: Same comment as 0158R01.

PRO-2018-0159R01 was NOTED

The contribution will be reviewed in future conference calls

PRO-2018-0159R02 was POSTPONED

| PRO-2018-0137R01 | Change_In_RSC_R3 | C-DOT |
| --- | --- | --- |

Presented by Neeta on Wednesday session-4 PRO

This contribution proposes to change the Response Status Code “NON_BLOCKING_REQUEST_NOT_SUPPORTED” to “NON_BLOCKING_SYNCH_REQUEST_NOT_SUPPORTED”.

Comment:

- If the change is agreed, the binding specifications CoAP and HTTP would need to be updated as well both Rel 2 and 3. Including the TS-0004, it means 6 CR.

- Question to be raised at the joint PRO/TST. Is it mandatory to support “nonBlocking Asynch”?  If yes, what it the RSC to be returned?

Action : To C-DOT :  To raise a set of binding CRs

Action : To consider a RSC for nonBlocling Asynch

PRO-2018-0137R01 was AGREED

| PRO-2018-0139R02 | Change_In_RSC_R2 | C-DOT |
| --- | --- | --- |

Presented by Neeta on Wednesday session-4 PRO

Mirror CR of PRO-2018-0137R01

PRO-2018-0139R02 was AGREED

| PRO-2018-0132 | TS-0004 consistencyStrategy multiplicity correction R2 | BOE |
| --- | --- | --- |

Presented by Albert on Wednesday session-1 PRO

No action is foreseen.

PRO-2018-0132 was NOTED

| PRO-2018-0162 | CSE_Actions_Corrections(R3) | C-DOT |
| --- | --- | --- |

Presented by Prateek on Wednesday session-1 PRO

This CR proposes corrections in TS-0004 section 7.3.2 Receiver CSE actions and section 7.3.3 Hosting CSE actions for validations on “Accept type” and “Release Version Indicator”.

Comment

- Discussion on the procedure described in clause 7.3.3.2, if the request “shall” be rejected or “may” be rejected.

Revision expected to reflect the new proposed text.

PRO-2018-0162 was NOTED

PRO-2018-0162R01 Presented by Prateek on Thursday session-2 PRO

PRO-2018-0162R01 was AGREED

| PRO-2018-0163 | CSE_Actions_Corrections(R2) | C-DOT |
| --- | --- | --- |

Presented by Prateek on Wednesday session-1 PRO

Mirror CR of PRO-2018-0162

Same comment than mirror CR

PRO-2018-0163 was NOTED

PRO-2018-0163R01 Presented by Prateek on Thursday session-2 PRO

PRO-2018-0163R01 was AGREED

| PRO-2018-0138R01 | locationContainerIDOccurenceInXSD_R3 | C-DOT |
| --- | --- | --- |

Presented by Prateek on Wednesday session-2 PRO

The attribute locationContainerId of the resource <locationPolicy> has multiplicity equal to 1.  But the minimum occurrence of the attribute in the resource xsd is given to be 0 which creates a conflict.

Thus it is proposed to remove the minimum occurrence of the attribute in the release 3 xsd version 3.7.0 which makes the default minimum occurrence equal to 1.

PRO-2018-0138R01 was AGREED

| PRO-2018-0140R02 | locationContainerIDOccurenceInXSD_R2 | C-DOT |
| --- | --- | --- |

Presented by Prateek on Wednesday session-2 PRO

Mirror CR of PRO-2018-0138R01

PRO-2018-0140R02 was AGREED

| PRO-2018-0146 | TimeSeries_XSD_Change_R3 | C-DOT |
| --- | --- | --- |

Presented by Prateek on Wednesday session-2 PRO

There are some inconsistencies in CDT-timeSeries-v3_7_0.xsd corresponding to TS-0001 Table 9.6.36.2 Attributes of <timeSeries> resource. This CR proposes to remove such inconsistencies.

PRO-2018-0146 was AGREED

| PRO-2018-0148R01 | TimeSeries_XSD_Change_R2 | C-DOT |
| --- | --- | --- |

Presented by Prateek on Wednesday session-2 PRO

Mirror CR of PRO-2018-0146

PRO-2018-0148R01 was AGREED

| PRO-2018-0141 | Clarification_subscription_verification_R3 | C-DOT |
| --- | --- | --- |

Presented by Prateek on Wednesday session-2 PRO

This CR propose to change Notify response primitive with response primitive as Hosting CSE shall not return Notify response primitive in this case.

Off line discussion needed .Revision expected

PRO-2018-0141 was NOTED

PRO-2018-0141R01 presented by Prateek on Thursday session-2 PRO

PRO-2018-0141R01 was AGREED

| PRO-2018-0142R01 | Clarification_subscription_verification_R2 | C-DOT |
| --- | --- | --- |

Presented by Prateek on Wednesday session-2 PRO

Mirror CR of PRO-2018-0141

Revision expected

PRO-2018-0142R01 was NOTED

PRO-2018-0142R02 presented by Prateek on Thursday session-2 PRO

PRO-2018-0142R02 was AGREED

| PRO-2018-0151 | RemovalOfMappingLocationUpdatePeriod_R3 | C-DOT |
| --- | --- | --- |

Presented by Prateek on Wednesday session-2 PRO

The contribution propose to remove the mapping of locationUpdatePeriod to duration attribute

PRO-2018-0151 was AGREED

| PRO-2018-0152 | RemovalOfMappingLocationUpdatePeriod_R2 | C-DOT |
| --- | --- | --- |

Presented by Prateek on Wednesday session-2 PRO

Mirror CR of PRO-2018-0151

PRO-2018-0152 was AGREED

| PRO-2018-0144R02 | Synchronous_non-blocking_mode_R2 | C-DOT |
| --- | --- | --- |

Presented by Neeta on Wednesday session-4 PRO

In TS-0004 Annex E, no-hop case of Synchronous Non-Blocking request, it is said that When Hosting CSE receives ‘nonBlockingSynch’ request, <request> resource is created with requestStatus attribute set to “ACCEPTED”. But “ACCEPTED” is not valid value for requestStatus.

PRO-2018-0144R02 was NOTED

PRO-2018-0144R03 was AGREED

| PRO-2018-0168R02 | UnsupportedMediaType_RSC(R3) | C-DOT |
| --- | --- | --- |

Presented by Prateek on Thursday session-2 PRO

This CR introduces addition of status code “UNSUPPORTED_MEDIA_TYPE” in Table 6.6.3.6-1 and additional check in section 7.3.3 Hosting CSE Actions in case an unsupported media type is sent by the originator, corresponding to CRs PRO-2018-0164R01 and PRO-2018-0166R01 .

Comment:

- Not clear for the rapporteur what is to be deleted due to the change mark. A revision is done.

- Edited online to add a change for clause 7.3.3.2, replacing a “shall” by a “may”

PRO-2018-0168R02 was NOTED

PRO-2018-0168R03 was AGREED

| PRO-2018-0169R01 | UnsupportedMediaType_RSC(R2) | C-DOT |
| --- | --- | --- |

Presented by Prateek on Thursday session-2 PRO

Mirror CR of PRO-2018-0168R02

Same comment than mirror R3 CR

PRO-2018-0169R01 was NOTED

PRO-2018-0169R02 was AGREED

| PRO-2018-0153 | accessControlPolicyIDs and default policy (R2) | KETI |
| --- | --- | --- |

Presented by SeungMyeong on Thursday session-5 ARC/PRO/SEC

This contribution is linked to ARC-2018-0067R02 (parent_resource_lookup_for_acpid(R2)  agreed at ARC#35.

Addition to the alignment to that TS-0001 CR, this CR proposes to remove the duplicated specifications to TS-0001 but to put clause reference where already has all information needed and defined.

Comment:

- Edited clause 7.3.3.15  ( check authorization of the originator) to clarify the text by adding a procedure specifying when the target resource conatins the accessControlPolicyID attribute

PRO-2018-0153 was NOTED

PRO-2018-0153R01 was AGREED

| PRO-2018-0154 | accessControlPolicyIDs and default policy (R3) | KETI |
| --- | --- | --- |

Presented by SeungMyeong on Thursday session-5 ARC/PRO/SEC

Mirror CR of PRO-2018-0153. Same Comment and update.

PRO-2018-0154 was NOTED

PRO-2018-0154R01 was AGREED

| PRO-2018-0155R01 | CreateLocationPolicyImmediateResponse_R3 | C-DOT |
| --- | --- | --- |

The flow is new, it has not been copied from either TS-0001 or TS-0004.

C-DOT to work with Echo to align between OMA/3GPP/location

This was previously noted during PRO 35

PRO-2018-0155R01 was NOTED

| PRO-2018-0173 | deviceIdentifier_Definition_Change_R3 | Convida |
| --- | --- | --- |

PRO-2018-0173 was NOTED

| PRO-2018-0170R02 | notifyAggregation_supplement_R2 | KETI |
| --- | --- | --- |

Presented by In Song on Friday session-3 PRO

This contribution proposes to add a missing attribute notifyAggregation

Comment:

- Edited online.

PRO-2018-0170R02 was NOTED

PRO-2018-0170R03 was AGREED

| PRO-2018-0172R01 | notifyAggregation_supplement_R3 | KETI |
| --- | --- | --- |

Presented by In Song on Friday session-3 PRO

Mirror CR of PRO-2018-0170R02

- Editorial made on the mirror would need to be reflected.

PRO-2018-0172R01 was NOTED

PRO-2018-0172R02 was AGREED

| PRO-2018-0180 | Editorial corrections to TS-0004 - R3 | PRO WG Chair |
| --- | --- | --- |

Presented by Peter on Friday session-3 PRO

This contribution proposes a set of miscellaneous editorial changes and corrections to R3. These include ones that were made to R2a prior to publication, but which weren’t reflected in R3.

PRO-2018-0180 was AGREED

| PRO-2018-0145R02 | locationStatusEnum_R3 | C-DOT |
| --- | --- | --- |

It will be addressed in future conference calls or WG meetings.

PRO-2018-0145R02 was POSTPONED

| PRO-2018-0147R02 | locationStatusEnum_R2 | C-DOT |
| --- | --- | --- |

It will be addressed in future conference calls or WG meetings.

PRO-2018-0147R02 was POSTPONED

| PRO-2018-0176R01 | ChildResourceRef_R3 | Convida |
| --- | --- | --- |

It will be addressed in future conference calls or WG meetings.

PRO-2018-0176R01 was POSTPONED

| PRO-2018-0175 | ts0004_networkCoordinated_R3 | Convida |
| --- | --- | --- |

It will be addressed in future conference calls or WG meetings.

PRO-2018-0175 was POSTPONED

6.2	Contributions on TS-0009: HTTP binding

| ARC-2018-0125 | Partial Update | KT |
| --- | --- | --- |

Presented by Francisco on Wednesday session-1 PRO

In order to review the contribution PRO-2015-0833R02, Francisco presented first the contribution ARC-2018-0125.

No disposition as it is an ARC document review in PRO session.

| PRO-2015-0833R02 | HTTP Method | KT |
| --- | --- | --- |

Presented by Francisco on Wednesday session-1 PRO

Update operation is mapped to PUT or POST. PUT method is for full Update and POST method is for partial Update. The POST method is used for Create, partial Update, Notify operation of M2M message. A Receiver needs to identify POST method for three kinds of operations. To reduce complexity, it is proposed in the contribution to consider PATCH method.

Comment

- We need more off line discussion. It needs to be raise again on Joint ARC/PRO

PRO-2015-0833R02 was NOTED

| PRO-2018-0164 | UnsupportedMediaType_Status_Addition_HTTP(R3) | C-DOT |
| --- | --- | --- |

Presented by Prateek on Wednesday session-1 PRO

If the Originator sends a request with Content-Type value which is not supported by the Hosting CSE, it shall return an appropriate error code back to the originator. Currently there is no status code mapped for this, though it is available for Accept type (406 NOT_ACCEPTABLE).

Thus this CR introduces new status code namely “UNSUPPORTED_MEDIA_TYPE” which maps to 415 ( Unsupported Media Type ) in HTTP RFC.

Comment:

- It is suggested to use the new code 4015 for Unsupported Media Type

- Question: There is already a code 4102 for CONTENTS_UNACCEPTABLE? Could it be used?

Revision expected

PRO-2018-0164 was NOTED

PRO-2018-0164R01 Presented by Prateek on Thursday session-2 PRO

PRO-2018-0164R01 was AGREED

| PRO-2018-0165 | UnsupportedMediaType_Status_Addition_HTTP(R2) | C-DOT |
| --- | --- | --- |

Presented by Prateek on Wednesday session-1 PRO

Mirror CR of PRO-2018-0164

It is suggested to use the new code 4015 for Unsupported Media Type

PRO-2018-0165 was NOTED

PRO-2018-0165R01 Presented by Prateek on Thursday session-2 PRO

PRO-2018-0165R01 was AGREED

| PRO-2018-0084R02 | TS-0009 RSC Mapping R3 | Qualcomm Inc. |
| --- | --- | --- |

Presented by Wolfgang on Wednesday session-2 PRO

Revision needed to reflect the changes in track mode.

PRO-2018-0084R02 was NOTED

PRO-2018-0084R03 was AGREED

| PRO-2018-0080 | TS-0009 Primitive Mapping R3 | Qualcomm Inc. |
| --- | --- | --- |

Presented by Wolfgang on Wednesday session-2 PRO

This CR proposes to define mappings from newly defined primitive parameters in Release 3 to HTTP binding options.

PRO-2018-0080 was AGREED

| PRO-2018-0112R01 | TS-0004 Reference Update R3 | TS-0004 Rapporteur (Nobu Uchida) |
| --- | --- | --- |

Presented by Wolfgang on Friday session-3 PRO

This CR is proposing some modifications related that some of the RFC references are obsoleted.

PRO-2018-0112R01 was NOTED

PRO-2018-0112R02 was AGREED

| PRO-2018-0113R01 | TS-0004 Reference Update R2 | TS-0004 Rapporteur (Nobu Uchida) |
| --- | --- | --- |

Presented by Wolfgang on Friday session-3 PRO

Mirror CR of PRO-2018-0112R01

PRO-2018-0112R01 was NOTED

PRO-2018-0112R02 was AGREED

| PRO-2018-0178 | request optionality for locationID attribute correction R3 | BOE, Convida, KETI |
| --- | --- | --- |

Presented by Albert on Friday session-3 PRO

PRO-2018-0178 was AGREED

| PRO-2018-0179 | request optionality for locationID attribute correction R2 | BOE, Convida, KETI |
| --- | --- | --- |

Presented by Albert on Friday session-3 PRO

PRO-2018-0179 was AGREED

6.3	Contributions on TS-0008: CoAP binding

| PRO-2018-0085R01 | TS-0008 RSC Mapping R3 | Qualcomm Inc. |
| --- | --- | --- |

Presented by Wolfgang on Wednesday session-1 PRO

In Release 3, additional RSCs have been defined in TS-0004. The corresponding updates are required in TS-0008.

Comment:

- typo fixed, in some of the RSC , already present in the TS-0008.

PRO-2018-0085R01 was NOTED

PRO-2018-0085R02 was AGREED

| PRO-2018-0081 | TS-0008 Primitive Mapping R3 | Qualcomm Inc. |
| --- | --- | --- |

Presented by Wolfgang on Wednesday session-2 PRO

This CR proposes to define mappings from newly defined primitive parameters in Release 3 to CoAP binding options.

Comment:

- One change made on the format of oneM2M-ASRI

PRO-2018-0081 was NOTED

PRO-2018-0081R01 was AGREED

| PRO-2018-0149R01 | Clarification_non-blocking_coap_R3 | C-DOT |
| --- | --- | --- |

Presented by Neeta on Wednesday session-4 PRO

The TS-0008 is not aligned with the text in TS-0004 for the non-blocking CoAP use case.

Comment:

- RSC 1001 and 1002 are not used in CoAP at the moment.

Long discussion raised on which RSC should be used 1000 or 1001 and 1002

PRO-2018-0149R01 was left open

PRO-2018-0149R01 Presented by Neeta on Thursday session-2 PRO

PRO-2018-0149R01 was NOTED

| PRO-2018-0150R01 | Clarification_non-blocking_coap_R2 | C-DOT |
| --- | --- | --- |

Mirror CR of PRO-2018-0149R01

PRO-2018-0150R01 was NOTED

| PRO-2018-0166R01 | UnsupportedMediaType_Status_Addition_CoAP(R3) | C-DOT |
| --- | --- | --- |

Presented by Prateek on Thursday session-2 PRO

PRO-2018-0166R01 was AGREED

| PRO-2018-0167R01 | UnsupportedMediaType_Status_Addition_CoAP(R2) | C-DOT |
| --- | --- | --- |

Presented by Prateek on Thursday session-2 PRO

PRO-2018-0167R01 was AGREED

| PRO-2018-0177R01 | TS-0008_multicastSecurity | Qualcomm Inc. (TIA) |
| --- | --- | --- |

Presented by Wolfgang on Thursday session-5 PRO/SEC

Review of this contribution which is linked to SEC-2018-0064 discussed at the same session, mainly to check if it is not contradictory regarding the text in SEC-2018-0064

It is suggested to mention in clause B.1 of TS-0008 that DTLS is not applicable for Multicast. It is also suggested to indicate this in the TS-0008 clause 7 Security Consideration

Revision expected

PRO-2018-0177R01 was NOTED

PRO-2018-0177R02 Presented by Wolfgang on Friday session-3 PRO

This contribution has also been reviewed in SEC. This revision refelects the change in agreed SEC-2018-0064R02.

PRO-2018-0177R02 was NOTED

PRO-2018-0177R03 was AGREED

6.4	Contributions on TS-0020: WebSocket binding

| PRO-2018-0157 | TS-0020_WebSocket_subprotocol_names_R2 | Qualcomm Inc. |
| --- | --- | --- |

Presented by Wolfgang on Wednesday session-2 PRO

This CR updates the notation of WebSocket subprotocol names defined in TS-0020. Since oneM2M protocol version indication is now included in the request and response primitives itself there is no need to indicate this information in the subprotocol name.

Comment:

- Minor editorial , fixed online

PRO-2018-0157 was NOTED

PRO-2018-0157R01 was AGREED

7	Planning for next Meetings

7.1	Conference calls

  - TBD

7.2	Face to Face

- PRO#37		Face to face  	17-21 Sept 2018		Bundang (KR)

8	Any other business

9	Closure of meeting

The Chair Peter thanked the participants for the successful meeting and wished them a safe trip home, then he closed the meeting.