| CHANGE REQUEST |
| --- |
| Meeting:* | TP37 |
| Source:* | InterDigital |
| Date:* | 2018-08-30 |
| Contact:* | Bob Flynn (bob.flynn@interdigital.com) |
| Reason for Change/s:* | ContentInfo XSD |
| CR against: Release* | Rel-2 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004-V2.18.0 |
| Clauses/Sub Clauses* | CDT-commonTypes-v2_18_0 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

While exploring the contentInfo attribute of a <contentInstance> we found that the XML schema does not properly enforce the defined structure.

Table 6.3.3-1: oneM2M Simple Data Types

| m2m:contentInfo | Content Information | application/xml:1 application/xml:1:0 application/xml:1:5 | A string consisting of a media type followed by a m2m:encodingType and optional m2m:contentSecurity, each separated by ':' character. If the m2m:contentSecurity value is not present, then the preceding ':' shall also be not present. If the m2m:contentSecurity value is not present then this has the same interpretation as a value of 0 for m2m:contentSecurity. See note. |
| --- | --- | --- | --- |

Based on this definition, the goal of the m2m:contentInfo schema is to enforce the following pattern

<mediaType>:<m2m:encodingType>[:<m2m:contentSecurity>]

Where

<mediaType> is not clearly defined but many examples exist that imply “application domain interpretation”

<mediaType> seems to allow “:” embedded (audio:AVP video:RTS/AVP) -> that could be mixing some of the use below.

<m2m:encodingType> is mandatory in the value 0,1,2

<m2m:contentSecurity> is optional in the value 0,1,2,3,4,5

This is the definition from commonTypes.xsd

<xs:simpleType name="cnf">

<xs:restriction base="xs:string">

<xs:pattern value="[\w/!#$^_.+&amp;\-]+(:[0-2])?"/>

<xs:pattern value="[\w/!#$^_.+&amp;\-]+((:[0-2])?)+((:[0-5])?)"/>

</xs:restriction>

</xs:simpleType>

This definition allows the following illegal or  ambiguous values

[1] foo [true]

[1] foo/bar [true]

[1] foo/bar/baz [true]

[1] foo/bar/baz/qux [true]

[1] /////   [true]

[1] !!!!!   [true]

[1] _____   [true]

[1] ^^^^^   [true]

[1] #####   [true]

[1] +++++   [true]

[1] -----   [true]

[1] &&&&&   [true]

[1] $$$$$   [true]

[1] .....   [true]

[1] 12345   [true]

[1] 12345/6789  [true]

[1] foo/bar:1:1:1:1:1:1 [true]

The following pattern gets closer to the desired result, rejecting all of the values above.

<xs:simpleType name="cnf">

<xs:restriction base="xs:string">

<xs:pattern value="^[^ ()<>@,;:\\=\"\/\[\]?]+\/[^ ()<>@,;:\\=\"\/\[\]?]+:[0-2](?::[0-5])?$"/>

</xs:restriction>

</xs:simpleType>

However, it still does not handle some of the media types referenced in TS-0004, such as the following:

| m2m:sessionCapabilities | Session Capability | audio:AVP video:RTS/AVP | Pair(s) of media type and corresponding protocol as defined in Session Description Protocol (IETF RFC 4566 [52]. The delimiter ofbetween the media type and the protocol is colon. |
| --- | --- | --- | --- |

Proposal is to remove the pattern for containerInfo as

- The current definition is a bug as it does not enforce the defined requirement for the m2m:encodingType

The argument there is that the generator of the content can define the data, perhaps using the semantic descriptor attributes.

Alternate proposal #1 is to make a proper definition that conforms to RFC2045.

Alternate proposal #2, reflected in change 1, is to use a pattern that gets us a bit closer to the desired result.

Based on informal discussion, we agreed to explore a pattern that better meets the intended purpose.

## ----------------------- Start of change 1 -----------------------

- <xs:simpleType name="cnf">

- <xs:restriction base="xs:string">

- <xs:pattern value="^[^ ()<>@,;:\\=\"\/\[\]?]+\/[^ ()<>@,;:\\=\"\/\[\]?]+:[0-2](?::[0-5])?$"/>

- </xs:restriction>

- </xs:simpleType>

## ----------------------- End of change 1 -----------------------

## ----------------------- Start of change 2 -----------------------

## ----------------------- End of change 2 -----------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?