| CHANGE REQUEST |
| --- |
| Meeting ID:* | PRO 37 |
| Source:* | Francisco Sang-Eon Kim, KT, kim.sangeon@kt.com |
| Date:* | 2018-09-09 |
| Reason for Change/s:* | Consistency between TS-0004 and TS-0008 |
| CR against: Release* | Release 3 |
| CR against: WI* | Active MNT maintenance / Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / WI-0050 |
| CR against: TS/TR* | TS-0008-V3.1.0 |
| Clauses * | 6.2.1 Header |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality |
| Impacted other TS/TR(s) | None |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

CoAP message format specified at section 3 in RFC 7252.

In case of a request, the Code field indicates the Request Method; in case of a response, a Response Code.

The IANA controls ‘Code’ for CoAP method that available at https://www.iana.org/assignments/core-parameters/core-parameters.xhtml as following

| Code | Name | Reference |
| --- | --- | --- |
| 0.01 | GET | [RFC7252] |
| 0.02 | POST | [RFC7252] |
| 0.03 | PUT | [RFC7252] |
| 0.04 | DELETE | [RFC7252] |
| 0.05 | FETCH | [RFC8132] |
| 0.06 | PATCH | [RFC8132] |
| 0.07 | iPATCH | [RFC8132] |
| 0.08-0.31 | Unassigned |  |

### -----------------------Start of change 1-------------------------------------------

### 6.2.1	Header

This clause specifies how to configure CoAP header information:

The Version field shall be configured as 1.

The Type field shall be configured according to clause 6.3. The Reset message is used to send a error message in response to a malformed Confirmable message in CoAP layer.

In case of a request, the Code field indicates CoAP Method. The oneM2M Operation parameter shall be mapped to a CoAP Method according to the table 6.2.1-1.

In case of a response, the Code field indicates CoAP Response Code. The oneM2M Response Status Code parameter shall be mapped to CoAP Response Code as specified in clause 6.2.4.

The configurations of Token Length and Message ID are left to implementation.

Table 6.2.1-1: oneM2M Operation Parameter Mapping

| oneM2M Operation Parameter | CoAP Method | CoAP Method Code |
| --- | --- | --- |
| CREATE | POST | 0.02 |
| RETRIEVE | GET | 0.01 |
| UPDATE | PUT | 0.03 |
| DELETE | DELETE | 0.04 |
| NOTIFY | POST | 0.02 |

At the Receiver, CoAP request message with POST method shall be mapped to oneM2M CREATE or NOTIFY Operation parameter in accordance with the existence of Resource Type parameter.  If Resource Type parameter exists then value of the Operation parameter is CREATE and if Resource Type parameter doesn't exist, the value of Operation parameter is NOTIFY.

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?