| CHANGE REQUEST |
| --- |
| Meeting ID:* | PRO#38 |
| Source:* | NTT |
| Date:* | 2018-12-06 |
| Contact:* | Kei Harada(harada.kei@lab.ntt.co.jp), NTT, |
| Reason for Change/s:* | Add a short note for the Delete operation of <fanOutPoint> |
| CR against: Release* | R3 |
| CR against: WI* | Active < > MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No STE Small Technical Enhancements / < WI-0087> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004 |
| Clauses * | 7.4 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | None |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

There is no detail expression for one of the note for <fanOut Point> deletion, so this CR adds  some expression for it.

This work is based on PRO action items (PRO-2018-0246-PRO_work_remaining_for_R3)  following:

Other TS-0004 issues that we are aware of (may need CRs to fix)

8. Clarify bullet in 7.4.14.3.5 that says "A Delete operation targeting a <fanOutPoint> does not remove members from the parent <group>."

## -----------------------Start of change 1-------------------------------------------

#### <fanOutPoint> resource specific procedure on CRUD operations

##### Introduction

This sub-clause describes <fanOutPoint> resource specific behaviour for CRUD operations.

##### Create

A Create operation sent to a <fanOutPoint> is fanned out to the members (if any) of the parent <group>. It is equivalent to sending a Create to each member and therefore results in new resources being created as children of these existing members.

If the Create is sent to a hierarchical URI containing a fanOutPoint and an additional path relative to that fanOutPoint then the new resources are not created as immediate children of the members, rather they are created as children of descendents of those members (as determined by the relative path).

Originator:

Primitive specific operation after Orig-1.0 "Compose Request primitive" and before Orig-2.0 "Send the Request to the receiver CSE": In the case the Originator wants to subscribe to all the member resources of the group and the originator wants the group hosting CSE to aggregate all the notifications come from its member hosting CSEs, the Originator shall include notificationForwardingURI attribute in the <subscription> resource.

If the Response Status Code in individual responses are other than CREATED then the Originator may issue a new CREATE request to the group Hosting CSE with Group Request Target Members parameter set in request containing list of members for which CREATE has failed.

Receiver:

Primitive specific operation after Recv-6.2 "Check existence of the addressed resource" and before Recv-6.3 "Check authorization of the Originator".

Primitive specific operation additional to Recv-6.3 "Check authorization of the Originator": The Group Hosting CSE shall check the authorization of the Originator based on the membersAccessControlPolicyIDs of the parent <group> resource. In the case the membersAccessControlPolicyIDs is not provided, the accessControlPolicyIDs of the parent <group> resource shall be used.

Primitive specific operation to replace Recv-6.5"Create/Update/Retrieve/Delete/Notify operation is performed" and Recv-6.6"Announce/De-announce the resource" in the generic procedure:

- Validate the type of resource to be created, refer to clause 7.4.14.2.1.

If the members are not in the Multicast Group Information locally, then perform Sub-group creation for members residing on the same CSE, refer to clause 7.4.14.2.2.

Assign URI for aggregation of notification, refer to clause 7.4.14.2.3.

If there is Multicast Group Information locally, the receiver shall perform the Multicast fan out procedure, refer to clause 7.4.14.2.6.  For the members which are not in the multicast group, the receiver shall perform  Fanout Request to each member, refer to clause 7.4.14.2.4.

Aggregation of member responses, refer to clause 7.4.14.2.5.

##### Retrieve

Originator:

No primitive specific operations.

If the Response Status Code in individual responses is other than OK then the Originator may issue a new RETRIEVE request to the group Hosting CSE with Group Request Target Members parameter set in request containing list of members for which RETRIEVE has failed.

Receiver:

Primitive specific operation after Recv-6.2 "Check existence of the addressed resource" and before Recv-6.3 "Check authorization of the Originator".

Primitive specific operation additional to Recv-6.3 "Check authorization of the Originator": The Group Hosting CSE shall check the authorization of the Originator based on the membersAccessControlPolicyIDs of the parent group resource. In the case the membersAccessControlPolicyIDs is not provided, the accessControlPolicyIDs of the parent group resource shall be used.

Primitive specific operation to replace Recv-6.5"Create/Update/Retrieve/Delete/Notify operation is performed" and Recv-6.6 "Announce/De-announce the resource" in the generic procedure:

- If the members are not in the Multicast Group Information locally, then perform Sub-group creation for members residing on the same CSE, refer to 7.4.14.2.2.

- If there is Multicast Group Information locally, the receiver shall perform the Multicast fan out procedure, refer to clause 7.4.14.2.6.  For the members which are not in the multicast group, the receiver shall perform  Fanout Request to each member, refer to 7.4.14.2.4.

- Aggregation of member responses, refer to clause 7.4.14.2.5.

##### Update

Originator:

No primitive specific operations.

If the Response Status Code in individual responses is other than UPDATED then the Originator may issue a new UPDATE request to the group Hosting CSE with Group Request Target Members parameter set in request containing list of members for which UPDATE has failed.

Receiver:

Primitive specific operation after Recv-6.2 "Check existence of the addressed resource" and before Recv-6.3 "Check authorization of the Originator".

Primitive specific operation additional to Recv-6.3 "Check authorization of the Originator": The Group Hosting CSE shall check the authorization of the Originator based on the membersAccessControlPolicyIDs of the parent group resource. In the case the membersAccessControlPolicyIDs is not provided, the accessControlPolicyIDs of the parent group resource shall be used.

Primitive specific operation to replace Recv-6.5 "Create/Update/Retrieve/Delete/Notify operation is performed" and Recv-6.6"Announce/De-announce the resource" in the generic procedure:

- If the members are not in the Multicast Group Information locally, then perform Sub-group creation for members residing on the same CSE , refer to 7.4.14.2.2.

- If there is Multicast Group Information locally, the receiver shall perform the Multicast fan out procedure, refer to clause 7.4.14.2.6.  For the members which are not in the multicast group, the receiver shall perform Fanout Request to each member. See Clause 7.4.14.2.4.

- Aggregation of member responses, refer to clause 7.4.14.2.5.

##### Delete

The primitive deletes the member resources and their child resources belonging to an existing <group> resource.

Originator:

No primitive specific operations.

If the Response Status Code in individual responses is other than DELETED then the Originator may issue a new DELETE request to the group Hosting CSE with Group Request Target Members parameter set in request containing list of members for which DELETE has failed.

Receiver:

Primitive specific operation after Recv-6.2 "Check existence of the addressed resource" and Recv-6.3 "Check authorization of the Originator": The To parameter consists of the URI of the group resource plus a suffix consisting of /fanOutPoint or /fanOutPoint/plus any additional appended relative address.

Primitive specific operation additional to Recv-6.3 "Check authorization of the Originator": The Group Hosting CSE shall check the authorization of the Originator based on the membersAccessControlPolicyIDs of the parent group resource. In the case the membersAccessControlPolicyIDs is not provided, the accessControlPolicyIDs of the parent group resource shall be used.

Primitive specific operation to replace Recv-6.5"Create/Update/Retrieve/Delete/Notify operation is performed" and Recv-6.6"Announce/De-announce the resource" in the generic procedure:

- If the members are not in the Multicast Group Information locally, then perform Sub-group creation for members residing on the same CSE , refer to 7.4.14.2.2

- If there is Multicast Group Information locally, the receiver shall perform the Multicast fan out procedure, refer to clause 7.4.14.2.6.  For the members which are not in the multicast group, the receiver shall perform Fanout Request to each member. See Clause 7.4.14.2.4

- Aggregation of member responses, refer to clause 7.4.14.2.5.

- If members respond with a DELETED Response Status Code, the <group> hosting CSE shall remove the members from the membersIDs attribute of the targeted <group> unless the member type is <latest> or <oldest>.

## -----------------------End of change 1-------------------------------------------