| INPUT CONTRIBUTION Initial requirements subset |
| --- |
| Group Name:* | REQ discussion at TP2 |
| Title:* | Initial requirements subset |
| Source:* | Telecom Italia (ETSI) |
| Contact: | Enrico Scarrone |
| Date:* | 2012-11-30 |
| Abstract:* | Initial requirements derived from ETSI TS 102 689 V2.0.3, M2M service requirements, this includes general requirements, management, charging and functional requirements. This requirements has been revised based on comments received after the presentation at the REQ-ARC electronic meeting calls. |
| Agenda Item:* | Requirements |
| Work item(s): | Requirements |
| Document(s) Impacted* | Requirement specification (number to be assigned) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Discussion and initial agreement for potential inclusion in the requirement TS at the TP2 meeting |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

NOTE: For definition of capitalized elements please refer to ETSI TR 102 725 in the pool.

The relevant used definitions are expected to be transferred in oneM2M documentation, as soon as the documentation structure for definitions in oneM2M will be defined.

| Requirement ID | Classification | Requirement Text |
| --- | --- | --- |

| 1 (Final number to be assigned ) | General requirements -M2M Application communication principles | The M2M System shall be able to allow communication between M2M Applications in the Network Domain, and the M2M Device Domain, by using multiple communication means based on IP Access. |
| --- | --- | --- |
| 1bis (Final number to be assigned ) | General requirements - M2M Application communication principles | The M2M System should abstract the underlying network structure. |
| 2 (Final number to be assigned ) | General requirements -Message Delivery for sleeping devices | The M2M System shall be able to manage communication towards a device which is not continuosly reachable |
| 3 (Final number to be assigned ) | General requirements - transmission scheduling | The M2M System shall be able to manage the scheduling of network access and of messaging. |
| 3bis (Final number to be assigned ) | General requirements - transmission scheduling | The M2M System shall be aware of the scheduling delay tolerance needed by the M2M Application and should schedule the communication acccordingly. |
| 4 (Final number to be assigned ) | General requirements - communication path selection | When multiple paths are available, the M2M System shall be able to select communication paths, based on e.g. policies or rely on routing mechanisms in case of transmission failures. |
| 5 (Final number to be assigned ) | General requirements -Communication with devices behind a M2M Gateway | The M2M System should be able to communicate with M2M Devices behind a M2M Gateway. |
| 6 (Final number to be assigned ) | General requirements -Communication failure notification | M2M Applications, requesting reliable delivery of a message, shall be notified of any failures to deliver the message. |
| 7 (Final number to be assigned ) | General requirements Scalability | The M2M System shall be scalable in terms of number of connected Thing. |
| 8 (Final number to be assigned ) | General requirements Abstraction of technologies heterogeneity | The M2M Gateway may be capable of interfacing to various M2M Area Network technologies. |
| 9 (Final number to be assigned ) | General requirements . M2M Service Capabilities discovery and registration | The M2M System shall support mechanisms to allow M2M Applications to discover M2M Service Capabilities offered to them. Additionally the M2M Device and M2M Gateway shall support mechanisms to allow the registration of its M2M Service Capabilities to the M2M system. |
| 10 (Final number to be assigned ) | General requirements -M2M Trusted Application | The M2M Core may handle service request responses for trusted M2M Applications by allowing streamlined authentication procedures for these applications. |
| 11 (Final number to be assigned ) | General requirements- Mobility | If the underlying network supports seamless mobility and roaming, the M2M System shall be able to re-use such mechanisms. |
| 12 (Final number to be assigned ) | General requirements - Communications integrity | The M2M System shall support mechanisms to assure communications integrity for M2M services. |
| 13 (Final number to be assigned ) | General requirements -Device/Gateway integrity check | The M2M System may support M2M Device and M2M Gateway Integrity Validation. |
| 14 (Final number to be assigned ) | General requirements -Continuous connectivity | The M2M System shall support M2M applications accessing the M2M system by means of a continuous connectivity. |
| 14bis (Final number to be assigned ) | General requirements -non Continuous connectivity | The M2M System shall support M2M applications accessing the M2M system by means of a non continuous connectivity. |
| 15 (Final number to be assigned ) | General requirements -Confirm | The M2M System may support mechanisms to confirm messages. delivering the confirmation in a time that is configurable e.g 1s. |
| 16 (Final number to be assigned ) | General requirements -Logging | Communications within the M2M system shall be capable of being logged. Important events (e.g. received information from the M2M Device or M2M Gateway is faulty, unsuccessful installation attempt from the M2M Device or M2M Gateway, service not operating, etc.) may be logged together with diagnostic information. Logs shall be retrievable upon request. |
| 16 (Final number to be assigned ) | General requirements -Logging | Important events (e.g. received information from the M2M Device or M2M Gateway is faulty, unsuccessful installation attempt from the M2M Device or M2M Gateway, service not operating, etc.) should be logged together with diagnostic information. |
| 16ter (Final number to be assigned ) | General requirements -Logging | Logs shall be retrievable upon request. |
| 17 (Final number to be assigned ) | General requirements -Time Stamp | The M2M System shall support accurate and time stamping of the managed M2M communications. |
| 18 (Final number to be assigned ) | General requirements Device/Gateway failure robustness | After a non-destructive failure, e.g. after a power supply outage, a M2M Device or Gateway should immediately return in a full operating state autonomously, after performing the appropriate initialization e.g. Integrity Validation if supported. |
| 19 (Final number to be assigned ) | General requirements -Operator telco capabilities exposure | The M2M interface to the external M2M applications shall enable the exposition of telco operator capabilities (e.g. SMS, USSD, localization, subscription configuration, authentication (e.g. Generic Bootstrapping Architecture), etc). |
| 19bis (Final number to be assigned ) | General requirements -Operator telco capabilities exposure | The undrelaying networks and telco operator resources shall be abstracted as M2M resources to provide to the applications a consistent use of the M2M system capabilities. |
| 20 (Final number to be assigned ) | General requirements -Location reporting support | The M2M System shall be able to report M2M Device/Gateway location to M2M applications when this information is available. The location information of the M2M device/M2M gateway can be determined by the underlying network procedures (taking into account relevant privacy/security settings for transfer of such information), by application-level information reported from the M2M device/ gateway application, or a combination of both. |
| 21 (Final number to be assigned ) | General requirements -Support of multiple M2M Applications | The M2M System shall support a mechanism to manage a multiple M2M Applications and to provide a mechanism to interact between multiple M2M Applications. |
| 22 (Final number to be assigned ) | General requirements Support for subscribing to receive notification | The M2M System shall support a mechanism for allowing applications to subscribe and being notified of changes. |
| 23 (Final number to be assigned ) | General requirements -Support for optimizing notification | The M2M System may support a mechanism for delaying notifying a Connected Objects. |
| 24 (Final number to be assigned ) | General requirements -Support for aggregated and delayed communications | The M2M System may support a mechanism to manage a remote access of information from Applicationa and shall be able to aggregate requests and delay to perform the request depending on a given delay and/or category. |
| 25 (Final number to be assigned ) | General requirements -Multiple M2M Service Providers | An Application on a in a M2M system (M2M Device, Gateway or Core)shall be able to operate resources belonging to a different M2M systems. |
| 26 (Final number to be assigned ) | Management - Fault Management: Proactive monitoring | The M2M System shall be capable of proactively monitoring the M2M system in order to attempt to prevent and correct errors. |
| 27 (Final number to be assigned ) | Management -Fault Management: Diagnostics mode | The M2M System shall provide the means to allow diagnostics for M2M Application functioning. |
| 28 (Final number to be assigned ) | Management -Fault Management: Connectivity test | The M2M System shall support testing the connectivity towards a selected set of Applications at regular intervals provided the Applications support the function. |
| 29 (Final number to be assigned ) | Management Fault Management: Fault discovery and reporting | The Applications and their resources operational status shall be monitorable, |
| 30 (Final number to be assigned ) | Management - Fault Management: Fault Recovery by Remote Management | M2M devices and Gateway may support remote management for fault recovery e.g. firmware update. After this operation of firmware update, the device may reboot to a known and consistent state. |
| 31 (Final number to be assigned ) | Management -Configuration Management: Pre-provisioning and auto configuration of the M2M Devices and Gateways | The pre-provisioning mechanism shall be able to work even when the communication path to the M2M Device/Gateway is absent. |
| 31 (Final number to be assigned ) | Management -Configuration Management: Pre-provisioning and auto configuration of the M2M Devices and Gateways | The M2M System shall support mechanisms to perform simple and scalable pre-provisioning of M2M Devices/Gateways. |
| 31 (Final number to be assigned ) | Management -Configuration Management: Pre-provisioning and auto configuration of the M2M Devices and Gateways | The pre-provisioning mechanism shall be able to work even when the communication path to the M2M Device/Gateway is absent. |
| 32 (Final number to be assigned ) | Management -Configuration Management: M2M Area Network resilience | An M2M Device or M2M Gateway experiencing a fault shall not affect the normal operation of the M2M Area Network. |
| 33 (Final number to be assigned ) | Management -Configuration Management: Time synchronisation | The M2M System should support time synchronisation. M2M Devices and M2M Gateways may support time synchronization. The level of accuracy and of security for the time synchronization can be system specific. |
| 33 (Final number to be assigned ) | Management -Configuration Management: Configuration Management | The M2M System shall support configuration management (i.e. manageability will depend on the end-system). |
| 34 (Final number to be assigned ) | Accounting and Charging -Charging recorded information | The M2M system shall be able to record charging specific information. The format of the recorded information shall be fully specified including mandatory and optional elements. |
| 34 (Final number to be assigned ) | Accounting and Charging -Charging recorded information | The M2M system shall support correlation between the charging records of the M2M service layer and available charging records from the Core/Access Network. |
| 35 (Final number to be assigned ) | Accounting and Charging - Offline Charging | The M2M system shall support offline charging at the M2M service layer. |
| 36 (Final number to be assigned ) | Accounting and Charging - Online Charging | TheM2M system shall support online charging at the M2M service layer. |
| 37 (Final number to be assigned ) | Accounting and Charging -Operational requirement | The M2M system shall be able to reuse existing charging mechanisms of Mobile and/or Fixed networks. |
| 38 (Final number to be assigned ) | Accounting and Charging -Security for charging | The M2M system shall be able to provide integrity protection of the stored and transferred charging related information (e.g. CDRs). |
| 39 (Final number to be assigned ) | Functional requirements -Data collection & reporting | The M2M System shall support the reporting from a specific M2M Device or M2M Gateway or group of M2M Devices or group of M2M Gateways in the way requested by the M2M Application as listed below: a periodic reporting with the time period being defined by the M2M application; an on-demand reporting with two possible modes. One is an instantaneous collecting and reporting of data, the other one is a reporting of the data that were pre-recorded at the indicated specific time period; a scheduled reporting; or an event-based reporting. |
| 41 (Final number to be assigned ) | Functional requirements -Group mechanisms | The M2M System shall support a mechanism to create and remove groups, and to introduce an entity into a group, modify the invariants (i.e. characteristics) of the members in a group, remove an entity from a group, list members of a group, check for an entity's membership in a group, search entities in a group, and identify all groups where the entity is a member. |
| 42 (Final number to be assigned ) | Functional requirements -M2M Devices/Gateways type varieties | The M2M System shall be able to support a variety of different M2M Devices/Gateways types, e.g. active M2M Devices and sleeping M2M Devices, upgradable M2M Devices/Gateways and not upgradable M2M Devices/Gateways. |
| 43 (Final number to be assigned ) | Functional requirements Information reception | The M2M System shall support the following mechanisms for receiving information from M2M Devices and M2M Gateways: Receiving unsolicited information (passive retrieval). Receiving scheduled information. Operating particular algorithms for retrieving information (e.g. round robin, random within given time window, round robin groups with random reply in given time window). |
| 44 (Final number to be assigned ) | Functional requirements -Reachability | The M2M System may be aware of the reachability state of the Applications. |
| 45 (Final number to be assigned ) | Functional requirements -Asymmetric flows | M2M Devices and Gateways should support asymmetric communication flows. |
| 46 (Final number to be assigned ) | Functional requirements -Paths diversity | The M2M System should support physical paths diversity if required by the M2M Application. |
| 47 (Final number to be assigned ) | Functional requirements -Heterogeneous M2M Area Networks | The M2M System shall be capable of interfacing heterogeneous M2M Area Networks at the M2M Gateway. |
| 48 (Final number to be assigned ) | Functional requirements -Information collection & delivery to multiple applications | The M2M System shall support the ability for multiple M2M Applications to interact with the same M2M Devices simultaneously. |
| 49 (Final number to be assigned ) | Functional requirements Management of multiple M2M Devices/Gateways | The M2M System shall support the ability for multiple M2M Applications to interact with the multiple M2M Devices/Gateways simultaneously. |
| 50 (Final number to be assigned ) | Functional requirements- M2M Devices/Gateways chracteristics awareness | M2M characteristics of the M2M Device/Gateway may be either preconfigured in the M2M System or provided by the M2M Device/Gateway to the M2M System; the characteristics provided by the M2M Device/Gateway take precedence over the preconfigured characteristics. M2M characteristics consist of the static information such M2M capabilities that may be assigned to M2M Devices and Gateways and the dynamic information such as location, state, availability, that may be associated to M2M Devices and Gateways. |
| 51 (Final number to be assigned ) | Functional requirements - Data store and share | The M2M System shall be able to store and retrieve data to enable data sharing of stored data subjected to access control. |
| 52 (Final number to be assigned ) | Functional requirements -Multiple M2M service providers | A M2M System shall be able to forward M2M communications and information to another M2M System. |