| INPUT CONTRIBUTION Initial requirements subset |
| --- |
| Group Name:* | Joint REQ-ARC-WGs |
| Title:* | Operations and Management Requirements |
| Source:* | Alcatel-Lucent, Huawei |
| Contact: | Tim Carey, Yongjing Zhang |
| Date:* | 2012-11-22 |
| Abstract:* | Requirements for the Operations and Management service capability. These include Device Management, Capillary Network Management, Application Management, Data Collection, Charging and General Operations and Management requirements. |
| Agenda Item:* | Requirements |
| Work item(s): | Requirements |
| Document(s) Impacted* | Requirement specification (number to be assigned) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Discussion and initial agreement for potential inclusion in the requirement TS at the TP2 meeting |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

| Req Number | Category | Text |
| --- | --- | --- |
| 1 (Final number to be assigned ) | M2M Service Layer Management - Subscription | The M2M System shall be capable of storing information to identify subscriptions to M2M services. |
| 4 (Final number to be assigned ) | M2M Service Layer Management – Communication Network Administration | The M2M System shall be capable of administering services provided to the M2M System by the underlying Communication Network. |
| 5 (Final number to be assigned ) | Device Management - Provisioning | The M2M System shall be capable of maintaining configuration information of M2M Gateways/M2M Devices associated with a M2M service subscription. |
| 6 (Final number to be assigned ) | Device Management - Diagnostics | The M2M System shall be capable of executing the following types of diagnostics initiated by a M2M Device: One-time, on demand, synchronous One-time, on demand, asynchronous Scheduled, synchronous Scheduled, asynchronous |
| 7 (Final number to be assigned ) | Device Management - Diagnostics | The M2M System shall be capable of executing diagnostics initiated by a M2M Device to assess connectivity within the Connectivity Layer. |
| 8 (Final number to be assigned ) | Device Management - Diagnostics | The M2M System shall be capable of executing diagnostics initiated by a M2M Device to assess connectivity within the M2M Service Capability Layer. |
| 9 (Final number to be assigned ) | Device Management – Firmware Update | The M2M System shall be capable of updating the firmware of a M2M Gateway or Device. |
| 10 (Final number to be assigned ) | Device Management – Firmware Update | The M2M System shall be capable of scheduling an update for the firmware of a M2M Gateway or Device. |
| 11 (Final number to be assigned ) | Device Management – Software Update | The M2M System shall be capable of updating software modules that execute within the M2M Gateway or Device. |
| 12 (Final number to be assigned ) | Device Management - Software Update | The M2M System shall be capable of scheduling an update of software modules within the M2M Gateway or Device. |
| 13 (Final number to be assigned ) | Device Management – Information Retrieval | The M2M System shall be capable of retrieving information related to the environment (e.g., battery, memory, current time) of a M2M Gateway or Device. |
| 14 (Final number to be assigned ) | Device Management – Information Retrieval | The M2M System shall be capable of retrieving events and information logged by a M2M Gateway or Device. |
| 15 (Final number to be assigned ) | Device Management - Reset | The M2M System shall be capable of rebooting a M2M Gateway or Device. |
| 16 (Final number to be assigned ) | Device Management - Reset | The M2M System shall be capable of resetting a M2M Gateway or Device to a factory default configuration. |
| 20 (Final number to be assigned ) | Application Management – Software Update | The M2M System shall be capable of updating M2M Applications that execute within a Server. |
| 21 (Final number to be assigned ) | Application Management - Software Update | The M2M System shall be capable of scheduling an update for M2M Applications that execute within a Server. |
| 22 (Final number to be assigned ) | Application Management – Software Administration | The M2M System shall be capable of administrating an M2M Application (start, stop, install, uninstall, restart) that executes within a Server. |
| 23 (Final number to be assigned ) | Application Management – Log Retrieval | The M2M System shall be capable of retrieving events and information logged by a M2M Application. |
| 24 (Final number to be assigned ) | M2M Service Layer Management –Subscription | The M2M System shall be capable of identifying the M2M devices pertaining to a M2M service subscription by means of service level identification. . |
| 25 (Final number to be assigned ) | M2M Service Layer Management –Subscription | The M2M system shall be capable of associating the service level identification of an M2M device with the device identification capabilities offered by the underlying connectivity network. NOTE: In certain scenarios, it is possible to re-use the device identification provided by an underlying network as the service level identification of an M2M device. |
| 27 (Final number to be assigned ) | Security – Subscription | The M2M System shall utilize service level identification when establishing trust for M2M services within the M2M System. |
| 30 (Final number to be assigned ) | Device Management - Interworking | The M2M System shall provide the capability to manage devices enabled by different management technologies in a unified manner. |
| 31 (Final number to be assigned ) | Device Management - Grouping | The M2M System shall provide the capability to manage multiple devices in a grouped manner. |
| 32 (Final number to be assigned ) | Capillary Network Management - Discovery | The M2M System shall provide the capability to discover the capillary network including the device information and network topology. |
| 33 (Final number to be assigned ) | Capillary Network Management - Discovery | The M2M System shall provide the capability to notify the changes of the capillary network including the device information and network topology. |
| 34 (Final number to be assigned ) | Capillary Network Management – Information Description | The M2M System shall provide the capability to maintain and describe the information model of devices and topology of a capillary network. |
| 35 (Final number to be assigned ) | Capillary Network Management- Device Management | The M2M System shall provide the capability to manage the devices in a capillary network when supported by the device, including: Provisioning & configuration Diagnostics Software Management Device Reset |
| 36 (Final number to be assigned ) | Capillary Network Management - Topology | The M2M System shall provide the capability to manage the network topology of a capillary network when supported by the capillary network technology, including: Adding/removing devices to/from the capillary network Modifying the interconnection relationship between devices |
| 40 (Final number to be assigned ) | Operations and Management – Data Collection | The M2M System shall able to initiate information recording belonging to an M2M application or an M2M device for the purposes of charging and collection of statistics. |
| 41 (Final number to be assigned ) | Operations and Management – Data Collection | The M2M System shall provide the capability to initiate information recording based on predefined events, a request for service, invocation of a network capability. |
| 42 (Final number to be assigned ) | Operations and Management - Charging | The M2M System shall be able to support correlation between the charging records of the M2M service layer and available charging records the Connectivity Layer. |
| 43 (Final number to be assigned ) | Operations and Management - Charging | The M2M system shall support offline charging at the M2M service layer. |
| 44 (Final number to be assigned ) | Operations and Management - Charging | The M2M system shall support online charging at the M2M service layer. |

# Comments

Phil Jacobs: This seems broad, is it meant to indicate that it can test connectivity between the device and other entities, or also between two other entities?

Phil Jacobs: Can we make more of a distinction between 7 and 8?

Phil Jacobs: Can we combine 9 and 11?

Phil Jacobs: Can we combine 10 and 12?

Phil Jacobs: I could use a use case to help explain 20 21 and 22

Phil Jacobs: Logged by the device, gateway or network application?