| INPUT CONTRIBUTION Initial requirements subset |
| --- |
| Group Name:* | REQ-ARC-WGs |
| Title:* | Compiled security requirements |
| Source:* | Gemalto (TIA), Gemalto (ETSI) |
| Contact: | Mireille Pauliac, Francois Ennesser |
| Date:* | 2012-11-28 |
| Abstract:* | Security requirements compiled from aggregated oneM2M requirements and other sources. |
| Agenda Item:* | Requirements |
| Work item(s): | Requirements |
| Document(s) Impacted* | Requirement specification (number to be assigned) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Discussion and initial agreement for potential inclusion in the requirement TS at the TP2 meeting |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

In the requirements below, we use the term M2M Core to refer to the M2M Service capabilities in the Network domain operated by an M2M SP.

| Requirement ID | Classification | Requirement Text | Related use cases (where applicable) |
| --- | --- | --- | --- |

| 1 (Final number to be assigned ) | Security requirements- Service level authentication (from SEC_001) | The M2M System shall support mutual authentication between the M2M Core and a M2M Device or a M2M Gateway or another M2M Core. The parties may choose the strength of authentication to ensure appropriate level of security. |  |
| --- | --- | --- | --- |
| 2 (Final number to be assigned ) | Security requirements- Application user identification | The M2M System shall enable M2M applications to identify and authenticate their users. | BUTLER Global NFR |
| 3 (Final number to be assigned ) | Security requirements- Application security (from SEC_001) | The M2M System shall enable M2M applications to establish secure end-to-end communication with peer applications, independently of the M2M Service providers with whom the applications are registered. | 36r5 |
| 4 (Final number to be assigned ) | Security requirements- (from SEC_003) | The M2M System shall provide security context (authentication, encryption, integrity protection) for secure connection between entities. The security context shall include mechanisms and techniques on how to setup a security connection , and where the security connection information is stored. |  |
| 5 (Final number to be assigned ) | Security requirements- Applicative updates (from SEC_005) | Where permitted by the security policy, the M2M System shall be able to remotely provide the following features, at the Application level: • Secure updates of application security software and firmware of the M2M Device/Gateway. • Secure updates of application security context (security keys and/or algorithms) of the M2M Device/Gateway. This functionality should be provided by a tamper-resistant Secured Environment (which may be an independent Security Element) in M2M Devices/Gateways supporting this functionality | 30r4 |
| 6 (Final number to be assigned ) | Security requirements- (from SEC_006) | The M2M System shall be able to ensure integrity protection of the data exchanged. | 30r4 |
| 7 (Final number to be assigned ) | Security requirements- (from SEC_007) | The M2M System shall be able to prevent unauthorized use of the M2M Device/Gateway. | 30r4 |
| 8 (Final number to be assigned ) | Security requirements- (from SEC_008) | The M2M System shall be able to ensure confidentiality protection of the data. | 30r4 |
| 9 (Final number to be assigned ) | Security requirements- (from SYS_014) | The M2M System may support M2M Device and M2M Gateway Integrity Validation. |  |
| 10 (Final number to be assigned ) | Security requirements- (from SYS_023) | Multiple actors are involved in the end-to-end M2M service. The M2M System shall allow for such different actors to deliver the service in collaboration, maintaining mutual authentication and confidentiality of the end-to-end service. | 30r4 |
| 11 (Final number to be assigned ) | Security requirements – Denial of Service | The M2M System shall incorporate protection against threats to its availability such as Denial of Service attacks. |  |
| 12 (Final number to be assigned ) | Security requirements- Credentials protection | M2M System should provide protection against misuse, cloning or theft of credentials (in M2M Device, Gateway and Core). |  |
| 13 (Final number to be assigned ) | Security requirements- Multiple M2M Service Providers | The presence of applications operating on resources belonging to a different M2M system shall comply with security requirements of the own and the other M2M systems. Privacy of the use of resources shall be maintained in case of applications operating on resources belonging to different M2M systems. |  |
| 14 (Final number to be assigned ) | Security requirements- (from REQ_057) | The M2M System shall enable M2M applications to manage access rights to their data, and provide mechanisms for mutual authentication with entities requesting access to their data. |  |
| 15 (Final number to be assigned ) | Security Requirements – Privacy | The M2M System shall provide mechanisms to enable users of M2M applications to preserve their privacy. |  |
| 16 (Final number to be assigned ) | Security requirements – Non-repudiation | The M2M System shall provide mechanisms to ensure the non-repudiation of messages transmitted within the M2M service layer. |  |
| 17 (Final number to be assigned ) | General requirements – Roaming | The M2M System shall enable roaming of mobile M2M devices between transport networks of their supported technology. | BUTLER – Smart transportation |
| 18 (Final number to be assigned ) | General Requirements – | The M2M System shall support migration of gateway connected devices between service gateways, where such devices may move out of range while in use. | BUTLER – Smart transportation |