| Input contribution Use case |
| --- |
| Use Case Title:* | Use Case <Home Energy Management System (HEMS)> |
| Group Name:* | <WG1> |
| Source:* | <Fujitsu(TTC), KDDI> |
| Contact: | Kazutomo Hasegawa (Fujitsu) <k.hase@jp.fujitsu.com>, Shingo Fujimoto (Fujitsu) <shingo_fujimoto@jp.fujitsu.com>, Nick Yamasaki (KDDI) <nr-yamasaki@kddi.com> |
| Date:* | <2012-12-10> |
| Abstract:* | Introducing a HEMS use case based on a prototype system for evaluating efficiency of energy saving technologies with monitoring power consumptions and controlling home appliances from multiple vendors with a remote server. |
| Agenda Item:* |  |
| Work item(s): |  |
| Document(s) Impacted* |  |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Approval |

oneM2M IPR STATEMENT

“Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of an agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

## Title

### <Home Energy Management System (HEMS)>

## Description

### This use case introduces several services based on HEMS technologies.

### Home appliances from multiple vendors are connected to a LAN or PAN, and controlled by the gateway device.

### The gateway device aggregates functionalities of home appliances by getting their status and sending this to the management server.

### The gateway device is also upgradable to host newly released home appliance(s).

### The gateway device provides an API for remote control which takes privacy and authorization issues into account.

## Source (as applicable)

### Fujitsu(TTC)

## FFSActors (as applicable)

### User: user(owner) of the home appliances

### Home Appliance: appliances which may be from multiple vendors and are monitored and/or controlled energy consumption

### Gateway Device: a device installed in the user’s home and receives remote control commands from the management server

### Management Server: the server which is in charge of collecting the status of appliances and controlling the appliances via the gateway device

### HEMS Application Server: the server which provides HEMS service for the user through the remote management server

## Pre-conditions (if any)

### WAN connectivity to the Gateway Device is installed

### Service contract is required, and authentication credentials for the Management Service are installed on the Gateway device.

## Triggers (if any)

### New Air Conditioner (for example) is installed

## Normal Flow (as applicable)

### User operates the Gateway Device to identify newly installed Air Conditioner (A/C) on the LAN.

### The newly installed A/C is identified by the Gateway Device.

### The Gateway Device requests the Management Server to provide support software for the A/C.

### The support software is installed on the Gateway Device.

### The Gateway Device registers the functionalities of the A/C to the Management Server.

### The Management Server notifies the event of the installation of the A/C to the HEMS Application Server .

### The HEMS Application Server is reconfigured with the newly installed A/C.

### The HEMS Application Server receives the latest status of all of the Home Appliances including the newly installed A/C from the Management Server.

### The HEMS Application Server sends management command(s) to the Management Server to minimize energy consumption.

### Alternative flow (if any)
(TBD)

## Post-conditions (if any)

### Energy consumption within the home is minimized by monitoring and controlling Home Appliances.

## High Level Illustration (as applicable)

## Potential requirements (as applicable)

### Gateway Device SHALL detect the newly installed Home Appliance.

### Gateway Device SHALL be provided appropriate software component which is required to host the Home Appliances.

### Gateway Device SHALL support Home Appliances from multiple vendors as an abstracted object model.

### Gateway Device SHALL provide IDs for the Management Server to distinguish the Home Appliances uniquely.

### Gateway Device SHALL allow control to be overridden of the Home Appliances by User’s direct operation.

## Gateway Device SHALL provide minimal HEMS service in case of WAN connectivity is lost.

## (More TBD)

### Note: The word “SHALL” is not meaningful for now, and we should consider better wording to harmonize with other use cases.