| INPUT CONTRIBUTION |
| --- |
| Group Name:* | REQ WG / ARC WG call |
| Title:* | M2M Functional Entities and related basic definitions |
| Source:* | NEC |
| Contact: | Joerg Swetina, (joerg.swetina@neclab.eu) |
| Date:* | 2013-01-08 |
| Abstract:* | This contribution provides a role model for functional entities in oneM2M. The intention is to introduce a terminology which shall be used for writing requirements. Note, that the current document does _not_ yet introduce a full set of requirements Additionally, it is proposed to add the description of functional entities in the introductory section 5 of the requirements specification and the related definitions to a definitions section of the requirements document. The document has been aligned to the agreed terminology in oneM2M-REQ-2012-0083R01-Draft_Requirement_TS |
| Agenda Item:* | Tbd |
| Work item(s): | Requirements |
| Document(s) Impacted* | Requirement specification (number to be assigned, latest version in oneM2M-REQ-2012-0083R01-Draft_Requirement_TS) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Discussion and initial agreement for potential inclusion in the requirement TS |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

1	Introduction

This contribution provides a role model for Functional entities in oneM2M. The intention is to agree on a terminology which shall be used for writing requirements.

Note, that the current document does _not_ yet introduce a full set of requirements.

Additionally, it is proposed to add the description of functional entities in the introductory section 5 of the requirements specification and the related definitions to a definitions section of the requirements document.

Definitions have been taken from various sources, some are new, some are modified. The change-marks indicate proposed changes to the original definitions.

  - Text for inclusion in the (non-normative) introductory section of the requirements specification

=================== begin text======================

The functional entities of the M2M ecosystem:

Functional entity description

- The Device

- Is a physical equipment that provides functions (e.g. measurements, actuation) to implement the service logic of an M2M Solution

- A Device has communication capabilities to communicate

  - over Wide Area Networks (WANs) with Network Infrastructure and/or other Devices

and/or

  - over Local Area Networks (LANs) with other Devices and/or Gateways.

- The Gateway

- Is a Device that provides communication means (e.g. a Local Area Network) for communicating with other Devices and/or other Gateways

- A Gateway may provide additional functionalities (e.g. data multiplexing, data concentration, device abstraction) to implement the service logic of an M2M Solution

- The Network Infrastructure

- Is physical equipment (e.g. a set of servers)  that provide central functions of the service logic of an M2M Solution

- The Network Infrastructure has communication capabilities to communicate over Wide Area Networks (WANs) with Devices and/or Gateways.

=================== end text======================

  - Text for inclusion in a definitions section of the requirements specification

=================== begin text======================

Device: equipment that consists of a set actuators and sensors and that has embedded electronic computing and communication capability. A Device provides functions (e.g. measurements, actuation) to implement the service logic of an M2M Solution

[source: ETSI TR 102 725 V0.8.0]

Gateway: an equipment with electronic computing and communication capability aimed to translating, sharing and transferring information between two type of communicating entities, or aimed to perform some routing and multiplexing function between the two communicating entities.

[source: ETSI TR 102 725 V0.8.0]

Network Infrastructure: equipment (e.g. a set of physical servers) that provides central functions of the service logic of an M2M Solution and has the capability to communicate with Devices and/or Gateways.

[new]

Local Area Network: provides connectivity between Devices  and Gateways.

[source: ETSI TR 102 725 V0.8.0]

Wide Area Network: provides connectivity between Devices, Gateways and Network Infrastructure.

[new]

=================== end text======================