| INPUT CONTRIBUTION |
| --- |
| Group Name:* | REQ WG / ARC WG call |
| Title:* | M2M Functional Roles and related basic definitions |
| Source:* | NEC(ETSI), NEC(TTC) |
| Contact: | Joerg Swetina, (joerg.swetina@neclab.eu) |
| Date:* | 2013-02-25 |
| Abstract:* | This contribution provides a role model for functional entities in oneM2M. The intention is to introduce a terminology which shall be used for writing requirements. Note, that the current document does _not_ yet introduce a full set of requirements Additionally, it is proposed to add the description of functional entities in the introductory section 5 of the requirements specification and the related definitions to a definitions section of the requirements document. The document has been aligned to the agreed terminology in oneM2M-REQ-2012-0083R01-Draft_Requirement_TS |
| Agenda Item:* | Tbd |
| Work item(s): | Requirements |
| Document(s) Impacted* | Requirement specification (number to be assigned, latest version in oneM2M-REQ-2012-0083R01-Draft_Requirement_TS) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Discussion and initial agreement for potential inclusion in the requirement TS |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

1	Introduction

This contribution provides a role model for Functional entities in oneM2M. The intention is to agree on a terminology which shall be used for writing requirements.

Note, that the current document does _not_ yet introduce a full set of requirements.

Additionally, it is proposed to add the description of functional entities in the introductory section 5 of the requirements specification and the related definitions to a definitions section of the requirements document.

Definitions have been taken from various sources, some are new, some are modified. The change-marks indicate proposed changes to the original definitions.

  - Text for inclusion in the (non-normative) introductory section 5 of the requirements specification

=================== begin text======================

5.x The functional entities of the M2M ecosystem:

Functional entity description

- The Device

- Is a physical equipment that provides functionality (e.g. for data processing, sensing or actuation) to implement an Application Service

- A Device has communication capabilities to communicate

  - over Wide Area Networks (WANs) with Network Infrastructure and/or other Devices

and/or

  - over Local Area Networks (LANs) with other Devices and/or Gateways.

- The Gateway

- Is a Device

- A Gateway provides additional communication means (e.g. a Local Area Network) to facilitate communication of other Devices and/or Gateways

- A Gateway may provide additional functionalities (e.g. data multiplexing, data concentration, device abstraction) to implement an Application Service

- The Back-end Infrastructure

- Is equipment (e.g. a set of physical servers) that provides coordination functions for Application Services.

- The M2M Capability Back-end Infrastructure (CBI) provides coordination capabilities for the M2M Service Provider (e.g. managing devices, administration of credentials, the root of access control) and communicates with Devices and/or Gateways.

- Equipment (e.g. servers of an Application Service Provider) for executing the coordination functions of Application Services is part of the Application Back-end Infrastructure (ABI). ABI is out of scope of oneM2M.

=================== end text======================

  - Text for inclusion in a definitions section of the requirements specification

=================== begin text======================

Device: equipment that provides functionality (e.g. for data processing, sensing or actuation) to implement an Application Service and that has embedded electronic computing and communication capability.

Device handler: A person who has physical access to a Device or parts of it. 
Note: A Device Handler may or may not be a legitimate authority to handle the Device.

Gateway:  a Device that provides additional communication means (e.g. a Local Area Network) to facilitate communication of other Devices and/or Gateways.

M2M Capability Back-end Infrastructure (CBI): equipment (e.g. a set of physical servers) that provides coordination capabilities for the M2M Service Provider (e.g. managing devices, administration of credentials, the root of access control) and communicates with Devices and/or Gateways.

Application Back-end Infrastructure (ABI): equipment (e.g. a set of physical servers of the Application Service Provider) that executes coordination functions of Application Services. ABI is out of scope of oneM2M.

Device Domain: consists of Devices and Gateways

Network Domain: consists of ABI and CBI

=================== end text======================