| Input contribution Use case |
| --- |
| Use Case Title:* | Use Case : Information Delivery service in the devastated area |
| Group Name:* | <WG1> |
| Source:* | < Advanced Telecommunications Research Institute International>, < Sumitomo Electric Industries Ltd. (TTC)>, < Alcatel-Lucent (ETSI)> |
| Contact: | Masahiro Uno (ATR), <uno@atr.jp> Yoji Okada (SEI), <okada-yoji@sei.co.jp> Timothy Carey (ALU), < timothy.carey@alcatel-lucent.com> |
| Date:* | <2012-12-02> |
| Abstract:* | The use case in the devastated area to provide the victims with the information automatically. |
| Agenda Item:* |  |
| Work item(s): |  |
| Document(s) Impacted* |  |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Approval |

oneM2M IPR STATEMENT

“Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of an agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

## Title

### Use Case: Information Delivery service in the devastated area

## Description

### Background

### When a disaster occurs in the metro area, many victims require various kinds of information such as traffic, safety and evacuation area. However, it may be difficult to collect such information immediately and properly.

### Description

### This is the use case of a M2M Service that transmits required information to the User Devices (UDs) of disaster victims immediately and automatically. Some of the information shall be maintained before a disaster happens.

### UD connects to the Wireless Gateways (WGs). The WGs properly provide the UDs with the information stored on its local DB to avoid the network congestion.

### When Disaster Sensor detect a serious disaster, the Service Provider multicasts the latest information which the victims need such as traffic congestion, locations of closest hospitals and evacuation area. The UDs receive and update the information automatically.

### After the disaster happens, the Service Provider continues to update the information according to the situation of traffic, safety and evacuation area as well as the data from Disaster Sensors and Equipments for public information.

## Source (as applicable)

### Advanced Telecommunications Research Institute International (ARIB),

### Sumitomo Electric Industries Ltd. (TTC).

### Alcatel-Lucent (ETSI) and

## FFSActors (as applicable)

### Service Provider has the aim to assist disaster victims by providing information to victims who have User Devices (UDs).

### Disaster Sensor shall detect a disaster and send the disaster detection to the Service Provider.

### Equipment shall send information to the Service Provider.

### The UDs shall receive the information from the Service Provider to support the disaster victim in emergency.

### Wireless Gateway (WG) can send the information from the Service Provider to the UDs by wireless connection (e.g., WiFi, 3GPP) in an emergency.

## Pre-conditions (if any)

### In times when disasters are not present (peace time), the Equipment collects information to be used for disaster situations (emergencies). The information is maintained in the DBs on the Service Provider’s Disaster Information Network.

### The Service Provider shall have reliable communication with the Disaster Sensor.

### When receiving information regarding a disaster from the Service Provider, the WGs shall have the method to check if the information is reliable prior to distributing the information to UDs.

### The WG may be used for the other services for specific UDs in peace time. In case of emergency, every subscribed UDs should be able to receive the message from the Service Provider through the WG.

### Communication connections among UDs, WGs and Service Provider are established.

### When the network connectivity is available, the information on DB in the Service Provider-Disaster Information Network and local DBs in the WGs should be capable of being regularly synchronized and updated.

## Triggers (if any)

### The detection of a disaster (emergency) by the disaster sensor

## Normal Flow (as applicable)

### Normal flow for collecting information during a disaster

### Fig.1.5-1 In Peace Time

### Fig.1.5-2 In Emergency

### 1. WGs request the updated information from the Service Provider in peace time repeatedly and stores the information in their local DBs.

### 2. Disaster Sensors send messages to start the processing flow of the information delivery service to the Service Provider if they detect the disaster trigger.

### 3. The Service Provider should be able to allow every UD to access to the Databases in the WGs and Service Provider’s Disaster Information Network.

### 4. The Service Provider sends the latest information to UDs automatically. WGs can send the stored information on the local DB to the UDs in order to suppress the network congestion.

## Alternative flow (if any)

### UDs can request their dedicated information from WGs. When the network connectivity between the WG and Service Provider is established, WGs can request from the Service Provider the dedicated information for the UDs (e.g., family safety and their refuge area, personal medical information).

## Post-conditions (if any)

## High Level Illustration (as applicable)

## Potential requirements (as applicable)

| Requirement ID | Classification | Requirement Text |
| --- | --- | --- |
| HLR-088-a | Data reporting | The M2M System shall provide capabilities to Applications to update/synchronize Application specific databases between the Network Application and Gateway Application |
| HLR-087 | Data reporting | The M2M System shall support transmission of Application specific data (e.g. tsunami and earthquake detection sensor data) from Devices and oneM2M external sources (e.g. ETWS data) to Applications in the Network. |
| HLR-088-b | Data storage | A (wireless) Gateway shall be able to autonomously provide Devices that are attached via the LAN of the Gateway with trusted data that is locally stored in the Gateway even when the communication over the WAN connection of the Gateway to the Service Provider is not possible (e.g., network congestion, connectivity issues, Service Provider application is not operational). |
| HLR-089 | Data reporting | A (wireless) Gateway shall be able to securely broadcast data (e.g. disaster warnings) to any UD in its vicinity |
| HLR-092-a | Security | A UD that receives broadcast data from a (wireless) Gateway shall be able to verify that the (wireless) Gateway is authorized to broadcast the data (e.g. disaster warnings) and that the data is authentic. |
| HLR-092-b | Security | The M2M System shall provide capabilities to the Service Provider to enable/disable open access of UDs to the Gateway. If access of UDs to the Gateway is open any UD shall be allowed to receive data from the Gateway. If access of UDs to the Gateway is not open only authorized UDs shall be allowed to receive data from the Gateway. |

### This work is supported by the Ministry of Internal Affairs and Communications under a grant entitled "Research and development of Dynamic Reconfigurable M2M Wireless Network Technology."