| INPUT CONTRIBUTION Requirement |
| --- |
| Group Name:* | REQ |
| Title:* | Input requirements on management |
| Source:* | Huawei (CCSA), Huawei (ETSI) |
| Contact: | Yongjing Zhang, zhangyongjing@huawei.com |
| Date:* | <2013-02-17> |
| Abstract:* | This contribution provides revised input management requirements based on comments received before TP#3. |
| Agenda Item:* | <Agenda item reference> |
| Work item(s): | WI0001 |
| Document(s) Impacted* | Technical Specification - M2M Requirements |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Approval and incorporation into oneM2M Requirement TS |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

Background

The following table shows the changes made to original requirements based on comments received in the requirement evaluation matrix.  Comments addressed by the modification are marked in green. The final proposed text (as accepted) for the requirement TS is shown in the next section “Proposed Requirements”.

| ID | Description | Comments received |
| --- | --- | --- |
| HLR-136 | The M2M System shall provide the capability to discover the Local Area Network including the device information and network parameters. | TI: Why the topology? Seems application specific Fujitsu: Needs confirmation of the necessity of having the "network topology" info. NTT_DoCoMo: Term "capillary network"should be clarified. MOTO: why you need info on the whole topology? Model for device and the parameters of capillary network are enough LGE: Terms are too technical and specific. |
| HLR-138 | The M2M System shall provide the capability to maintain and describe the information model of devices and parameters of a Local Area Network. | MOTO: why you need info on the whole topology? Model for device and the parameters of capillary network are enough IDCC: Could it be re-worded so it is not as application/vertical specific? KDDI: Needs clarification for topology. TI: Why the topology? Seems application specific Fujitsu: Shall -> may |
| HLR-137 | The M2M System shall provide the capability to notify M2M Applications the changes of the Local Area Network including the device information and network parameters. <to be merged with HLR-029 /030 /031/ 032 in group 13> | TI: Why the topology? Seems application specific Moto: To whom the notification could be provided to needs to be clarified and there are undefined terms such as capillary network Sprint: Specify an object of the notification in order to make this requirement more clear. Fujitsu: Shall -> may LGE: Capillary network can be reworded. Change notification can be included in maintainence (124). |
| HLR-169 | The M2M System shall support unified generic means to manage devices enabled by different management technologies (e.g. OMA DM, BBF TR069). | Moto: Concern that it's too open ended, since there are no bounds on the number of management technologies. What would appear useful is a generic means to add support for additional management technologies. IDCC: example for our clarification? |
| HLR-170 | The M2M System shall provide the capability to manage multiple devices in a grouped manner. | No comment. |
| HLR-171 | - | Sprint: Split this into separate requirements: 1) The M2M System shall provide the capability to manage management-enabled devices in a capillary network. 2) The M2M System shall provide the capability to provision and configure management-enabled devices in a capillary network. 3) ... Moto: Missing definition of capillary network. Such services would seem to be supported via the gateway, which is not mentioned. "supported by the device" - which device? LGE: define "capillary network" or delete "in a capillary network" ALU: The M2M System shall provide the capability to manage the devices in a M2M Area Networkk when supported by the device, including: · Provisioning & configuration · Diagnostics · Software Management · Device Reset Cisco: List is not complete Cisco: The M2M System shall provide the capability to manage devices when supported by the device, including: · Provisioning & configuration · Diagnostics · Software Management · Device Reset |
| HLR-171a | The M2M System shall provide the capability for provisioning or configuration of devices in a Local Area Network via an M2M Gateway, when supported by the devices. |  |
| HLR-171b | The M2M System shall provide the capability for monitoring and diagnostics of devices in a Local Area Network via an M2M Gateway, when supported by the devices. |  |
| HLR-171c | The M2M System shall provide the capability for software management of devices in a Local Area Network via an M2M Gateway, when supported by the devices. |  |
| HLR-171d | The M2M System shall provide the capability for resetting devices in a Local Area Network via an M2M Gateway, when supported by the devices. |  |
| HLR-172 | - | TI: Why the topology? Seems application specific MOTO: It's not clear that network topology is within the scope of oneM2M, however it would seem reacting and managing changes to the capillary network triggered by the capillary technology would be. Sprint: Split this into separate requirements: ALU: The M2M System shall provide the capability to manage the network topology of a M2M Area Network when supported by the M2M Area Network technology, including: · Adding/removing devices to/from the M2M Area Network · Modifying the interconnection relationship between devices |
| HLR-172a | The M2M System shall provide the capability for adding/removing devices to/from a Local Area Network, when supported by the Local Area Network technology. |  |
| HLR-172b | The M2M System shall provide the capability for modifying the interconnection relationship between devices in a Local Area Network, when supported by the Local Area Network technology. |  |

Proposed Requirements

The following table lists the proposed requirement text for oneM2M requirement TS.

| Requirement ID | Classification | Requirement Text |
| --- | --- | --- |
| HLR-136 | Management | The M2M System shall provide the capability to discover the Local Area Network including the device information and network parameters. |
| HLR-138 | Management | The M2M System shall provide the capability to maintain and describe the information model of devices and parameters of a Local Area Network. |
| HLR-137 | Management | The M2M System shall provide the capability to notify M2M Applications the changes of the Local Area Network including the device information and network parameters. <to be merged with HLR-029 /030 /031/ 032 in group 13> |
| HLR-169 | Management | The M2M System shall support unified generic means to manage devices enabled by different management technologies (e.g. OMA DM, BBF TR069). |
| HLR-170 | Management | The M2M System shall provide the capability to manage multiple devices in a grouped manner. |
| HLR-171 | Management | <replaced by HLR-171a, HLR-171b, HLR-171c and HLR-171d> |
| HLR-171a | Management | The M2M System shall provide the capability for provisioning or configuration of devices in a Local Area Network via an M2M Gateway, when supported by the devices. |
| HLR-171b | Management | The M2M System shall provide the capability for monitoring and diagnostics of devices in a Local Area Network via an M2M Gateway, when supported by the devices. |
| HLR-171c | Management | The M2M System shall provide the capability for software management of devices in a Local Area Network via an M2M Gateway, when supported by the devices. |
| HLR-171d | Management | The M2M System shall provide the capability for resetting devices in a Local Area Network via an M2M Gateway, when supported by the devices. |
| HLR-172 | Management | <replaced by HLR-172a and HLR-172b> |
| HLR-172a | Management | The M2M System shall provide the capability for adding/removing devices to/from a Local Area Network, when supported by the Local Area Network technology. |
| HLR-172b | Management | The M2M System shall provide the capability for modifying the interconnection relationship between devices in a Local Area Network, when supported by the Local Area Network technology. |