| Input contribution Use case |
| --- |
| Use Case Title:* | Event Triggered Task Execution Use Case |
| Group Name:* | WG1 - Requirement |
| Source:* | Fujitsu (TTC) |
| Contact: | Shingo Fujimoto, Fujitsu, shingo_fujimoto@jp.fujitsu.com Ryuichi Matsukura, Fujitsu, r.matsukura@jp.fujitsu.com Kazutomo Hasegawa, Fujitsu, k.hase@jp.fujitsu.com |
| Date:* | 2013-Feb-18 |
| Abstract:* | This use case is regarding HEMS application, and introduced related high level requirements. |
| Agenda Item:* | Input Contribution |
| Work item(s): |  |
| Document(s) Impacted* | Use Case |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Potential Requirements should be considered to include use case TR document. |

oneM2M IPR STATEMENT

“Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of an agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

## Title

### Event Triggered Task Execution Use Case

## Description

### Gateway Device may be required to configure for executing some tasks which are triggered by pre-defined events.

## Source (as applicable)

### Fujitsu (TTC)

## FFSActors (as applicable)

Management Server,

Gateway Device,

Thermometer and Air Conditioner (M2M Device),

Data Storage Server,

User

## Pre-conditions (if any)

Gateway Device is configured to work as the gateway for collecting data from some sensor devices installed at home network.

Sensor Devices are configured to accept the request from Gateway Device which requests sending measured data.

## Triggers (if any)

M2M System is going to configure scheduled task execution for data collection from sensor devices.

## Normal Flow (as applicable)

Management Server requests Gateway Device to report collected data from a thermometer (one of the Sensor Devices in this use case) every 30 minutes.

Gateway Device establishes the connection to the thermometer, and collects measured data.

Gateway Device reports the collected data to Data Storage Server.

### Alternative flow 1

- (after step 2 in normal flow,) Gateway Device stores measured data associating with the source Sensor Device.

- Management Server requests Gateway Device to report the log data which summarize series of measured data by Sensor Devices for one day.

### Alternative flow 2

- Management Server configures Gateway Device to start monitoring energy consumption of Air Conditioner, when the device is turned on, and to stop monitoring when that is turned off.

- Gateway Device subscribes the power status change of Air Conditioner.

- When the user turned on the Air Conditioner, the Gateway Device is notified the status change.

- Gateway Device starts monitoring the energy consumption of the Air Conditioner.

- When User turned off the Air Conditioner, the Gateway Device is notified the status change

- Gateway Device stops monitoring the energy consumption of the Air Conditioner.

### Alternative flow 3

- Management Server configures Gateway Device to report the energy consumption when the total energy consumption exceeded over the 20kW per day.

- Gateway Device keeps collecting data about energy consumption from home electronics (i.e. Air Conditioner).

- When the total energy consumption exceeded over the 20kW per day, the Gateway sends notify the report to the Data Storage Server.

## Post-conditions (if any)

Collected data is stored on the Data Storage Server for further use.

## High Level Illustration (as applicable)

## Potential requirements (as applicable)

Gateway Device shall support to collect measured data from M2M Device periodically.

Gateway Device may support to record the measured data in order to report them to Data Storage Server as sequential records.

Gateway Device may support to start/stop monitoring triggered by status change of M2M Device to be monitored.

M2M System may request M2M Gateway to send conditional report on measured data by M2M Device(s). The condition can be expressed as threshold and/or size of value change.