| INPUT CONTRIBUTION Requirement |
| --- |
| Group Name:* | WG1, REQ |
| Title:* | Requirements for Information Delivery service in the devastated area |
| Source:* | Advanced Telecommunications Research Institute International, Sumitomo Electric Industries Ltd. (TTC), Alcatel-Lucent (ETSI) |
| Contact: | Masahiro Uno (ATR), <uno@atr.jp> Yoji Okada (SEI), <okada-yoji@sei.co.jp> Timothy Carey (ALU), < timothy.carey@alcatel-lucent.com> |
| Date:* | 2013-02-17 |
| Abstract:* | This contribution provides the altered potential requirements for Information Delivery service in the devastated area. |
| Agenda Item:* | Requirements |
| Work item(s): | Requirements |
| Document(s) Impacted* | Requirement specification |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Approval |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

The following potential requirements are changed in oneM2M-REQ-2012-074.

HLR-088 and 092 are divided into two parts.

| Requirement ID | Classification | Requirement Text |
| --- | --- | --- |
| HLR-088-a | Data reporting | The M2M System shall provide capabilities to Applications to update/synchronize Application specific databases between the Network Application and Gateway Application |
| HLR-087 | Data reporting | The M2M System shall support transmission of Application specific data (e.g. tsunami and earthquake detection sensor data) from Devices and oneM2M external sources (e.g. ETWS data) to Applications in the Network. |
| HLR-088-b | Data storage | A (wireless) Gateway shall be able to autonomously provide Devices that are attached via the LAN of the Gateway with trusted data that is locally stored in the Gateway even when the communication over the WAN connection of the Gateway to the Service Provider is not possible (e.g., network congestion, connectivity issues, Service Provider application is not operational). |
| HLR-089 | Data reporting | A (wireless) Gateway shall be able to securely broadcast data (e.g. disaster warnings) to any UD in its vicinity |
| HLR-092-a | Security | A UD that receives broadcast data from a (wireless) Gateway shall be able to verify that the (wireless) Gateway is authorized to broadcast the data (e.g. disaster warnings) and that the data is authentic. |
| HLR-092-b | Security | The M2M System shall provide capabilities to the Service Provider to enable/disable open access of UDs to the Gateway. If access of UDs to the Gateway is open any UD shall be allowed to receive data from the Gateway. If access of UDs to the Gateway is not open only authorized UDs shall be allowed to receive data from the Gateway. |

### This work is supported by the Ministry of Internal Affairs and Communications under a grant entitled "Research and development of Dynamic Reconfigurable M2M Wireless Network Technology."