| INPUT CONTRIBUTION |
| --- |
| Group Name:* | REQ #2 |
| Title:* | Correction to M2M Healthcare Gateway Use Case |
| Source:* | Qualcomm Inc. (TIA) |
| Contact: | Dilip Krishnaswamy, Qualcomm, dilipk@qti.qualcomm.com Josef Blanz, Qualcomm, jblanz@qti.qualcomm.com |
| Date:* | 2013-02-18 |
| Abstract:* | This document suggests some corrections to the M2M Healthcare Gateway Use Case included in the Use Case TR. |
| Agenda Item:* | 4.2 |
| Work item(s): | WI 0001 |
| Document(s) Impacted* | Technical Report - oneM2M use case collection |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree to include proposed changes in section 7 of the use case TR |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

# 7	M2M Healthcare Gateway

## Description

### This use case addresses a healthcare gateway to transport healthcare sensor data from a patient to a backend server, and to also support bidirectional communications between a backend server via a gateway. The use case results in a set of potential requirements out of which some are specific to the fact that cellular connectivity is assumed between gateway and backend. Other than that, this use case is not restricted to cellular connectivity.

## Source (as applicable)

## Qualcomm.

## Several scenarios also supported by guidelines defined in Continua Health Alliance should be covered by this use case.

## Target Industry

### Healthcare

## Actors (as applicable)

### Patients using healthcare sensors

### Health-care gateways (also known as AHDs (Application Hosting Devices) in Continua Health Alliance terminology). Examples of healthcare gateways can include wall plugged devices with wired or wireless connectivity, or mobile devices such as smartphones.

### Operating healthcare service enterprise backend servers (equivalent to a WAN Device (Wide Area Network Device) in Continua Health Alliance terminology)

### Health care providers

### Care givers and authorized users that could eventually access health sensor data

### Wide Area Network operators

## Pre-conditions (if any)

## •	Operational healthcare sensor(s) that requires occasionally or periodically transport of sensor data to a backend server.

## •	A local healthcare gateway is available that can be used to transport data from the healthcare sensor to a backend server. It is open as regards who owns and/or operates this local gateway. Different scenarios shall be possible supported (patient, healthcare provider, care-giver, M2M service provider, wide area network operator).

## •	Network connectivity is available for transporting healthcare sensor data from the local gateway to the backend server.

## •	A backend server that is hosting applications to collect measurement data and makes it available to care-givers, healthcare-providers or the patient.

## Triggers

### The following triggers could initiate exchange of information according to the flows described further-below:

### Patient-initiated measurement request (Trigger A). In this case, the patient decides to take a measurement and triggers the processing in the system.

### Static configured policy at a healthcare gateway that requests patient to initiate measurement (Trigger B). This can be an explicit message from the gateway device to a patient device, or it could just a indicator on the gateway itself such as a pop-up message or an indicator light requesting measurement.

### Static configured policy at a healthcare gateway that directly requests sensor data without patient intervention (Trigger C). This can be used in conjunction or in lieu of Triggers A or B. Some sensor data may be measurable or accessible without patient intervention so that the gateway merely needs to communicate with one or more sensors to obtain the data.

### Patient monitoring app on healthcare service backend server that triggers generation of sensor data (Trigger D).

### Dynamic patient monitoring request from the healthcare service provider (Trigger E).

### Availability of new patient healthcare data at a healthcare gateway that requires transport to a backend server.

### Availability of new patient healthcare data at a backend server that requires sharing with authenticated users such as a nurse/doctor (healthcare provider) and a patient’s relative (such as a child care-giver)

### Analysis of healthcare patient sensor info or trends that triggers the need to take action on behalf of patient (for example determination of a deteriorating health condition).

### QoS-aware data buffering policy on the healthcare gateway

### Network-aware and/or device-aware delay-tolerant data management policy on the healthcare gateway. Network dynamic access constraints or network utilization constraints or prior network access policy constraints or device energy minimization considerations that can cause delay tolerant sensor data to be buffered (and aggregated if needed) at the gateway and transmitted at a later time.

## Normal Flow

### A measurement of the healthcare sensor is initiated as shown in Figure 1. Patient can initiate the generation of sensor data such as taking a glucometer measurement (Trigger A). The measurement may also be initiated based on some pre-defined schedule at the healthcare gateway (Trigger B or C).

### The healthcare sensor data is forwarded to a backend server by a healthcare-gateway. If the data has a QoS indicator such as dynamic latency/bandwidth and/or delay tolerance, the gateway can determine whether to send the data immediately, or whether to buffer and send the data at a later time. Buffered data can be aggregated with past data or future data for a future aggregated transmission over the network. In wireless/cellular networks, aggregated transmissions can reduce the utilization of the network by requesting access to the network less frequently.

### Measured data (or processed/interpreted versions of the data) that arrives at the healthcare service enterprise backend server may need to be forwarded to authorized subscribers – such as family care-giver or a nurse/doctor – via notifications. Subscriptions can be set up in advance, and configured at the backend server, so that when the data arrives, the subscribers can be notified. Filters can be associated with the subscriptions, so that only selective data or alert information can be sent to subscribers.

## Figure 1: Normal Healthcare Measurement Data Processing Flow

### Alternative Flow 1 – Network/Device-aware transmissions

### This flow (Figure 2) is the same as the regular flow with the following exceptions: The healthcare sensor data may need be stored on the gateway and forwarded at a future time based on one or more of the following factors:

### •	delay tolerances associated with the data

### •	network policy constraints (efficiency, avoidance of peak loads, protection of spectrum)

### •	device constraints (energy consumption, data tariff).

### •	temporary lack of coverage of network connectivity

### Multiple measurements can be aggregated and transmitted together at a future time.

### Measurements can be taken with or without patient intervention and sent to the healthcare gateway. As measured data arrives at the healthcare gateway, its QoS indicators such as dynamic latency/bandwidth and delay tolerance can be processed. Delay tolerant data can be buffered and aggregated with past and future delay-tolerant data, with network/device-aware constraints can applied to determine an appropriate time to transmit the data.

### Figure 2: Network/Device-aware Flow

### Alternative Flow 2 – Remote Monitoring

### The backend server may expect the patient to submit sensor data periodically or with a pre-defined schedule. In the absence of a typically expected sensor data event, the backend server can trigger an event to request the patient to take a measurement.

### In this case, the trigger (Trigger D) arrives over a wide-area-network from the patient monitoring app on the healthcare service backend server delivered to the healthcare gateway. The patient monitoring app could generate this request based on a statically configured policy to request measurements or due to some dynamic needs based on processing of previous patient data.

### Optionally, the healthcare service provider may generate a measurement request (Trigger E) that can be received by the patient monitoring app on the backend server, which can subsequently submit a request over the wide area network for the patient monitoring request to the healthcare gateway.

### The healthcare gateway forwards the received request to the patient. In many cases, it is possible that a device associated with the patient, such as the healthcare cellular gateway, or the

### The patient subsequently takes the sensor measurement upon receiving the request. Alternatively, some sensor measurements could be taken without patient intervention. Measured sensor data is then received at the healthcare gateway, and subsequently transmitted based on processing the QoS/Network/Device-aware constraints for transmission.

### Figure 3: Remote Monitoring Flow

### Alternative Flow 3 – Local Gateway Data Analysis

### The local gateway node can continuously process the data that it forwards. It can have smart algorithms to detect health anomalies associated with the patient. In case no anomalies are detected, the health sensor data may only be forwarded occasionally (see also alternative flow 1). In case an anomaly is detected, the local gateway needs to send an alert to the health care provider or the care-giver or to the patient if desired.

### Figure 4: Local Gateway Data Analysis Flow

## Post-conditions (if any)

## Normal flow

## Sensor data is stored in a database associated with the backend server. Healthcare provider and care-giver observe data to ascertain status of patient’s health.

## Alternative flow 1

## Data is buffered and transmitted when the network constraints or policy constraints or device energy minimization constraints allow the transmission of delay-tolerant data

## Alternative flow 2

## Patient takes measurement and sends data to backend server.

## Alternative flow 3

## Local data analysis with indication of abnormal condition results in an alert message sent to the health care provider and optionally to the patient.

## High Level Illustration

## The diagram below summarizes the overall description of this use-case. All the flows and connectivity should be self-explanatory based on the discussions in the previous sections.

## Potential requirements

### Rationale

### This use case sets out from the presence of a gateway between one or more healthcare sensor(s) and a backend server. Even though the use case is assuming a cellular gateway, this restriction is not needed in general.

### Resulting requirement:

### 1.	The M2M system shall be capable of supporting gateway nodes that are capable of transporting sensor measurements to back end servers.

### Rationale

### Sensors can measure patient data with or without patient initiation. Therefore, new measurement data may become available at any time.

### Resulting requirement:

### 2.	Whenever a healthcare sensor has measurement data available, it shall be possible for the sensor to send a request to the local healthcare gateway to transport new measurement data to the backend server.

### Rationale

### Incoming requests from the healthcare sensor to the healthcare gateway may not result in immediate forwarding of the data to the backend server if any of the following is applicable: Dynamically changing cellular network availability (coverage); cellular network utilization constraints (policies); device energy consumption or memory constraints. In one of the flows also the quality of the data to be transported (alert=high priority) was relevant for determining when the connection needs to be triggered.

### Resulting requirements:

### 3.	The local healthcare gateway needs to be capable to buffer incoming requests from the healthcare sensor for transporting data to the backend server and support forwarding them at a later time – which could potentially be a very long time in the order of hours, days or even more – depending on cellular network availability, cellular network utilization policies, device constraints

### 4.	The local healthcare gateway needs to be capable to accept parameters with incoming requests from the healthcare sensor which define a delay tolerance for initiating the delivery of the sensor measurements or parameters for categorizing sensor measurements into different levels of priority/QoS.

### 5.	The local healthcare gateway needs to be cable of receiving policies which express cellular network utilization constraints and which shall govern the decision making in the gateway when initiating connectivity over cellular networks.

### 6.	The local healthcare gateway needs to be capable to trigger connections to the cellular network in line with the parameters given by the request to transport data and in line with configured policies regarding utilization of the cellular network

### A subscription and notification mechanism was described in this use case. Only authenticated and authorized users (e.g. care-giver, relatives, doctors) shall be able to subscribe to healthcare sensor measurement data and get notifications and access to the measured data. These authenticated and authorized stakeholders are typically using applications that use the M2M system to access the measured data. Resulting requirement:

### 7.	The M2M system shall be capable of supporting a mechanism to allow applications (residing on the local gateway, on the backend server or on the sensor itself) to subscribe to data of interest and get notifications on changes or availability of that data.

### 8.	The M2M system needs to be able to allow access to data that is being transported or buffered only to authenticated and authorized applications

### Rationale

### The use case also describes a flow in which the backend server could initiate an action on the local healthcare gateway. Resulting requirements:

### 9.	The M2M system shall support transport of data from the backend server to the cellular healthcare gateway.

### 10.	The M2M system shall support of triggering a cellular connection to the local healthcare gateway in case the gateway supports such functionality.

### Rationale

### Different subscribers may be interested in different information so that each subscriber may want to get notified only for events of interest to that subscriber:

### 11.	Subscriber-specific filters can be set up at the healthcare service enterprise backend server so that each subscriber can be notified only when information/events relevant to the subscriber are available/occur.

### Rationale

### The M2M healthcare gateway device can be in a sleep mode of operation to save energy and can be without an active network connection. A patient monitoring app may be desirous of communicating with the gateway device when the gateway device is in this sleep mode of operation

### 12.	The M2M system shall be able to support a wakeup trigger (aka "shoulder-tap") mechanism (such as using SMS or alternate mechanisms) to wake up the gateway. The gateway can subsequently establish a network connection and query the enterprise backend server for additional information, and the enterprise backend server may then respond with adequate information to enable further processing of its request.

# Text boxes

Alert (Optional)