| INPUT CONTRIBUTION Requirement |
| --- |
| Group Name:* | REQ |
| Title:* | Role Description Text Proposal |
| Source:* | Qualcomm Inc. (TIA) |
| Contact: | Josef Blanz, Qualcomm, jblanz@qti.qualcomm.com Phil Hawkes, Qualcomm, phawkes@qti.qualcomm.com |
| Date:* | 2013-02-25 |
| Abstract:* | In this contribution we propose to include a text proposal on a description of Roles of Stakeholders into the TR on ‘Roles and Focus Areas’. The purpose of the proposed description is to establish a common understanding of what are the Stakeholder Roles that oneM2M needs to take into account in its work. |
| Agenda Item:* | REQ_ARC#2, Agenda Item 4.2 |
| Work item(s): | WI0003 |
| Document(s) Impacted* | TR XYZ ‘Roles and Focus Areas’ |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree to include the text proposal in this contribution into the TR ‘Roles and Focus Areas’ |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

# Introduction

In this contribution we propose to include the following text proposal on a high-level description of stakeholders and their roles into TR on ‘Roles and Focus Areas’. The purpose of the proposed description is to establish a common understanding of who the stakeholder in an M2M should be from a oneM2M perspective and how their respective roles could be described. Since this description is done before a precise and consistent framework for vocabulary terms is derived, some terms need to be used without a clear definition. In separate input contributions such derived clear definitions are proposed.

# Text Proposal

# 6	High-Level Descriptions of Roles and Focus Areas

## 6.1	Assumptions

Due to the objective to start with a high-level description of roles and focus areas before arriving at an agreeable set of vocabulary candidates, it is necessary to use some terms in the descriptions without having defined them clearly. Therefore in this Clause 6, some terms will be used to explain what the possible roles are and what focus areas oneM2M is working on even though they may only be defined in a more precise manner later on in Clause 5 or may not be defined at all if a common understanding can be assumed.

## 6.2	Roles of Stakeholders

In order to establish a common understanding of the entities interacting in a M2M system from a oneM2M perspective and what their possible roles are, this sub-clause provides a high-level description. The provided descriptions are not pre-empting the derivation of more precise definitions further-below in Clause 7 of this document. The oneM2M scope statement is setting out from some layering of an M2M system as expressed for instance by the following excerpts taken from the oneM2M scope statement:

“…

- Use cases and requirements for a common set of Service Layer capabilities;

- Service Layer aspects with high level and detailed service architecture, in light of an access independent view of end-to-end services;

…

- Common use cases, terminal/module aspects, including Service Layer interfaces/APIs between:

  - Application and Service Layers;

  - Service Layer and communication functions

“

Therefore is seems appropriate to stick with a high-level layering of the  in line with the oneM2M scope statement. As a consequence a simple layered model as depicted below is used in the context of describing stakeholders and roles.

Application Layer

Service Layer

Underlying Network Layer

Figure 1. High-level layered model.

In this layered view of an M2M system some potential stakeholders would play together. Please note that the following list is NOT intended as precise definitions of stakeholders and their roles, but rather serves the purpose of establishing an easy to understand description. Also Note that a single stakeholder in an M2M system could play multiple of the roles described below:

- A User of an M2M system is a role of a stakeholder that is interested to use communication means provided by the Application Layer to achieve one or more of the following

  - Influencing events external to the system (for example, sending an instruction to an actuator to switch something external to the communication system on or off) ;

  - Getting informed about events external to the system (for example, receiving a reading from a sensor external to the communication system) ;

  - Influencing the operation of a component of the M2M system (for example, sending a set of configuration parameters to a particular component);

  - Getting informed about the operation of a component of the M2M system (for example, receiving an error log or performance report from a particular component).

- An Application Service Provider is a role of a stakeholder that provides the functions in the Application Layer as a service to one or more Users of the M2M system. The functions residing inside the Application Layer can be very specific to the User’s needs. Those functions will serve as the means that allow the User of the M2M system to interact with the external events mentioned above and process that information based on the business needs of the User. The Application Layer functions could for instance contain all the logic to monitor a certain type of external machine assets including evaluation of sensor data and generation of commands for actuators. Note that the Application Servcie Provider could potentially be the same stakeholder as the User of the M2M system

- An M2M Management Service Provider is a role of a stakeholder that provides functions as a service to one or more Users of the M2M system or to other stakeholder listed here so that the operation of the components that those stakeholder are interested to control can actually be influenced or be monitored.

- An M2M Service Provider is a role of a stakeholder that provides the functions in the Service Layer to one or more Application Service Provider. Those functions are commonly needed communication functions that should be useful for a number of different industry segments and could be used by a number of different Application Service Providers. The main goal for that set of functions is to allow efficient and easy to use communications between the different components in the Application Layer. For instance, the functions provided by the M2M Service Provider could allow for an easy an efficient access to data generated by a number of sensors connected to devices located in several distributed machine assets that need to be monitored so that some remote applications could process that information in order to check the correct functioning of these machine assets and then generate some alarms in case of an error. Note that The M2M Service Provider could be the same stakeholder as the Application Service Provider. Also other combinations of roles for a single stakeholder are possible.

- A Network Service Provider is a role of a stakeholder that provides communications services for data transport and exposes other capabilities of an underlying network to an M2M Service Provider.

It is important to note that the precise boundary between the layers depicted in Figure 1 and as a consequence the precise responsibility of the respective stakeholders need to be very flexible in order to allow for various valid business models. For instance it is possible that a single stakeholders plays the role of a Network Service Provider, A M2M Service Provider and an M2M Management Service Provider at the same time.

## 6.3	Focus Areas