| INPUT CONTRIBUTION |
| --- |
| Group Name:* | Requirements |
| Title:* | Update“Group 3” Requirements for Requirements TS |
| Source:* | Alcatel-Lucent |
| Contact: | Timothy.carey@alcatel-lucent.com |
| Date:* | 2013-03-09 |
| Abstract:* | This contribution contains updated requirements to Subscription requirements (Group 3). |
| Agenda Item:* | TBD |
| Work item(s): | TBD |
| Document(s) Impacted* | Requirements TS |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | To incorporate requirements into requirements TS. |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

Background

Between TP#2 and TP#3, a oneM2M requirements matrix was generated containing candidate requirements. The  “Group 3” requirements, identified in the matrix as HLR-008, HLR-009 and HLR-168, covering:

- The assignment of unique M2M  service identifiers for a device

- A mechanism to assign devices to M2M service subscriptions.

- The association of underlying network identifiers for devices with the M2M service identifier for a device

Proposal

Incorporate the updated requirements into the Requirements TS.

Discussion

As we looked at these requirements we utilized the best definitions we have to date for subscription and subscriber.

Note:  Contribution oneM2M-REQ-2013-0242-Subscription_Term_Update.DOC discusses an update to the subscription term that would include time periods for the subscription.

| Subscriber | A role for a legitimate stakeholder who is accountable to a provider for consumption of a service by either the subscriber or other consumers that are authorized by the subscriber. [Contributor’s note: This concept of a “subscriber” is not the concept involved in a “subscribe/notify” mechanism such as mentioned in HLR-029, HLR-030 and HLR-032. Appropriate terms for that concept are for future study.] |
| --- | --- |
| Subscription | A classification of an agreement; where the agreement is between a provider and a subscriber for consumption of a service. A subscription is typically a commercial agreement. [Contributor’s note: This concept of a “subscription” is not the concept involved in a “subscribe/notify” mechanism such as mentioned in HLR-029, HLR-030 and HLR-032. Appropriate terms for that concept are for future study.] |

Group 3 did’t have any duplication so we needed to work on the wording of the requirements.

The following is the original requirement with the company comments and the initial draft of the requirements.

| Group 3 | Source | Contribution | Requirement | Comment |
| --- | --- | --- | --- | --- |
| HLR-008 | Alcatel-Lucent (ETSI), Huawei (CCSA) | oneM2M-REQ-2012-0035R04 | The M2M System shall be capable of identifying the M2M devices pertaining to a M2M service subscription by means of service level identification. | InterDigital Need to re-phrase to make it more straitforward. NEC unclear requirement LGE Not easy to get it. Motorola device identities should not depend on service levels. If you remove "by means of service level identification", then it is ok. Sprint The M2M System shall be capable of identifying the M2M devices associated (assigned?) to a M2M service subscription by means of service level identification. |
| HLR-009 | Alcatel-Lucent (ETSI), France Telecom (ETSI), NEC (ETSI) | 2012-0046R03 | The M2M System shall support one or more globally unique identifiers for the device. These identifiers do not change for the lifetime that the device has associated M2M Services. | KDDI Not only Global ID/address but private ID such as private address should be supported. The ID should be changeable. NTT The system should cover both of global and private IDs. InterDigital Line 61 and 62 can be merged Fujitsu If the identifiers are generated in the M2M System, we disagree them to be globally unique. We also disagree them not to be changed for the lifetime. If the identifiers are defined globally outside the M2M System, we agree with this requirement. Huawei 1) Clarification for associated M2M Services. 2) "devices" defined here do not include those that are invisible to the service platform? E.g. device behind a gateway Cisco Needs justification NXP The identifier should be inalterable and unclonable ALU The M2M System shall assign one or more globally unique identifiers for a device: - shall be globally unique in the M2M Service Capability Layer - shall not change over the lifetime of the device - shall not be re-used for different devices |
| HLR-168 | Alcatel-Lucent (ETSI), Huawei (CCSA) | oneM2M-REQ-2012-0035R04 | The M2M system shall be capable of associating the service level identification of an M2M device with the device identification capabilities offered by the underlying connectivity network. NOTE: In certain scenarios, it is possible to re-use the device identification provided by an underlying network as the service level identification of an M2M device. | LGE Need to define what service level is. Cisco Disagree Motorola needs clarification Sprint The M2M System shall be capable of associating the service level identification of an M2M device with the device identification capabilities offered by the underlying connectivity network if provided by the underlying connectivity network operator. |

Discussion Comments:

HLR-008: The M2M System shall be capable of identifying the M2M devices assigned to a M2M service subscription.

<TimC> M2M devices – This was suppose to include devices that host M2M services (e.g., M2M Device) as well as devices that require a M2M proxy. In ETSI these were D, D’ and d devices. I would change M2M devices in the above requirement to just “devices”.

The suggestion to resolve this was:

The M2M System shall be capable of identifying the devices assigned to a M2M service subscription.

HLR-009: The M2M System shall assign one or more globally unique identifiers for a device:

- shall be globally unique in the M2M Service Capability Layer

- shall not change over the lifetime of the device

- shall not be re-used for different devices

Concern of using the wording global for something that is only required to be unique within the context of the M2M System.

<TimC> There is some discussion around globally unique identifiers. The purpose of a globally unique is so that applications have a mechanism to identify the device. As such the identifier needs to be unique (assigned to only that device); needs to be global (if you have 2 M2M system instances – the device identifier needs to be unique across these instances; needs to be stable in that the identifier should not change over as long as the device is assigned to a M2M service subscription.

The suggestion to resolve this was:

The M2M System shall support one or more globally unique M2M service identifiers for the device. These identifiers do not change for the lifetime that the device is assigned to M2M services.

HLR-168:  The M2M System shall be capable of associating the service level identification of an M2M device with the device identification capabilities offered by the underlying connectivity network if provided by the underlying connectivity network operator.

Clarification has been requested for Service Level Identifications. Some confusion exist that this meaning was the same as SLA (bronze, silver, gold). This was not the intent. A better term would be “service identifier”

<TimC> This requirement was meant to say that we need to be able utilize the underlying network layer(s) capabilities to identify a device and associate/assign these identifiers to the globally unique identifier assigned by the service layer.

The suggestion to resolve this was:

If provided by the Underlying Network Layer, the M2M System shall be capable of associating the M2M service identifier of a device with the device identifiers offered by the Underlying Network Layer.