| Input contribution Use case |
| --- |
| Use Case Title:* | Use Case on M2M data traffic management by underlying network operator |
| Group Name:* | WG1 |
| Source:* | NTT DOCOMO |
| Contact: | Sunguk (Justin) Moon, NTT DOCOMO (moon@nttdocomo.co.jp) Kazuyuki Kozu, DOCOMO Euro-labs (kozu@docomolab-euro.com) Katsutoshi Nishida, NTT DOCOMO (nishidak@nttdocomo.co.jp) |
| Date:* | 2013-02-18 |
| Abstract:* | This use case introduces handling of M2M data transmission based on data traffic condition information of underlying networks and interworking among M2M service application servers, M2M platforms and underlying networks. |
| Agenda Item:* | 4.2 Use case |
| Work item(s): |  |
| Document(s) Impacted* |  |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Approval |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

## Title

### Use Case on M2M data traffic management by  underlying network operator

## Description

### According to the data traffic condition, e.g. current traffic congestion status, in underlying networks, the underlying network operators  (e.g. mobile network operators) would like to manage the M2M data traffic in their networks in conjunction with M2M service platform and/or M2M application server providers in order to avoid losing the M2M communication data packets in the networks.

### The M2M service platform and/or M2M application server providers will change their configuration such as data transmission interval or stop sending data over the underlying networks for some duration after receiving the notification from underlying networks.

### This use case illustrates handling of M2M data transmission based on the data traffic condition  information of underlying network and interworking among the M2M service application server, M2M platform and the underlying network.

## Source (as applicable)

### NTT DOCOMO

## Actors

### The M2M application server providing data transmission control according to the data traffic condition of underlying  network

### The application server has  functions to receive  data traffic condition information  from the M2M platforms and/or the underlying networks, and control M2M data transmissions according to the received information.

### The M2M service platform providing data transmission control according to the data traffic condition information of underlying  networks

### The M2M service platform has  functions to receive the data traffic condition information from the underlying networks, and/or control M2M data transmissions according to the information.

### The underlying network  providing the data traffic condition information

### The underlying network has  functions to send the data traffic condition information to M2M application servers, M2M service platforms, and/or M2M devices.

### The data traffic condition information includes required transmission interval, required maximum data rate, required maximum data volume, current traffic congestion status,  etc.

### The M2M device providing data transmission control according to the data traffic condition information

### The M2M device to receive the data traffic condition information from the underlying networks or M2M service platforms, and control M2M data transmissions.

## Pre-conditions (if any)

### The underlying network monitors the status of the data traffic, analyze the status, define the traffic condition  and provides the data traffic condition information to M2M application servers, M2M platforms and/or M2M devices.

## Triggers (if any)

## Normal Flow (as applicable)

## Normal Flow I

### The mobile network sends the data traffic condition information to the M2M service platform and/or M2M application server.

### The M2M application server receives the data traffic condition information and controls M2M data transmission accordingly.

### The M2M service platform receives the data traffic condition information and controls M2M data transmissions accordingly.

### The M2M service platform may send M2M data transmission condition information to the M2M device.

### The M2M device may receive M2M data transmission condition information and may control M2M data transmission.

## Normal Flow II (alternative)

### The mobile network sends the data traffic condition information to the M2M device as well as M2M service platform.

### Upon receiving the information, the M2M device re-configures the application behavior, e.g. the interval extension of communication, by M2M service layer capability. The re-configuration profile may be statically stored or can be overwritten by control from the M2M service platform.

### Upon receiving the information, the M2M service platform perform necessary control procedures, e.g. sending alerting message to a manager of M2M service subscriber, and may notify the network event to the M2M application server.

## Post-conditions (if any)

## High Level Illustration (as applicable)

## Potential requirements

### The M2M application server SHALL be able to control M2M data transmission based on the Underlying Network data traffic condition.

### The M2M service platform MAY be able to control M2M data transmission based on the Underlying Network data traffic condition.

### The M2M device SHALL be able to control M2M data transmission based on the Underlying Network data traffic condition.

### The M2M device SHALL control M2M application behavior implemented on top of M2M service layer when the M2M device received notification regarding Underlying Network data traffic condition from the Underlying Network.

# Text boxes

M2M application server

1

M2M service platform

2

3

1

Unerlying network

5

4

M2M device

2

Mobile network

1

M2M device