| INPUT CONTRIBUTION Requirement |
| --- |
| Group Name:* | REQ |
| Title:* | Input requirements on charging |
| Source:* | Huawei (CCSA), Huawei (ETSI) |
| Contact: | Yongjing Zhang, zhangyongjing@huawei.com |
| Date:* | <2013-02-17> |
| Abstract:* | This contribution provides revised input charging requirements based on comments received before TP#3. |
| Agenda Item:* | <Agenda item reference> |
| Work item(s): | WI0001 |
| Document(s) Impacted* | Technical Specification - M2M Requirements |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Approval and incorporation into oneM2M Requirement TS |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

Background

The following table shows the changes made to original requirements based on comments received in the requirement evaluation matrix.  Comments addressed by the modification are marked in green. The final proposed text (as accepted) for the requirement TS is shown in the next section “Proposed Requirements”.

| ID | Description | Comments received |
| --- | --- | --- |
| HLR-071 | The M2M System shall be able to support correlation between the charging records of the M2M service layer and available charging records of underlying network layer(e.g. data transport). <To be merged with HLR-073 in group 5 and the 4th charging requirement in oneM2M-REQ-2013-0153> | France Telecom: redundant with row 75 InterDigital: how are " the charging records of the M2M service layer " and the " charging records the Connectivity Layer" defined/specified? NEC: needs clarification NTT DoCoMo: <Comment> Term "M2M Service Layer" and "Connectivity Layer" should be clarified. ATT: *it depends on the definition of connectivity layer, *or available charging records provided by underlying networks? Fujistu: shall to may NTT: Items related to "charging" should be merged as a few number of "high level requirements". LGE: Add "of" (i.e. records "of" the connected layer). Replace shall with should/may. Cisco: The M2M System shall be able to support correlation between the charging records of the M2M service layer and available charging records of the transport services. Motorola: You should not have to "correlate", if you measure metrics from each layer separately. So The requirement should focus on the abiity to provide metrics at each level. Correlation may be done by a separate logic based on the metrics provided The M2M System shall be able to support collection of the charging records from both the M2M service layer and the Connectivity Layer. Sprint: this should be taken care of by offboard processing. |
| HLR-075 | The M2M system should support offline (i.e. post processed) charging at the M2M service layer. Note: Offline charging is a mechanism where charging information does not affect, in real-time, the service rendered. (refer to 3GPP TS 32.240 Section 4.1) | KDDI: "shall" should be changed to "should" or "may". NEC: What is online/offline charging in a M2M scenario? NTT DoCoMo: <Comment> Term "Offline Charging" should be clarified. Fujistu: shall to may NTT: Items related to "charging" should be merged as a few number of "high level requirements". LGE: Add definitions for onlin/offline charging and merge them in one REQ. Cisco: not clear Telefonica: want does on-line and off-line mean? Does it refer to post processed and real-time charging? |
| HLR-076 | The M2M system should support online (i.e. real-time) charging at the M2M service layer. Note: Online charging is a mechanism where charging information can affect, in real-time, the service rendered and therefore a direct interaction of the charging mechanism with the control of network resource usage is required. (refer to 3GPP TS 32.240 Section 4.1) <To be merged with the 3rd charging requirement in oneM2M-REQ-2013-0153> | KDDI: "shall" should be changed to "should" or "may". NEC: What is online/offline charging in a M2M scenario? NTT DoCoMo: Term "Online Charging" should be clarified. Fujistu: shall to may NTT: Items related to "charging" should be merged as a few number of "high level requirements". Cisco: not clear |
| HLR-134 | The M2M System shall be able to initiate charging specific information recording belonging to an M2M application or an M2M Gateway / Device for the purposes of charging and collection of statistics. <To be merged with HLR-072 in group5 and the 1st charging requirement in oneM2M-REQ-2013-0153> | France Telecom: The M2M System shall able to initiate information recording belonging to an M2M application or an M2M Gateway / Device for the purposes of charging and collection of statistics. Telecom Italia: We guess that the charging events tracked by the platform keep the application information InterDigital: May need to better define what is meant by 'information recording' Gemalto: Why just "initiate information recording"? Fujistu: shall to may NTT: Items related to "charging" should be merged as a few number of "high level requirements". LGE: 1) Remove "belonging to an M2M application or an M2M device" ALU: The M2M System shall be capable of maintaining configuration information of M2M Applications associated with a M2M service subscription. Motorola: subject to adherence to privacy regulations Sprint: The reference to M2M application leads me to believe that this is out of scope. Possibly more clarification of this requirement is needed to better understand. |
| HLR-135 | The M2M System shall provide the capability to initiate charging specific information recording based on triggers including timer and request for service or network capability invoking. <To be merged with the 1st charging requirement in oneM2M-REQ-2013-0153> | InterDigital: Information recording I think needs to be better clarified ATT: merge w row95. Gemalto: To whom/what does the system "provide the capability"? Should either be specific to service data, or should be reworded to indicate a decision of the M2M application for a recording, current wording may mean that application data can be recorded on decision from the M2M SP independently from the application! Motorola: repeat, see 82 |

Proposed Requirements

The following table lists the proposed requirement text for oneM2M requirement TS.

| Requirement ID | Classification | Requirement Text |
| --- | --- | --- |
| HLR-071 | Charging | The M2M System shall be able to support correlation between the charging records of the M2M service layer and available charging records of underlying network layer (e.g. data transport). <To be merged with HLR-073 in group 5 and the 4th charging requirement in oneM2M-REQ-2013-0153> |
| HLR-075 | Charging | The M2M system should support offline charging (i.e. post processed) at the M2M service layer. Note: Offline charging is a mechanism where charging information does not affect, in real-time, the service rendered. (refer to 3GPP TS 32.240 Section 4.1) |
| HLR-076 | Charging | The M2M system should support online (i.e. real-time) charging at the M2M service layer. Note: Online charging is a mechanism where charging information can affect, in real-time, the service rendered and therefore a direct interaction of the charging mechanism with the control of network resource usage is required. (refer to 3GPP TS 32.240 Section 4.1) <To be merged with the 3rd charging requirement in oneM2M-REQ-2013-0153> |
| HLR-134 | Charging | The M2M System shall be able to initiate charging specific information recording belonging to an M2M application or an M2M Gateway / Device for the purposes of charging and collection of statistics. <To be merged with HLR-072 in group5 and the 1st charging requirement in oneM2M-REQ-2013-0153> |
| HLR-135 | Charging | The M2M System shall provide the capability to initiate charging specific information recording based on triggers including timer and request for service or network capability invoking. <To be merged with the 1st charging requirement in oneM2M-REQ-2013-0153> |