| INPUT CONTRIBUTION Requirement |
| --- |
| Group Name:* | WG1, REQ |
| Title:* | Requirements for Information Delivery service in the devastated area |
| Source:* | Advanced Telecommunications Research Institute International, Sumitomo Electric Industries Ltd. (TTC), Alcatel-Lucent (ETSI) |
| Contact: | Masahiro Uno (ATR), <uno@atr.jp> Yoji Okada (SEI), <okada-yoji@sei.co.jp> Timothy Carey (ALU), < timothy.carey@alcatel-lucent.com> |
| Date:* | 2013-04-07 |
| Abstract:* | This contribution provides the altered potential requirements for Information Delivery service in the devastated area. |
| Agenda Item:* | Requirements |
| Work item(s): | Requirements |
| Document(s) Impacted* | Requirement specification |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Approval |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

The following potential requirements are changed in oneM2M-REQ-2012-074.

HLR-088 and 092 are divided into two parts.

| Requirement ID | Classification | Requirement Text |
| --- | --- | --- |
| HLR-088-a | Data reporting | The M2M System shall provide capabilities to Applications to update/synchronize Application specific databases between the Network Application and Gateway Application Fulfilled by HLR-041. |
| HLR-087 | Data reporting | The M2M System shall support transmission of Application specific data (e.g. tsunami and earthquake detection sensor data) from Devices and oneM2M external sources (e.g. ETWS data) to Applications in the Network. Fulfilled by HLR-046. |
| HLR-088-b | Data storage | A (wireless) Gateway shall be able to autonomously provide Devices that are attached via the LAN of the Gateway with trusted data that is locally stored in the Gateway even when the communication over the WAN connection of the Gateway to the Service Provider is not possible (e.g., network congestion, connectivity issues, Service Provider application is not operational). Trusted data and retrieval fulfilled by HLR-041 ACLs. |
| HLR-089 | Data reporting | A (wireless) Gateway shall be able to securely broadcast data (e.g. disaster warnings) to any M2M Device in its vicinity Fulfilled by HLR-010 |
| HLR-088-c | Data reporting | When the connection between the Gateway and M2M Service infrastructure is not available, authorized Devices shall be able to continue to access data that is locally stored by the M2M Service Layer in the Gateway. Fulfilled by R-2 of oneM2M-REQ-2013-0187R04 |
| HLR-092-a | Security | A M2M Device that receives broadcast data from a (wireless) Gateway shall be able to verify that the (wireless) Gateway is authorized to broadcast the data (e.g. disaster warnings) and that the data is authentic. Fulfilled by HLR-185 and HLR-213. |
| HLR-092-b | Security | The M2M System shall provide capabilities to the Service Provider to enable/disable open access of M2M Devices to the Gateway. If access of M2M Devices to the Gateway is open any M2M Device shall be allowed to receive data from the Gateway. If access of M2M Devices to the Gateway is not open only authorized M2M Devices shall be allowed to receive data from the Gateway. Fulfilled by HLR-180, HLR-201 |

### This work is supported by the Ministry of Internal Affairs and Communications of Japan under a grant entitled "Research and development of Dynamic Reconfigurable M2M Wireless Network Technology."