| Input contribution Use case |
| --- |
| Use Case Title:* | Use Case <Remote Maintenance services> |
| Group Name:* | <WG1>, <WG4> |
| Source:* | <Fujitsu (TTC)> |
| Contact: | Shingo Fujimoto, Fujitsu, <shingo_fujimoto@jp.fujitsu.com> Seigo Kotani, Fujitsu, <skotani@jp.fujitsu.com> |
| Date:* | <2013-04-11> |
| Abstract:* | This use case introduces a remote maintenance service based on the Car’s integrity which is endorsed by the hardware key which is protected by TPM. R01: revised based on discussions at TP#3 meeting. R02: revised based on private comments. R03: revised based on discussions at Apr.9th REQ WG call. |
| Agenda Item:* |  |
| Work item(s): |  |
| Document(s) Impacted* |  |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Potential Requirements should be considered to include the use case TR document. |

oneM2M IPR STATEMENT

“Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of an agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

## Title

### Use Case on the Remote Maintenance services

## Description

### This use case introduces a remote maintenance service for the automobiles (cars).

### Because integrity of the cars is a matter of human life, the remote maintenance service of the car (treated as M2M Gateway in this use case) should be strongly secured.

### Therefore, the integrity measurements both before and after the remote maintenance operation should also be severely performed.

### One of the methods to endorse the process might be guaranteed by HSM (Hardware Security Modules) in the M2M Gateway. In this case, the integrity measurement report can be made by the mechanism in the HSM and put the electronic signature by the key in the HSM.

### This use case is derived from the automobiles, but the similar case of the remote maintenance services could be considered with Medical equipment, Household applications, Financial transaction terminals and Industrial control and machinery.

### In the case where the security requirement is lower, the other methods such as software emulator could be used instead of HSM. In this case, the integrity measurement report would be made by the emulator and put the electronic signature by the key in the emulator. Therefore, the reliability level of the report should be lower than that of HSM case.

## Source (as applicable)

### Fujitsu(TTC)

## FFSActors (as applicable): 
Relevant to the name in the figure in Section 1.8, High Level Illustration.

### Car: the machine works as a M2M Gateway in which M2M Device(s) is implemented as the parts of it.

### Center: the M2M Platform which provides remote maintenance.

### TPM (Trusted Platform Module): one of the examples of HSM in the M2M Gateway, the hardware component for hardware level of security functions, to endorse the integrity measurement process and hold the electronic signature key.

### White list: data base in the center for verifying the integrity measurement report from the M2M Gateway, through TNC which is the secure communication protocol.

### Support software: installable software module to check the integrity of the Car assisted by TPM or the emulator and to support the newly implemented M2M Device(s) (i.e. sensor(s)).

## Pre-conditions (if any)
Center recognizes the software which is installed in the Car shall be updated.

## Triggers (if any)

### (None)

## Normal Flow (as applicable)

### Mutual authentication between the Car (M2M Gateway) and the Center (M2M Platform) is performed.

### Center requests the Car to report the integrity check on that Car.

### Support software which is installed in the Car runs integrity check of the Car assisted by TPM or the emulator.

### Generated integrity information data is endorsed by the hardware key which is protected by TPM. This report may contain a detection of the newly implemented sensor(s) (M2M Device(s)).

### Support software sends the report based on TNC (Trusted Network Connect, which is application level secure communication protocol) to the Center.

### Center verifies the report securely based on the White list.

### Center determines whether the Car contains the software which shall be updated.

### Center selects corresponding software modules.

### Center delivers the support software module to the Car.

### The support software is applied at the Car.

### The applied result endorsed by the device key (actual process is done by TPM or the emulator) is reported to the Center.

### Center side confirms the completion of delivery/embedding.

### Center side stores the sequence of operations log as certifiable evidence for indemnity.

## Post-conditions (if any)

### Newly installed software/sensor(s) is correctly identified as authorized part(s) on the Car, and working correctly with installed support software. The Car’s integrity information data which is endorsed by the key which is protected by TPM or the emulator is sent to the Center side.

## High Level Illustration (as applicable)

## Potential requirements (as applicable)

## The M2M service SHALL provide the mechanism for authorization for installing software/hardware component(s) on M2M Device(s) by referring the White List. In the case where the security requirement is higher, the White List SHALL be managed by Trusted Third Party.

## The M2M system SHALL support endorsement using device key on the integrity check for M2M Device(s).

## In the case where the security requirement is higher, the M2M Device SHALL support HSM(Hardware Security Module) to protect integrity of system itself.

# Text boxes

Trusted Computing enables:

- Verify current situation remotely

- Confirm installation completion

- Keep certifiable log for indemnity