| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG1 REQ |
| Title:* | Addendum to M2M Healthcare Gateway Use Case |
| Source:* | Qualcomm Inc. (TIA) |
| Contact: | Dilip Krishnaswamy, Qualcomm, dilipk@qti.qualcomm.com Josef Blanz, Qualcomm, jblanz@qti.qualcomm.com |
| Date:* | 2013-04-15 |
| Abstract:* | This document suggests an addendum to the M2M Healthcare Gateway Use Case included in the Use Case TR. |
| Agenda Item:* | REQ #26 |
| Work item(s): | WI 0001 |
| Document(s) Impacted* | Technical Report - oneM2M use case collection |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree to include proposed changes in section 7 of the use case TR |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

## Potential requirements

### Rationale

### This use case sets out from the presence of a gateway between one or more healthcare sensor(s) and a backend server. Even though the use case is assuming a cellular gateway, this restriction is not needed in general.

### Resulting requirement:

### 1.	The M2M system shall be capable of supporting gateway nodes that are capable of transporting sensor measurements to back end servers.

### Rationale

### Sensors can measure patient data with or without patient initiation. Therefore, new measurement data may become available at any time.

### Resulting requirement:

### 2.	Whenever a healthcare sensor has measurement data available, it shall be possible for the sensor to send a request to the local healthcare gateway to transport new measurement data to the backend server.

### Rationale

### Incoming requests from the healthcare sensor to the healthcare gateway may not result in immediate forwarding of the data to the backend server if any of the following is applicable: Dynamically changing cellular network availability (coverage); cellular network utilization constraints (policies); device energy consumption or memory constraints. In one of the flows also the quality of the data to be transported (alert=high priority) was relevant for determining when the connection needs to be triggered.

### Resulting requirements:

### 3.	The local healthcare gateway needs to be capable to buffer incoming requests from the healthcare sensor for transporting data to the backend server and support forwarding them at a later time – which could potentially be a very long time in the order of hours, days or even more – depending on cellular network availability, cellular network utilization policies, device constraints

### 4.	The local healthcare gateway needs to be capable to accept parameters with incoming requests from the healthcare sensor which define a delay tolerance for initiating the delivery of the sensor measurements or parameters for categorizing sensor measurements into different levels of priority/QoS.

### 5.	The local healthcare gateway needs to be cable of receiving policies which express cellular network utilization constraints and which shall govern the decision making in the gateway when initiating connectivity over cellular networks.

### 6.	The local healthcare gateway needs to be capable to trigger connections to the cellular network in line with the parameters given by the request to transport data and in line with configured policies regarding utilization of the cellular network

### A subscription and notification mechanism was described in this use case. Only authenticated and authorized users (e.g. care-giver, relatives, doctors) shall be able to subscribe to healthcare sensor measurement data and get notifications and access to the measured data. These authenticated and authorized stakeholders are typically using applications that use the M2M system to access the measured data. Resulting requirement:

### 7.	The M2M system shall be capable of supporting a mechanism to allow applications (residing on the local gateway, on the backend server or on the sensor itself) to subscribe to data of interest and get notifications on changes or availability of that data.

### 8.	The M2M system needs to be able to allow access to data that is being transported or buffered only to authenticated and authorized applications

### Rationale

### The use case also describes a flow in which the backend server could initiate an action on the local healthcare gateway. Resulting requirements:

### 9.	The M2M system shall support transport of data from the backend server to the cellular healthcare gateway.

### 10.	The M2M system shall support of triggering a cellular connection to the local healthcare gateway in case the gateway supports such functionality.

### Rationale

### Different subscribers may be interested in different information so that each subscriber may want to get notified only for events of interest to that subscriber:

### 11.	Subscriber-specific filters can be set up at the healthcare service enterprise backend server so that each subscriber can be notified only when information/events relevant to the subscriber are available/occur.

### Rationale

### The M2M healthcare gateway device can be in a sleep mode of operation to save energy and/or save radio/network resources  and can be without an active network connection. A patient monitoring app may be desirous of communicating with the gateway device when the gateway device is in this sleep mode of operation

### 12.	The M2M system shall be able to support a wakeup trigger (aka "shoulder-tap") mechanism (such as using SMS or alternate mechanisms) to wake up the gateway. The gateway can subsequently establish a network connection and query the enterprise backend server for additional information, and the enterprise backend server may then respond with adequate information to enable further processing of its request.