| INPUT CONTRIBUTION Requirement |
| --- |
| Group Name:* | REQ-WG TP#4 |
| Title:* | Requirements for Road Hazard Signaling application |
| Source:* | Huawei technologies |
| Contact: | Qi Yu, Huawei technologies, yuqi@huawei.com Linyi Tian, Huawei technologies, tianlinyi@huawei.com Bin Zhen, Huawei technologies, zhenbin@huawei.com Abdelmajid Khelil, Huawei technologies, abdelmajid.khelil@huawei.com |
| Date:* | <2013-04-07> |
| Abstract:* | This contribution updates the potential requirements for Road Hazard Signaling application. |
| Agenda Item:* | Requirements |
| Work item(s): | Requirements |
| Document(s) Impacted* | Requirement specification |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Approval |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

- Rationales

To fulfil the use case listed in contribution oneM2M-REQ-2013-0146-Use_case-Road_Hazard_Signalling_application, we propose REQ-WG to adopt the following requirements which were revised based on the comments.

Geocast is defined at [1] which means the action to broadcast information into a well delimited geographical area to receiver tuned for receiving.

- Requirement

| Requirement ID | Classification | Requirement Text |
| --- | --- | --- |
| R-xxxx | System | The M2M system shall provide a mechanism for the M2M Device to geocast a message to all M2M devices subscribed to the service. |
| R-xxxxx | System | The M2M system shall provide a mechanism for the M2M Gateway to geocast the message to the M2M Devices after received the trigger from the M2M application. |

- Reference

[1] ETSI TS 103 084 V0.0.3 (2012-10) Geomessaging Enabler