| Input contribution Use case |
| --- |
| Use Case Title:* | Oil and Gas Pipeline Cellular/Satellite Gateway |
| Group Name:* | WG1 REQ |
| Source:* | Qualcomm Inc. (TIA) |
| Contact: | Dilip Krishnaswamy, Qualcomm, dilipk@qti.qualcomm.com Heidi Broeking, Qualcomm, broeking@qualcomm.com Yenamandra Rao, Qualcomm, ysrao@qti.qualcomm.com ..... Josef Blanz, Qualcomm, jblanz@qti.qualcomm.com |
| Date:* | 2013-041-15 |
| Abstract:* | An M2M cellular gateway for Oil and Gas Pipelines is described. |
| Agenda Item:* | REQ #26 (No Agenda available at time of drafting) |
| Work item(s): | oneM2M-WI-0001-Requirements |
| Document(s) Impacted* | oneM2M-TR-0001-UseCase |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree to include the proposed use case into the TR. |

oneM2M IPR STATEMENT

“Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of an agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

## Title

### Oil and Gas Pipeline Cellular/Satellite Gateway

## Description

### This use case addresses a cellular gateway to transport oil and gas pipeline data to a backend server, to remote monitor and manage pipeline meters, Oil and gas companies can have meters are remote destinations that makes manual monitoring of the state of these meters as an expensive task to be pursued on a regular basis. Automated monitoring of oil and gas pipeline data can streamline the remote monitoring and management of these remote pipeline meters.

## Source

### Qualcomm

## Actors

### Oil and gas pipeline meters, cellular networks, backend servers, remote monitoring and management software

## Pre-conditions

### Cellular network connectivity, Satellite connectivity

## Triggers

### New pipeline sensor data requiring transport to a backend server

### Network dynamic access constraint or network utilization constraints or prior network access policy constraints or device energy minimization considerations can cause delay tolerant sensor data to be buffered (and aggregated if needed) at the gateway and transmitted at a later time

### Processing of recent measurements can result in remote requests for additional or more frequent measurements

### A firmware upgrade becomes available that needs to get pushed to the gateways

## Normal Flow

### Sensor data related to oil/gas quantity and quality, pressure, load, temperature, and consumption data is forwarded to backend server that is processed by a remote monitoring service associated with the oil and gas pipeline. Pipeline sensors and pipeline cellular gateways can communicate with each other wirelessly (if sensors and gateways are different nodes in the system). Pipeline cellular or satellite gateways can serve as aggregation points.  Sensor data may be locally forwarded until it reaches a gateway or directly transmitted to the gateway depending on proximity of the sensor(s) to each gateway on the pipeline.

### Alternative flow 1

### Pipeline meter data can be stored, aggregated, and forwarded at an appropriate time based on network availability constraints or policy constraints or energy minimization constraints for the pipeline meter gateway. Transmission policies can be designed made to minimize network overhead.

### Alternative flow 2

### Pipeline meter data can be processed by the remote monitoring and management service. If any anomalies are detected, additional measurements could be triggered, or more frequent measurements could be triggered, or measurements by additional sensors can be triggered by the remote service manager. Firmware upgrades can also be provided by the remote management service. Remote measurement requests are typically triggered or polled only as absolutely needed so as to avoid the overhead of unnecessary polling and network congestion using such schemes with Normal Flow or Alternative Flow 1 preferred for reporting sensor data.

## Post-conditions

### Sensor data is stored in a database associated with the backend server. Remote monitoring service verifies the status of the different pipeline meters.

### Alternative flow 1

### Data is buffered and transmitted when the network or policy constraints or energy optimization constraints allow transmission of delay-tolerant pipeline sensor data

### Alternative flow 2

### More frequent or additional measurement request events can get triggered from the network based on processing of recent measurement data.

## High Level Illustration

## Potential requirements

### Pipeline sensor data can be stored-and-forwarded and aggregated to be transmitted at an appropriate time

### Gateway needs to be able to aware of dynamically changing network access and link utilization constraints and gateway device energy constraints

### End-to-end system needs to allow for provisioning of policies at the gateway for data transmission

### Backend processing can result in additional or more frequent measurement of sensor data

### Ability to provide remote firmware upgrades is desirable for these pipeline gateways at remote locations

### Ability to locally forward data wirelessly between nodes to a local aggregation point serving as a gateway may be desirable depending on the location of sensor nodes and gateway nodes.

### System shall determine policy for transmitting data such as a scheduled transmission versus an aggressive polling request based on the urgency of information, or aggregating information based on delay tolerance, to best utilize network resources.