| INPUT CONTRIBUTION Requirement |
| --- |
| Group Name:* | REQ |
| Title:* | Requirements from use cases oneM2M-REQ-2013- 0231 and oneM2M-REQ-2013-0137 |
| Source:* | Joerg Swetina, NEC, Joerg.swetina@neclab.eu |
| Contact: |  |
| Date:* | 2013-04-15 |
| Abstract:* | This contribution collects the requirements from use cases oneM2M-REQ-2013-0120 and oneM2M-REQ-2013-0137, which are submitted to TP#3 / REQ#2 |
| Agenda Item:* | <Agenda item reference> |
| Work item(s): | Requirements |
| Document(s) Impacted* | Requirements Specification |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | It is proposed to include the requirements into oneM2M Requirements Specification. |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

| Requirement ID | Classification | Requirement Text |
| --- | --- | --- |
| R-xxxx | Interfaces to Underlying Networks, Support of Optimization for M2M traffic in mobile networks | Service Capabilities in the M2M Service Infrastructure shall be able to provide the Underlying Network with information related to M2M Devices that allows optimizations in the Underlying Network with regard to M2M traffic. Examples of such information, useful to a cellular network, are: the current (or change of the) set of data transmission scheduling descriptors including interval times (5min, 30 min, 1h), time ranges(10pm-6pm) etc. of the M2M Device the current (or change of the) mobility characteristics including moving range (e.g. high mobility, low mobility, no mobility, or speed range), moving direction and moving speed, etc. of the M2M Device Note 1: How to utilize such information by the cellular network is dependent on the Network Operator’s implementation and outside the scope of oneM2M. Note 2: The interface to convey such information to the Underlying Network will depend on the type (e.g. 3GPP, 3GPP2, fixed) of the Underlying Network |
|  | Interfaces to Underlying Networks, Support of Optimization for M2M traffic in mobile networks | Service Capabilities in the M2M Service Infrastructure may support receiving information related to M2M Devices that allows optimizations in the Underlying Network from the M2M Application to compute the information to be provided to the Underlying Network by analyzing the information received from the M2M Application before providing it to the Underlying Network. |