| INPUT CONTRIBUTION Requirement |
| --- |
| Group Name:* | REQ |
| Title:* | Requirements derived from use cases oneM2M-REQ-2013-0231R02 and oneM2M-REQ-2013-0137R02 |
| Source:* | NEC |
| Contact: | Takanori Iwai, NEC(t-iwai@hx.jp.nec.com) Joerg Swetina, NEC (joerg.swetina@neclab.eu) Ataru Kobayashi, NEC(a-kobayashi@df.jp.nec.com) Tetsuo Inoue, NEC(t-inoue@fp.jp.nec.com) |
| Date:* | 2013-06-06 |
| Abstract:* | This contribution collects the requirements from use cases oneM2M-REQ-2013-0231R02 (was 0120) and oneM2M-REQ-2013-0137R02, which were agreed at REQ#26 (TP#4) |
| Agenda Item:* | <Agenda item reference> |
| Work item(s): | Requirements |
| Document(s) Impacted* | Requirements Specification: oneM2M-TS-0002-Requirements |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | It is proposed to include the requirements into oneM2M Requirements Specification. |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

Introduction

Use cases oneM2M-REQ-2013-0231R02 (was 0120) and oneM2M-REQ-2013-0137R02, which were agreed at REQ#26 (TP#4), illustrated interworking of oneM2M with mobile networks (e.g. 3GPP, 3GPP2 ..). Information about the traffic characteristics of an M2M device allows oneM2M to support the underlying mobile network with network specific parameters for the device that can be used for M2M traffic shaping.

While it is not clear yet, if dedicated interfaces to underlying mobile networks – e.g. 3GPP– will be available for that purpose (see LS oneM2M-TP-2013-0251R01 to 3GPP SA2), an M2M Solution may still provide this information to underlying mobile networks through operator network specific interfaces or other open access models (e.g. OMA, GSMA OneAPI framework). [See also requirements OSR-005 and OSR-006]

Proposed Requirement:

| Requirement ID | Classification | Requirement Text |
| --- | --- | --- |
| tbd | Operational requirements | The M2M System shall be able to receive information from M2M Applications related to usage and traffic characteristics of M2M Devices or M2M Gateways by the M2M Application. It includes the following MTC Features for a device as specified in section 7.2 of 3GPP TS 22.368: Low mobility for characterizing devices that do not move, move infrequently, or move only within a certain region Time controlled devices to send or receive data only during defined time intervals |
| tbd | Operational requirements | Depending on availability of suitable interfaces provided by the Underlying Network the M2M System shall be able to provide information related to usage and traffic characteristics of M2M Devices or M2M Gateways to the Underlying Network |