| INPUT CONTRIBUTION Initial requirements subset |
| --- |
| Group Name:* | REQ-WGs |
| Title:* | Sleepy Node Requirements |
| Source:* | InterDigital Communications, Sprint |
| Contact: |  |
| Date:* | 2013-05-20 |
| Abstract:* |  |
| Agenda Item:* | Requirements |
| Work item(s): | Requirements |
| Document(s) Impacted* | Requirements TS |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Discussion and initial agreement for potential inclusion in the requirement TS at the TP2 meeting |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

# Potential requirements

# Sleepy Node related requirements for resubmission

The following is a list of previously submitted requirements with impact on SN functionality, which are now re-submitted for consideration for this scenario.

| Temp req. nr. | Submitted req. number | Text |
| --- | --- | --- |
| SNR-001 | HLR-118 | The M2M System may be aware of the reachability state of the nodes. Editor’s Note : node needs to be defined |
| SNR-002 | HLR-024, OSR-002 | The M2M system shall support communication means that can accommodate devices with capabilities of: Constrained computing (e.g. small CPU, small/zero available volatile memory, small/zero non-volatile memory, battery) or rich computing (e.g. large CPU, large memory) and Constrained communication (e.g. 2G wireless modem, certain WLAN node, sleepy node) or rich communication (e.g. 3/4G wireless modem, wireline). |
| SNR-003a | HLR-055 | The M2M System should support time synchronization with a universal clock source. |
| SNR-003b | HLR-055 | M2M Devices and M2M Gateways may support time synchronization with the M2M System. |
| SNR-004 | HLR-114 | The M2M System shall support testing the connectivity towards a selected set of M2M Applications |
| SNR-005 | HLR-047 | The M2M System shall be able to manage the scheduling of network access and of messaging. |
| SNR-006 | HLR-096 | The M2M System shall be able to aggregate requests depending on a given delay and/or category. |
| SNR-007 | HLR-115 | The M2M System shall be able to monitor the operational status of M2M Applications and their resources |

# Newly proposed requirements.

| Temp req. nr. | Text |
| --- | --- |
| N-001 | The M2M System shall support communication with devices which go to sleep and wake up according to well defined time schedules (e.g. periodic) as well as devices which go to sleep and wake up in an unpredictable and spontaneous manner (e.g. event based). |
| N-002 | The M2M System shall be able to utilize sleep schedules generated by either the M2M Device or the M2M Application . |