| INPUT CONTRIBUTION |
| --- |
| Group Name:* | REQ WG / MAS WG |
| Title:* | Consolidated ABS-related requirements from WG5 |
| Source:* | NEC (ETSI), Samsung SDS, InterDigital, LG Electronics |
| Contact: | Jaeseung Song (jaeseung.song@neclab.eu) |
| Date:* | 2013-06-04 |
| Abstract:* | This contribution proposes consolidated requirements and definitions for Abstraction and Semantics from WG5. |
| Agenda Item:* | Tbd |
| Work item(s): | Requirements, Abstraction&Semantics |
| Document(s) Impacted* | The Requirements TS and the Definitions TR |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Discussion and agreement for potential inclusion in the Requirement TS and the Definitions TR. |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

- Introduction

From various input documents proposing ABS-related requirements, MAS WG has prepared a list of consolidated requirements.

Please note that the input documents used as the source of the discussion are as follows:

- oneM2M-REQ-2013-0162R02

- oneM2M-REQ-2013-0159R4 (InterDigital, Samsung SDS, LGE)

- oneM2M-MAS-2013-0020 (NEC)

This contribution shows a list of consolidated ABS-related requirements from WG5 and proposes to add them to the Requirements TS.

This contribution also proposes several required definitions for Abstraction and Semantics Enablement.

- Consolidated requirements (Proposal)

NOTE:

  - Blue colored cell (Previously agreed requirements)

  - Yellow colored cell (Merged and under discussion)

| REQ-Number | Category | Requirements | Status |
| --- | --- | --- | --- |
| ABS-02 | Abstraction | The M2M system shall be able to provide translation mechanisms among Information Models (including meta-data) used by M2M Applications, M2M Devices/Gateways, and other devices. | Agreed but revised |
| ABS-03 (X-02) | Semantics | The M2M System shall provide capabilities to manage semantic descriptions of resources and M2M Applications, e.g, create, retrieve, update, delete, associate/link. Editor’s Note: Resources may be changed the meaning after the discussion of WG2. Editor’s Note: If M2M Application is part of Resource, M2M Application need to be removed. | Agreed |
| ABS-04 (E-01) | Semantics | The M2M System shall support a common modeling language for semantic descriptions (including relationships between Things) in order to make them available to M2M Applications. | Agreed |
| ABS-07 (out of X-05) | Semantics | The M2M System shall be able to provide interworking capabilities between different modeling languages for semantic descriptions. | Agreed |
| ABS-08 (E-03) | Abstraction | The M2M System shall provide capabilities to represent Virtual Devices and Things, (which are not necessarily physical devices.) | Agreed |
| ABS-9 (out of HLR-101, E-02) | Semantics | The M2M System shall provide capabilities to discover M2M Resources based on semantic descriptions. | Agreed |
| ABS-10 (X-01b) | Semantics | The M2M System shall support the capability to access semantic descriptions which are outside of the M2M System. | Agreed |