| INPUT CONTRIBUTION Requirement |
| --- |
| Group Name:* | WG1 REQ @ TP#5 |
| Title:* | New Requirements based on Healthcare GW |
| Source:* | Dilip Krishnaswamy, Qualcomm Incorporated, dilipk@qti.qualcomm.com |
| Contact: | Josef Blanz, Qualcomm Incorporated, jblanz@qti.qualcomm.com |
| Date:* | 2013-06-09 |
| Abstract:* | This contribution suggests new requirements based on the Healthcare Gateway Use Case. |
| Agenda Item:* | WG1 REQ session on Requirements TS (Agenda not available at time of drafting this) |
| Work item(s): | WI-0001 |
| Document(s) Impacted* | oneM2M-TS-0002-Requirements |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree to the inclusion of the proposed requirements in R0001-R0006 |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement..

| Requirement ID | Classification | Requirement Text |
| --- | --- | --- |
| R-0001 | Communication Request Processing | M2M Gateways and M2M Devices or in general M2M nodes that offer communication services to attached application or other nodes need to be capable of buffering incoming requests for communicating data to another node in the M2M system and support forwarding them at a later time depending on communication policies and based on associated Preferred Communication Characteristics. |
| R-0002 | Communication Request Processing | Preferred Communication Characteristics associated with a Communication Request shall allow the definition of delay tolerance and/or QoS stream processing parameters for initiating the delivery of data categorizing communication requests into different levels of priority or QoS classes |
| R-0003 | Communication Request Processing | M2M Gateways and M2M Devices or in general M2M nodes that offer communication services to attached application or other nodes need to be able to concurrently process multiple threads of communication requests from different sources with awareness for the request-specific Preferred Communication Characteristics. Each of request-specific Preferred Communication Characteristics shall be taken into account for the processed of the individual communication request while observing the provisioned communication policies. |
| R-0004 | Communication Request Processing | The M2M system shall be able to support a mechanism by which M2M nodes in the system that are not always reachable by other M2M nodes through supported communication connections can be triggered to establish a connection to the M2M system such that M2M functions on the triggered nodes can be reached from other nodes. |
| R-0005 | Communication Request Processing | The M2M system shall be able to support a mechanism to send data to a group of recipients. |
| R-0006 | Communication Request Processing | When supporting M2M-sessions (OSR-0003), the M2M system shall be able to support persistent existence of M2M-sessions across periods of time when previously used communication links have been disabled. |