| INPUT CONTRIBUTION |
| --- |
| Group Name:* | REQ |
| Title:* | Update on OSR-033 |
| Source:* | LG Electronics |
| Contact: | Hongbeom Ahn, LG Electronics, hongbeom.ahn@lge.com Seungmyeong Jeong, LG Electronics, seungmyeong.jeong@lge.com |
| Date:* | 2013-06-18 |
| Abstract:* | Update on requirement OSR-033 following the revision oneM2M-REQ-2013-0335R02 |
| Agenda Item:* | REQ |
| Work item(s): | WI 0001 |
| Document(s) Impacted* | Technical Specification - M2M Requirements |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Approve the requirements and integrate the requirements into the TS document |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

1	Rationale

Following the discussion on “Definition of Local Context” (oneM2M-REQ-2013-0335R02), the agreed requirement OSR-033 needs to be changed against oneM2M-TS-0002-Requirements-V0_3_0.

- oneM2M-REQ-2013-0335R02, Dynamic Device/Gateway context is Dynamic metrics, which may impact the M2M operations of M2M Devices/Gateways

:

2	Proposed Requirements

========== Changes against oneM2M-TS-0002-Requirements-V0_3_0.=======

| OSR-033 | Based on the dynamic device/gateway context (e.g., low battery) of the M2M Gateway and/or Device and the defined event categorization, the M2M System shall provide the capability to dynamically adjust the scheduling of reporting and notification of the M2M Device/Gateway. Note: for example, if the battery of Gateway is remained only 10% or below, the Gateway notifies the M2M service platform of the status. The M2M Application in the Infrastructure node will adjust the scheduling of reporting and notification based on the event categorization associated with each message. Consequently, the M2M Gateway operates longer. |
| --- | --- |