| INPUT CONTRIBUTION Initial requirements subset |
| --- |
| Group Name:* | REQ-WGs |
| Title:* | Sleepy Node Requirements |
| Source:* | InterDigital Communications Sprint |
| Contact: | Catalina.Mladin@InterDigital.com, Laurent.Laporte@sprint.com |
| Date:* | 2013-07-20 |
| Abstract:* | Requirements supporting the Sleepy Node Use Case. R01 update: SNR-005 wording change based on Cisco input. R02 update: N-001 and N-002 updated based on TP#5 comments |
| Agenda Item:* | Requirements |
| Work item(s): | Requirements |
| Document(s) Impacted* | Requirements TS |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Discussion and initial agreement for potential inclusion in the requirement TS at the TP5 meeting |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

# Potential requirements

# Newly proposed requirements.

| Temp req. nr. | Text |
| --- | --- |
| N-001 | The M2M System shall support communication with devices which are reachable based on well defined time schedules (e.g. periodic) as well as devices which are reachable in an unpredictable and spontaneous manner (e.g. event based). |
| N-002 | The M2M System shall be able to utilize reachability schedules generated by either the M2M Device or the M2M Application . |

# Sleepy Node requirements based on previous submissions

The following is a list of requirements with impact on Sleepy Node  functionality, which are based on previous requirement submissions. They are now proposed for consideration based on this scenario, with possible modifications.

| Temp req. nr. | Previous req. nr. | Text |
| --- | --- | --- |
| SNR-001 | HLR-118 | The M2M System may be aware of the reachability state of the nodes. Editor’s Note : node needs to be defined |
| SNR-002 | HLR-024, OSR-002 | The M2M system shall support communication means that can accommodate devices with capabilities of: Constrained computing (e.g. small CPU, small/zero available volatile memory, small/zero non-volatile memory, battery) or rich computing (e.g. large CPU, large memory) and Constrained communication (e.g. 2G wireless modem, certain WLAN node, sleepy node) or rich communication (e.g. 3/4G wireless modem, wireline). |
| SNR-003a | HLR-055 | The M2M System should support time synchronization with a universal clock source. |
| SNR-003b | HLR-055 | M2M Devices and M2M Gateways may support time synchronization with the M2M System. |
| SNR-004 | HLR-114 | The M2M System shall support testing the connectivity towards a selected set of M2M Applications. |
| SNR-005 | HLR-047 | The M2M System shall be able to manage the scheduling of M2M Device/Gateway network connectivity and of messaging. |
| SNR-006 | HLR-096 | The M2M System shall be able to aggregate requests depending on a given delay and/or category. |
| SNR-007 | HLR-115 | The M2M System shall be able to monitor the operational status of M2M Applications and their resources. |