| INPUT CONTRIBUTION Proposed Requirements from “Hydro-Power Generation using Satellite” Use Case |
| --- |
| Group Name:* | WG1 |
| Title:* | Proposed Requirements from Hydro-Power Monitoring Satellite Use Case |
| Source:* | Inmarsat |
| Contact: | Hilary David Tolga Ors Kerry-Lynn Gauci Nicolas Damour |
| Date:* | 2013-June-03 |
| Abstract:* | This contribution contains requirements from a Hydro-Power Generation using Satellite Use Case which was noted in TP3. This document is for TP5 to formally submit requirements for consideration in the Requirement-TS. |
| Agenda Item:* | Input Contribution for Requirements |
| Work item(s): | Requirements |
| Document(s) Impacted* | Requirement-TS |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Proposed requirements should be part of requirement TS. |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

Rationale

M2M systems will communicate primarily using IP-based communications.

Remote sensors are normally connected to a Remote Terminal Unit (RTUs) that condition the sensors values into registers that are transmitted to a host. The RTU polls (or changes register value in some circumstances) register values from sensors. The RTU will then use a M2M communication protocol to send the register values to the host. The used protocols are usually designed to be very compact, only sending the minimum required data to the host. If the data is critical that acknowledgement that the data was received is important and the underlying network should support protocol acknowledgement mechanisms as those used by TCP/IP.

There were additional requirements in the Hydro-Power Monitoring Satellite Use Case which are not presented here because either they were covered by other existing requirements or the requirements or because they will  be presented at a later date supported by new use cases.

Suggested Requirements

| Requirement ID | Classification | Requirement Text |
| --- | --- | --- |
| OSR-SWIR-YY (to be renumbered) | <System, Protocols> | The M2M system shall be able to support capability for the M2M application to select communication protocol acknowledgment mechanisms. |