| INPUT CONTRIBUTION Requirement |
| --- |
| Group Name:* | WG1 REQ @ TP#5 |
| Title:* | New Requirements based on Healthcare GW |
| Source:* | Dilip Krishnaswamy, Qualcomm Incorporated, dilipk@qti.qualcomm.com |
| Contact: | Josef Blanz, Qualcomm Incorporated, jblanz@qti.qualcomm.com |
| Date:* | 2013-06-09 |
| Abstract:* | This contribution suggests new requirements based on the Healthcare Gateway Use Case. |
| Agenda Item:* | WG1 REQ session on Requirements TS (Agenda not available at time of drafting this) |
| Work item(s): | WI-0001 |
| Document(s) Impacted* | oneM2M-TS-0002-Requirements |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree to the inclusion of the proposed requirements in R0001-R0006 |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement..

| Requirement ID | Classification | Requirement Text |
| --- | --- | --- |
| R-0001 | Communication Request Processing | The M2M System shall be able to support M2M Gateways and M2M Devices or in general M2M nodes that offer communication services to attached application or other nodes to buffer incoming requests for communicating data to another node in the M2M system and support forwarding them at a later time depending on communication policies and based on service preference associated with the communication reuests. |
| R-0002 | Communication Request Processing | Service preferenceassociated with a communication request by the issuer shall allow the definition of delay tolerance and/or QoS stream processing parameters for initiating the delivery of data categorizing communication requests into different levels of priority or QoS classes Editor’s note: OSR-013 and OSR-032 seems similar requirements, but this requirement is specifically talking about the service preference included in the communication request. [OSR-013] The M2M System shall be aware of the delay tolerance acceptable by the M2M Application and shall schedule the communication accordingly or request the underlying network to do it, based on policies criteria. [OSR-032] The M2M System shall support event categorization (e.g., normal, urgency) associated with data for M2M applications when collecting, storing and reporting that data. |
| R-0003 | Communication Request Processing | The M2M System shall be able to support M2M Gateways and M2M Devices or in general M2M nodes that offer communication services to attached application or other nodes to concurrently process multiple threads of communication requests from different sources with awareness for theservice preference associated with the requets while observing the provisioned communication policies. |
|  |  | Editor’s Note: Covered by OSR-012 and OSR-40. [OSR-012] The M2M System shall support communications between M2M Applications and Devices supporting M2M services by means of continuous or non-continuous connectivity. [OSR] The M2M system shall be able to leverage multiple communication mechanisms (such as USSD or SMS) when available in the underlying networks. |
|  |  | Editor’s Note: Covered by OSR-037. [OSR-037] The M2M System shall enable a M2M Application to request to send data, in a manner independent of the Underlying Network, to the M2M Applications of a group of M2M Devices and M2M Gateways in geographic areas that are specified by the M2M Application. |
| R-0006 | Communication Request Processing | The M2M System shall be able to partially maintain M2M sessions while some of the services needed for a session are unavailable when previously used communication links have been disabled. |