| INPUT CONTRIBUTION Requirement |
| --- |
| Group Name:* | WG1 REQ @ TP#5 |
| Title:* | New Requirements based on Healthcare GW |
| Source:* | Dilip Krishnaswamy, Qualcomm Incorporated, dilipk@qti.qualcomm.com |
| Contact: | Josef Blanz, Qualcomm Incorporated, jblanz@qti.qualcomm.com |
| Date:* | 2013-06-09 |
| Abstract:* | This contribution suggests new requirements based on the Healthcare Gateway Use Case. |
| Agenda Item:* | WG1 REQ session on Requirements TS (Agenda not available at time of drafting this) |
| Work item(s): | WI-0001 |
| Document(s) Impacted* | oneM2M-TS-0002-Requirements |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree to the inclusion of the proposed requirements in R0001-R0006 |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement..

| Requirement ID | Classification | Requirement Text |
| --- | --- | --- |
| R-0001 | Communication Request Processing | The M2M System shall be able to support M2M Gateways and M2M Devices that offer communication services to M2M Application to buffer incoming messages for communicating data to another M2M Gateway/Device/Infrastructure and support forwarding them at a later time depending on communication policies and based on service preference associated with the messages. |
| R-0002 | Communication Request Processing | The M2M system shall enable an M2M Application to send a communication request with the following service preference: delay tolerance and/or QoS parameters for initiating the delivery of data categorizing communication requests into different levels of priority or QoS classes |
| R-0003 | Communication Request Processing | The M2M System shall be able to support M2M Gateways and M2M Devices that offer communication services to M2M application to concurrently process messages from different sources with awareness for theservice preference associated with the messages while observing the provisioned communication policies. |
| R-0006 | Communication Request Processing | The M2M System shall be able to maintain context associated with M2M sessions (e.g. security context or network connectivity context during the interruption of the session). |