| INPUT CONTRIBUTION |
| --- |
| Group Name:* | REQ |
| Title:* | Requirements for Quality of Service |
| Source:* | KT |
| Contact: | Hyung-soo (Hans) KIM, hans9@kt.com |
| Date:* | 2013-06-05 |
| Abstract:* | M2M systems should meet the required QoS-level for M2M applications. This contribution suggests QoS-related requirement, such as QoS classes, Performance Objectives, etc. |
| Agenda Item:* | REQ |
| Work item(s): | WI 0001 |
| Document(s) Impacted* | Technical Specification - M2M Requirements |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Approve the requirements and integrate the requirements into the TS document |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

1	Rationale

An M2M application is needed to meet the required QoS-level on M2M system. The required QoS-level will be varied from Best Effort to the stringent level and a number of levels (as many as applications defined) should be indentified depending on the different purposes of data delivery.

The limited number of QoS classes can support a wide range of applications. While the performance needs of these applications are more demanding than most, there may be other applications that require new or revised classes. Any desire for new classes must be balanced with the requirement of feasible implementation, and the number of classes must be small for implementations to scale in M2M underlying networks.

In order to support on planning, development (design), operations and maintenance of M2M system, the QoS-level should be clearly observable and measurable, based on the parameters quantified through performance objectives such as delay, delay variation, loss and error, etc.

2	Proposed Requirements

| Requirement ID | Classification | Requirement Text |
| --- | --- | --- |
| R-0xx | Overall System Requirements | The M2M system shall meet the required QoS-level for M2M applications. The M2M underlying network shall support a few number of QoS (Quality of Service) classes to deliver M2M applications. And each QoS class shall specify the performance objectives in association with QoS parameters, such as delay, delay variation, loss ratio and error rate, etc. |