| INPUT CONTRIBUTION REMAINING PROPOSED REQUIREMENTS from “Computation and Analytics” Use case |
| --- |
| Group Name:* | WG1 |
| Source:* | Cisco Systems |
| Format:* |  |
| Date:* | 2013-06-24 |
| Contact:* | Philip Jacobs, phjacobs@cisco.com |
| Abstract:* | This contribution contains remaining potential requirements from the Analytics Use Case accepted on 19 March (oneM2M-REQ-2012-0102R02). This was formerly oneM2M-REQ-2013-0157R05 This revision compares the potential requirements against existing requirements and reduces the proposed requirements down to 3. |
| Agenda Item:* | Requirements |
| Work item(s): | WI 0001 - Requirements TS |
| Document(s) Impacted* | oneM2M-TR-0001-Requirements |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Inclusion of requirements |

oneM2M IPR STATEMENT

“Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of an agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

# Analytics for M2M

# Analytics can involve a range of computations from very simple to extremely complex algorithms. We suggest using the term compute/analytics in the proposed requirements to recognise the range. This contribution proposes oneM2M support for analytics which is independent of the algorithm.

# While the TR analytics use case focussed on backhaul traffic reduction where the distributed compute/analytics reduced the device data to send just the critical stuff, distributed compute/analytics also supports many other functions, such as local actions like closed-loop control, and the triggering of other oneM2M services.

# The benefit of using a common service layer is the similar to “cloud” – rather than have separate local compute/analytics platforms for each application; the common service layer aggregates the demand from many applications onto a set of local compute platforms. The utilization of the platforms can be kept high and elastic compute demands of applications can be met.

# As a brief introduction, we include:

# A simple classification of the levels of analytics which oneM2M could support.

# Questions and Answers covering feedback received.

# An example functional view

## 1.1 Classification of analytics infrastructure for oneM2M

The main differences between the four levels below are:

- Centralized or distributed

- Whether the analytics are part of the Application or provided by oneM2M

- Whether analytics output can directly trigger oneM2M actions (as opposed to the data flowing up to the Application Server and back down through the oneM2M System)

## 1.2 Questions and Answers

# Q1- Does this proposal cross the boundary into the application domain?

# A1 - This proposal enables distributed infrastructure to run application analytics geographically close to devices, which trigger oneM2M actions and/or provide output to remote applications

# Q2 – Does this proposal need oneM2M to understand the meaning of device data from different domains?

# A2 – No, device data meaning is opaque to oneM2M

# Q3 – What interfaces get standardized?

# A3a – Inputs from Applications to oneM2M

# A oneM2M framework for proprietary VM spin-up directives e.g. compute, storage as used by cloud services

# OneM2M geo-location directives to specify where to place analytics

# Application analytics package (e.g. DMTF Open Virtualization Format Specification)

# A3b – Triggers from distributed application analytics to oneM2M to initiate actions

## 1.3 Example Functional View

# In the example figure below, Remote Application would likely be the application running on a server, oneM2M Core would likely be the oneM2M code running on servers.

# An example message sequence might be:

# Remote application requests analytics service and provides package pointer

# oneM2M system matches appropriate Local Distribution Compute Platform then loads package and local elements of oneM2M

# oneM2M redirects Device output to package which upon running compute/analytics, triggers an action to manage local devices and notifies the Remote Application

# Converting the analytics use case terminology to oneM2M terms:

# A compute/analytics package is an application program.

# A Local Distributed Compute Platform is an intermediate node.

# Where an intermediate node may have one or more application programs

## 1.4. Accepted requirements

### So far, one proposed requirement has been accepted from the analytics use case:

### The oneM2M system should provide mechanisms to accept requests from M2M application service providers for compute/analytics services.

## Consideration of other existing requirements

### The first remaining proposed requirement is “ The oneM2M system should provide mechanisms to accept application programs for distribution to intermediate nodes from M2M application service providers.”

### The closest existing requirement is OPR-002 “ The M2M System shall provide the capability for software management of M2M Applications.” However, this seems to assume that the M2M System already has the application program available. Whereas 1. Includes the previous uncovered step of accepting the application program from the M2M applications service provider. OPR-002 says nothing about where the managed applications reside, if can we assume it includes intermediate nodes then we could omit this from the proposed requirement, making it “The oneM2M system should provide mechanisms to accept application programs for distribution, from M2M application service providers.”

### The second remaining proposed requirement is “The oneM2M system should support the placement and running of application programs in intermediate nodes at locations requested by M2M applications service providers.”

### There are no requirements to place application programs in any nodes. There are no requirements for the M2M System to accept placement requests from M2M application service providers. Generalising, it seems we should not limit the requirement to “intermediate” nodes, making it “The oneM2M system should support the placement and running of application programs in M2M nodes at locations requested by M2M applications service providers.”

### The third remaining proposed requirement is “The oneM2M system should manage the lifecycle of application programs located in intermediate nodes.”

### This seems to be completely covered by OPR-002.

### The fourth remaining proposed requirement is “The oneM2M system should steer device data to applications located in intermediate nodes.”

### The closest existing requirement is OPR-019:

The M2M System shall support the capabilities to collect/store and report data from one or more M2M Devices or M2M Gateways, in ways requested by the M2M Application Infrastructure as listed below:

- action initiated either by an M2M Device, M2M Gateway, M2M Services Infrastructure, or M2M Application Infrastructure

- when triggered by schedule or event;

- for specified data

for delivery to one or more M2M Gateways, M2M Services Infrastructure, or M2M Application Infrastructure.

This seems to completely cover the fourth remaining proposed requirement, assuming that there is a service to orchestrate this.

### The fifth remaining proposed requirement is “The oneM2M system should take operational and management action as a result of an intermediate node’s application’s inputs”.

The closest existing requirement is OSR-9: The M2M System shall support the ability for single or multiple M2M Applications to interact with a single or multiple M2M Devices/Gateways (application in the device/gateway). However, the focus of this requirement is on the 1:1, 1:m, n:m aspects, and “interact” is non-specific. There is no requirement for the M2M System to accept requests from M2M Applications, therefore it would seem that this requirement be generalised to all nodes as “The oneM2M system should take operational and management action as a result of an application’s inputs”.

### 6. The sixth remaining proposed requirement is “The oneM2M system should specify supported application program triggers and actions”. What actions the M2M System supports in response to the applications inputs will be part of the oneM2M specification, so this proposed requirement is not needed.

## Revised Proposed requirements

### The oneM2M System shall be able to provide mechanisms to accept M2M Applications for distribution, from M2M application service providers.

### The oneM2M System shall be able to support the placement and operation of M2M Applications in selected M2M nodes per criteria requested by M2M Applications service providers, subject to access rights.

### The oneM2M System shall be able to take operational and management action as requested by M2M Applications.