| LIAISON STATEMENT |
| --- |
| Title:* | DRAFT LS on interfaces of oneM2M with Underlying Networks |
| Source:* | NEC |
| Date:* | 2013-04-19 |
| To:* | 3GPP SA1, 3GPP SA2, 3GPP SA3 |
| Copy: |  |
| Response to: | n/a |
| Send replies to:* | oneM2M_liaison@list.onem2m.org |
| Contacts* | Joerg Swetina, NEC, joerg.swetina@neclab.eu |
| List of attachments: | n/a |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

1	Discussion

OneM2M would like to thank 3GPP SA2 for its reply on our LS on “interaction of oneM2M with Underlying Networks”. The reply LS helped our understanding of the scope of MTCe work in 3GPP Rel-12: small data and device triggering enhancements (SDDTE) and UE power consumption optimizations (UEPCOP).

At the last oneM2M Technical Plenary meeting (TP#5) held in Seoul, S. Korea, 17-21 June 2013, it was considered beneficial to establish an on-going collaborative exchange of information between oneM2M and 3GPP.

Some of the features that oneM2M is working on that could require interworking with 3GPP Rel-12 and Rel-13 are listed below:

- An The M2M service provider may request broadcasting/multicasting to multiple devices in the Underlying Network (e.g. addressing a group of devices within a specified area for broadcast/multicasting of identical M2M data).

- An M2M service provider may request QoS and Prioritization for M2M communications to/from individual devices or groups of devices. A device may request QoS and Prioritization for M2M communications to/from the M2M Service Provider.

- An M2M service provider and an Underlying Network Service Provider may exchange information related to characteristics of M2M Devices or M2M Gateways, such as indications for small data, transmission scheduling parameters, mobility characteristics, etc..

- An M2M service provider and an Underlying Network Service Provider   may exchange information related to the congestion and load status in the 3GPP Network in order to allow the scheduling of the traffic by the oneM2M Service Layer (e.g. delay specific M2M traffic when the 3GPP Network experiences high traffic load).

- Dynamically (e.g. to enable plug and play) correlate the Service Enablement Framework identifier of M2M clients with the External Identifier used by the 3GPP network for the same MTC client.

- Enable the Service Layer to know the reachability status of the devices (e.g. status of last event to MTC device …).

- An M2M service provider and an Underlying Network Service Provider may exchange information on charging and subscriptions to support interworking with M2M service providers.

- An M2M service provider and an Underlying Network Service Provider may exchange information related to location information of M2M Devices or M2M Gateways, including parameters for expressing preferred positioning methods.

oneM2M expects that the type and contents of information exchange for the above would need to be discussed in more detail jointly

2	Actions

For 3GPP SA1:

oneM2M requests feedback on the following:

- In the existing 3GPP requirements for support of M2M, are there plans to specify interfaces & capabilities for the MTC features?

- What future plans does 3GPP have to include requirements for the enablement of external interfaces to a service layer in support of the above capabilities?

For 3GPP SA2 and SA3:

oneM2M requests feedback on the following:

- Are the existing interfaces within the 3GPP Network sufficient to be used by oneM2M to support the M2M capabilities listed above, or are enhancements required?

oneM2M meeting schedule:

| oneM2M TP#6 | Toronto, Canada | 05-09/08/2013 |
| --- | --- | --- |
| oneM2M TP#7 | Sophia-Antipolis, France | 14-18/10/2013 |
| oneM2M TP#8 | Miyazaki, Japan | 09-13/12/2013 |

# Comments

The agreed requirements do not address this so far. They only address reuse of GBA. We should not put this item in at this point in time since it is to vague and open to interpretation. We can wait until we have a better understanding of the security related interworking needs.

Can we remove this action?  I think that this item isn’t necessary. No actions will be taken in R12 beyond what has already been agreed.

We should not restrict this to Rel-12. So for Rel-13 the question is justified

Not sure if I understand: SA1 is not defining Interfaces or Capabilities, correct? If that is true, we should only ask them about plans on further requirements. Maybe I am off. I think it would be better to remove this.

Should we clarify what is meant by ‘above capabilities’? I think what is meant is the list of features in Section 1. Is that right? So then we should refer to those.

Same as previous comment: Not clear what ‘capabilities listed’ means… we call them ‘features’ earlier.

What we meant? I can work leveraging 3GPP security on some portion, and soemthing elseon other portions

I think we should remove this question until we have a more precise formulation from security experts. How should 3GPP experts know whether an oneM2M SL can operate securely based on current 3GPP defined security mechanisms if the M2M SL is not yet defined. This is a very vague question that is probably not possible to answer correctly with the information available to 3GPP so far.

I would like to get the security experts to formulate this question.  Also, we need to make sure that anything that we put here is consistent with the LS that we will be receiving from SA3 and the response that we may have to it.