| INPUT CONTRIBUTION Requirement |
| --- |
| Group Name:* | WG1 REQ |
| Title:* | Input Requirements for Correlation of Service Statuses Between Different Layers |
| Source:* | China Telecom, Huawei |
| Contact: | Yi Wang <wy@sttri.com.cn> Jiaxin Yin<yinjiaxin@huawei.com> |
| Date:* | <2013-06-26> |
| Abstract:* | This contribution provides some requirements related with M2M service status management between different layers , derived from the contribution ”M2M Service Provisioning for Equipment with Built-in M2M Device”. It is also a child document derived from REQ-173R05. |
| Agenda Item:* |  |
| Work item(s): |  |
| Document(s) Impacted* | Technical Specification - M2M Requirements |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Approval and incorporation into oneM2M Requirement TS |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

Background

This contribution provides some requirements related with M2M service status management between different layers. These requirements are derived from the contribution, “M2M Service Provisioning for Equipment with Built-in M2M Device”. It is also related with REQ-173R05.

Proposed Requirements

The following is the definition of different service statuses.

1. The administrative status of the service

Definition：The administrative status of the service for a user or a device is to tell whether the service provider allows this service to be run for this user or within this device.

Explanation:  The service provider may allow or prohibit the service to be run for a user or within a device following the rules in service contract, management policy, or some other management reasons. A user can use the service or a device can run the service only if the service provider sets the administrative status of the service for this user or this device as 'allowed'. If the service provider sets the administrative status of the service for this user or this device as 'not allowed', the user can't use the service or a device can't run the service.

2. The operational status of the service

Definition: The operational status of the service for a user or a device is to tell whether this service is operational or available for this user or within the device in the current time.

Explanation: Normally, the operational status of the service for a user or a device is ‘available’. But sometimes, the service for a user or a device is not available for the time being due to some reasons, such as the lack of necessary resource, some system modules’ recovery process from failure, the shutdown of supporting service, or some other reasons.   In this case, the operational status of the service for a user or a device is ‘unavailable’.

Note 1: The administrative status and operational status of the service for a user or a device are independent of each other. But the operational status for a user or a device will be 'unavailable' when the administrative status for this user or this device changes to 'not allowed'.

Note 2: There are three kinds of services corresponding with three layers in M2M ecosystem. They are Network service, M2M service, and Application service, which correspondingly is provided by MNO, M2M SP and Application Provider.  For each kind of service, there are two kinds of statuses, administrative status and operational status. But normally, it’s enough for M2M System to identify and manage three of them,

- M2M Service administrative status of devices

- M2M Service operational status of devices

- Network Service administrative status of mobile network identifiers

The following table lists the proposed requirement text for oneM2M requirement TS.

| Requirement ID | Classification | Requirement Text |
| --- | --- | --- |
| REQ-A | Management | The M2M System should support the correlation between the service identifier of a device in service layer and the related mobile network identifier in underlying mobile network layer. Note1: Different MNOs may expose different kinds of network identifiers to the M2M System. Note 2: This requirement is the same as the requirement HLR-168 described in oneM2M-REQ-2013-0148R04. |
| REQ-B | Management | The M2M System shall identify and manage M2M Service administrative status and M2M Service operational status of devices. |
| REQ-C | Management | The M2M System should identify Network Service administrative status of device-related network identifiers such as IMSI, MSISDN, MDN, or External Id if underlying mobile network can provide the administrative status info. |
| REQ-D | Management | The M2M System may produce a notification to update the Network Service administrative status of related mobile network identifier to ‘allowed’ or ‘not allowed’ when the M2M Service administrative status of the device changes to ‘allowed’ or ‘not allowed’, if underlying mobile network can receive such notification and has subscribed such notification. |
| REQ-E | Management | When the M2M System receives the notification from the underlying mobile network that Network Service administrative status of a mobile network identifier has changed to ‘not allowed’, the M2M System should update the M2M Service operational status of related device as ‘unavailable’, if the underlying mobile network can send such notification to the M2M System. |
| REQ-F | Management | The M2M System shall notify the M2M Application when M2M Service administrative status or M2M Service operational status of a device changes if M2M Application has subscribed such notification. |
| REQ-G | Management | The M2M System should be able to have a M2M Application change M2M Service administrative status of a device. |