| INPUT CONTRIBUTION Requirement |
| --- |
| Group Name:* | REQ |
| Title:* | Health Vertical Requirements |
| Source:* | Michael Kirwan, Continua Health Alliance, <contact info> |
| Contact: |  |
| Date:* | 2013-07-27 |
| Abstract:* | Members of the Continua Health Alliance have identified a number of requirements that may be useful in developing health sensors with embedded cellular modems, yet are outside the scope of the Continua Health Alliance Design Guidelines. These out-of-scope requirements are articulated herein. Furthermore, many of these requirements may also be useful in supporting Smart Building, Devices & Things, and Audio/Video Use Cases currently being defined by oneM2M. |
| Agenda Item:* |  |
| Work item(s): |  |
| Document(s) Impacted* | <A list of the Technical Report(s), Technical Specification(s) or other documents that are impacted by this contribution> |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Identify which requirements are applicable to oneM2M and make recommendations as to which standards organization would best address any remaining requirements. |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

Informational Background regarding Continua:

Continua Health Alliance is an international not-for-profit industry organization enabling end-to-end, plug-and-play connectivity of devices and services for personal health management and healthcare delivery. Its mission is to empower information-driven health management and facilitate the incorporation of health and wellness into the day-to-day lives of consumers. Continua is a pioneer in establishing standards-based guidelines and security for connected health technologies such as smart phones, gateways and remote monitoring devices. Its activities include a certification and brand support program, events and collaborations to support technology and clinical innovation, as well as outreach to employers, payers, governments and care providers. With over 200 member companies reaching across the globe, Continua is comprised of technology, medical device and healthcare industry leaders and service providers dedicated to making personal connected health a reality. For more information visit: www.continuaalliance.org.

Continua references standards and specifications selected by Continua members for ensuring interoperability of devices. It also contains additional Design Guidelines for interoperability that further clarify these standards and specifications by reducing options in the underlying standard or specification or by adding a feature missing in the underlying standard or specification. These guidelines focus on the following interfaces:

TAN-IF – Interface between Touch Area Network health devices and Application Hosting Devices

PAN-IF - Interface between Personal Area Network health devices and Application Hosting Devices

LAN-IF - Interface between Local Area Network health devices and Application Hosting Devices

WAN-IF - Interface between Application Hosting Devices and Wide Area Network health devices

HRN-IF - Interface between Wide Area Network health devices and Health Record Network health devices

The below requirements are associated with only the Continua WAN Interface.

In the Continua End-to-End Reference Architecture, the WAN Interface (WAN-IF) connects an Application Hosting Device (AHD) to a WAN Device (WD). See figure below.

The Continua WAN-IF Design Guidelines are focused on enabling the interoperable transmission of messages related to device observations across a Wide Area Network.  By enabling Continua device data to be securely and interoperably exchanged, personal health data can be liberated from the dead-end of device displays in order to provide insight to service providers and care specialists.  This information can be used to drive more intelligent processes that will reduce overall cost and improve the health and wellness of consumers.

Additional information regarding Continua can be found within their Design Guidelines found within the oneM2M document pool (ftp://ftp.onem2m.org/Pool/Continua/).

Critical Requirements for discussion and decision at TP#6 are noted below (highlighted).

| Requirement ID | Classification | Requirement Text |
| --- | --- | --- |
| R-Note | OSR | The following set of requirements may be useful to facilitate communication between Continua compliant medical devices over a cellular network. |
| R-001 | OSR: WAN-IF_Bidirectional | WAN-IF SHALL support the bidirectional exchange of data. |
| R-002 | OSR: WAN-IF_Notification | WAN-IF SHALL support the notification/event from WAN device to the AHD. |
| R-003 | OSR: WAN-IF_Notification_Ack | AHD SHALL respond to the notification/event send from the WAN Device. |
| R-004 | OSR: WAN-IF_AHD_Reliable_Delivery | WAN-IF SHALL guarantee reliable delivery of WAN data from AHD to the WAN Device and from the WAN Device to the AHD. |
| R-005 | OSR: WAN-IF_Session_Layer_Request_Queuing | WAN-IF session layer SHALL support the ability to queuing incoming requests in case that network connectivity is interrupted and resume processing queued requests when network connectivity is re-established. |
| R-006 | OSR: WAN-IF_IP | WAN-IF SHALL use IP based exchange methodologies. |
| R-007 | OSR: WAN-IF_AHD_WAN_Device_Class_Capabilities_Query | WAN-IF SHALL enable an AHD to query the WAN device for its' supported device classes and capabilities. |
| R-008 | OSR: WAN-IF_WAN_Service_Discovery | WAN-IF SHALL enable a WAN Device to query an AHD for its' supported device classes and capabilities. |
| R-009 | OSR: WAN-IF_AHD_Connection_Establishment | Setting up the transport connection of the Continua WAN interface SHALL be initiated only from the Application Hosting Device. |
| R-010 | OSR: WAN-IF_AHD_Service_Discovery | WAN-IF SHALL enable an AHD to query the WAN device whether it supports a specific service (e.g. questionnaire service) |
| R-011 | OSR: WAN-IF_WAN_Service_Discovery | WAN-IF SHALL enable a WAN Device to query an AHD whether it supports a specific service (e.g. questionnaire service) |
| R-012 | OSR: WAN-IF_Exchange_Configuration_Information | WAN-IF SHALL enable AHDs and WAN devices to exchange the configuration information necessary to initiate a specific service. |
| R-013 | OSR: WAN-IF_AHD_Query | WAN-IF SHALL enable AHD to query the WAN Device for new content. |
| R-014 | OSR: WAN-IF_AHD_Retrieval | WAN-IF SHALL enable retrieval (or download) of the content from the WAN device. The type of content is denoted by MIME type. |
| R-015 | OSR: WAN-IF_Local_Service_Discovery | WAN will enable local service discovery (WAN device to discover local services at AHD) |
| R-016 | OSR: WAN-IF_Remote_Service_Discovery | WAN will enable remote service discovery (AHD to discover remote services) |
| R-017 | OSR: WAN-IF_Local_Device_Discovery | WAN will enable local device discovery (WAN device to discover local devices associated with AHD) |
| R-018 | OSR: WAN-IF_Remote_Device_Discovery | WAN will enable remote device discovery (AHD to discover devices (such as subscribed devices) connected to WAN device) |
| R-019 | OSR: WAN-IF_Local_Resource_Discovery | WAN will enable local resource discovery (WAN device to be able to discover resources associated with AHD) |
| R-020 | OSR: WAN-IF_Remote_Resource_Discovery | WAN will enable remote resource discovery (AHD to be able to discover resources associated with WAN device) |
| R-021 | OSR: WAN-IF_RESTful_Local_Access | WAN will provide RESTful local resource access (WAN device to able to query and access resources associated with AHD) |
| R-022 | OSR: WAN-IF_RESTful_Remote_Access | WAN will provide RESTful remote resource access (AHD to be able to query and access resources associated with WAN device) |
| R-023 | OSR: WAN-IF_Delay_Tolerant_Data | WAN will support delay tolerant data transfer over WAN interface based based on a prespecified delay management policy (testable) |
| R-024 | OSR: WAN-IF_Security_Profile_Selection | WAN will enable selection of a security profile across its endpoints (AHD and WAN to agree upon a security profile from a set of possible profiles) |
| R-025 | OSR: WAN-IF_Aggregate_Data | WAN interface will be able to aggregate data to enable a bulk data transfer upon network connectivity |
| R-026 | OSR: WAN-IF_Network_Connectivity_Policy | WAN interface will support the ability to delay/postpone network connectivity by buffering data based on a network connectivity policy (testable time-based policy or link quality-based policy) |
| R-027 | OSR: WAN-IF_Network_Selection_Policy | WAN will support the ability to select a network interface for connectivity when multiple connectivity options are available based on a network connectivity selection policy (testable time-based or link-quality based policy) |
| R-028 | OSR: WAN-IF_Network_Lacking | WAN interface will provide feedback on availability or lack of availability of network connectivity |
| R-029 | OSR: WAN-IF_Guarantee_Delay | WAN interface will provide guarantees (mean, worst-case) for delay tolerance for delay-tolerant processing |
| R-030 | OSR: WAN-IF_Bandwidth_Availability | WAN interface will provide guarantees (mean, worst-case) on bandwidth availability for streaming |
| R-031 | OSR: WAN-IF_EndtoEnd_Latency | WAN interface will provide guarantees (mean, worst-case) on end-to-end latency for streaming |
| R-032 | OSR: WAN-IF_QoS_Parameter | WAN interface will provide change in QoS parameter (delay tolerance, bandwidth, end-to-end latency) guarantees dynamically to enable interface adaptation |
| R-033 | OSR: WAN-IF_Device_Trigger | WAN will enable incoming device triggering/wakeup (from WAN to AHD) |
| R-034 | OSR: WAN-IF_Incoming_Event_Notification | WAN will enable incoming event notification (from WAN device to AHD) |
| R-045 | OSR: WAN-IF_Outgoing_Event_Notification | WAN will enable outgoing event notification (from AHD to WAN device) |
| R-036 | OSR: WAN-IF_Subscribe_Notification | WAN will allow devices/users to subscribe to notifications |
| R-037 | OSR: WAN-IF_Subscribe_Event_Notification | WAN will notify subscribed users upon event occurrence on interface |
| R-038 | OSR: WAN-IF_Capability_Adaptation | WAN shall support end-to-end capability adaptation. |
| R-039 | OSR: WAN-IF_Session_Layer_Reliability | WAN shall support session layer reliability. |
| R-040 | OSR: WAN-IF_AHD_DEVICE_MANAGEMENT | WAN-IF SHALL support secure transport of device management exchanges allowing the WAN device to manage the AHD in line with industry standards for device management. |
| R-041 | OSR: WAN-IF_AHD_REMOTE_DEVICE_MANAGEMENT | WAN-IF SHALL support secure transport of device management exchanges allowing the WAN device to manage remote devices connected to the AHD in line with industry standards for device management |
| R-042 | OSR: Store and Forward_Interface | Store and Forward AHD shall support RESTful exchange of data. |
| R-043 | OSR: E2E_Arch_DataFlow_Episodic_Sensors_Upload | The architecture shall support the bottom-up transfer of episodic sensor information. |
| R-044 | OSR: E2E_Arch_DataFlow_Batch_Sensors_Upload | The architecture shall support the bottom-up transfer of batch sensor information. |
| R-045 | OSR: E2E_Arch_UID_Exchange | The architecture shall support exchange of the user information across the end-to-end services. |
| R-046 | store and forward_input_sensors | Store and Forward AHD shall have the capability to receive observations on continua certified interfaces from a set of sensors |
| R-047 | OSR: store and forward_output_service_providers | Store and Forward AHD shall have the capability to forward observations to a set of service providers on Continua certified WAN-IFs. |
| R-048 | OSR: store and forward_identification | Store and Forward AHD shall identify users as an AHD may be used by multiple users. |
| R-049 | OSR: store and forward_authentication | Store and Forward AHD shall have the capability to authenticate the user. |
| R-050 | OSR: Provisioning | SL shall support remote provisioning of devices with credentials for using the service layer. |
| R-051 | OSR: Connectivity Types | SL shall support multiple connectivity types (e.g. WLAN vs. WWAN). |
| R-052 | OSR: Interface | The interface to the SF Function shall use RESTful style to exchange data. Data to be exchanged shall be addressed using URIs. Requests could be one of Create, Retrieve, Update, Delete (CRUD). |
| R-053 | OSR: Tolerable Delay | Requests for data exchanges shall support optional indication of time tolerance. If no time tolerance is indicated a default value shall be used (provided by policies). |
| R-054 | Categorization of Traffic | Requests for data exchanges shall support optional indication of a traffic category that can be used inside the SL to determine appropriate connectivity. If no traffic category is indicated a default value shall be used (provided by policies). |
| R-055 | OSR: Buffering Behavior (over time) | The SF function shall indicate on request how much data it is capable of storing. The minimum buffer size that the SL shall support per device is XXX MB. |
| R-056 | OSR: Data Exchange Request Size | SF function shall be capable of supporting individual requests for exchanging data with a size of XXX MB. On request, the SF function shall indicate what the maximum supported individual request size is. |
| R-057 | OSR: Data Rate | On request, the SF function shall be capable of indicating the supported data rate and types of connectivity (e.g. 2G, 3G, WIFI). |
| R-058 | OSR: Time-Synchonization | The SF function shall support requests with absolute time deadline (e.g. needs to be there by midnight). |
| R-059 | OSR: Preferred Transport | The SL shall be capable of taking into account preferred transport technologies during decision making for connectovoyt management (this may over-ride SL decision). |
| R-060 | OSR: EAN interface | the EAN device shall be able to run a certifiable Continua interface |
| R-061 | OSR: EAN shall enable the use of 3GPP and/or 3GPP2 defined radio protocols | since an embedded cellular module is a pre-requisite the cellular network is also |
| R-062 | OSR: Time-Synchonization | EAN (Embedded Area Network) should allow for automatic setting of time |
| R-063 | OSR: Data access | EAN (Embedded Area Network) shall restrict use of cellular data to registered services |
| R-064 | OSR: Interoperability Support | EAN (Embedded Area Network) shall interoperate with the new WAN reciever |
| R-065 | OSR: Maintain IP Connectiivity | The EAN (Embedded Area Network) interface shall seek the best WAN interface (wired, wifi, cellular) to provide seamless IP connectivity under mobility constraints. |
| R-066 | OSR: Data volume | EAN (Embedded Area Network) should limit the global data message volume (REST better than SOAP) in order to reduce the cost of transmission and the power |
| R-067 | OSR: Access |  |
| R-068 | OSR: Coverage |  |
| R-069 | OSR: Capacity |  |
| R-070 | OSR: Efficiency |  |
| R-071 | OSR: Latency |  |
| R-072 | OSR: Data Rate | Data rate shall be sufficient to recreate a 120 hz 12 bit waveform in near real time. |
| R-073 | OSR: Interface Selection | Interface shall have a policy to dynamically select between available interfaces based on connectivity cost and performance. |
| R-074 | OSR: Maintain IP Connectivity | Interface shall seek the best WAN interface to provide seamless IP connectivity under mobility constraints. |
| R-075 | OSR: Interoperable | Interface shall interoperate with the new WAN receiver. |
| R-076 | OSR: Bit Rate | Interface shall determine appropriate bit rate for application based on available WAN performance. |
| R-077 | OSR: Frame Rate | Video shall be presented at a frame rate that creates a moving image sufficient to allow a tending physician to properly assess the patient condition. |
| R-078 | OSR: Latency | Latency of the video shall be minimized to support real-time conversation. |
| R-079 | OSR: Adaptive | Interface shall scale up or down performance based on parameters such as network conditions and remaining battery life. |
| R-080 | OSR: Interoperable | Interface shall interoperate with the new WAN receiver. |
| R-081 | OSR: Maintain IP Connectivity | Interface shall seek the best WAN interface (wired, wifi, cellular) to provide seamless IP connectivity under mobility constraints. |
| R-082 | MGR: Store and Forward_Policies | Store and Forward AHD should support policy specification/configuration functionality on the AHD. |
| R-083 | MGR: E2E_Arch_UID | The architecture shall support user identification. |
| R-084 | MGR: E2E_Arch_ MultiUser_device_Share | The architecture shall support physical device sharing among multiple individuals |
| R-085 | MGR: E2E_Arch_ MultiServices_device_Share | The architecture shall enable more than one end-to-end service to interact with the same physical device. |
| R-086 | MGR: E2E_Arch_CC_Time_Track_Creation_3 | If an Application Hosting Device (AHD) receives measurement data without a time mark, then the AHD that receives the measurement data shall supply a time mark based upon the AHD’s receive time of the data. |
| R-087 | MGR: store and forward_store | Store and Forward AHD shall have the capability to temporarily store observations |
| R-088 | MGR: store and forward_identity_mapping | Store and Forward AHD shall provide identity mapping functionality as different user IDs may be used across the input and output interfacess. |
| R-089 | MGR: store and forward_configuration | Store and Forward AHD shall be configurable (for example, it could classify measurements from a specific class of device to be of high priority and must be uploaded asap). |
| R-090 | MGR: Device Management | SL shall integrate protocols for device management (e.g. OMA DM) |
| R-091 | MGR: Scheduling & Connectivity Management | SL shall support scheduling of stored information for later forwarding according to provisioned policies to optimize network cost and load. Traffic shall be stored and forwarded later if the type of traffic is tolerant to that. SL shall also determine which connectivity among available options is appropriate to use as a function of categories of traffic - WLAN vs. WWAN. |
| R-092 | MGR: Policies | The SL shall support provisioning mechanisms to define policies on scheduling & connectivity management decisions. For instance, such policies could define what the minimum amount of data would be to trigger a network connection of a certain type. |
| R-093 | MGR: PAN/LAN interface | An EAN device shall include a WAN interface |
| R-094 | MGR: User Interace | An EAN shall enable headless (no display or input) device. |
| R-095 | MGR: User Identification | An EAN device shall provide a globally unique ID |
| R-096 | MGR: EAN shall support IEEE-11073 data semantics | devices may be Continua certified using 11073 |
| R-097 | MGR: Form Factor Sensor Device | EAN should only affect form factor in relation to adding cellular capability |
| R-098 | MGR: Communication Capability | EAN will respect IP abstration. |
| R-099 | MGR: Power Supply | an EAN shall enable battery powered devices |
| R-100 | MGR: Certification | EAN shall use a certified communication module |
| R-101 | MGR: Store and forward | EAN shall be able to store readings locally in case of loss of communication until memory is full or communcations restored when it shall transmit |
| R-102 | MGR: Regulatory | EAN shall conform to regulatory environment |
| R-103 | MGR: Sustainability | EAN should be not harmful to humans |
| R-104 | MGR: Battery |  |
| R-105 | MGR: Signaling |  |
| R-106 | MGR: Payload |  |
| R-107 | MGR: Form Factor |  |
| R-108 | MGR: User Interface |  |
| R-109 | MGR: Device Identification |  |
| R-110 | MGR: User Identification |  |
| R-111 | MGR: Authentication |  |
| R-112 | MGR: Provisioning |  |
| R-113 | MGR: Device Management |  |
| R-114 | MGR: Time Synchronization |  |
| R-115 | MGR: Codec |  |
| R-116 | MGR: Regulatory |  |
| R-117 | MGR: Radio |  |
| R-118 | MGR: Protocols |  |
| R-119 | MGR: Batch Transmission | Device shall be able to store waveforms for later transmission. |
| R-120 | MGR: Mobile Resolution | Video signal to mobile device shall use standardized horizontal and vertical resolutions. |
| R-121 | MGR: Clinic Monitor Resolution | Video signal to typical monitor shall use standardized horizontal and vertical resolutions |
| R-122 | MGR: Codec | Video frame sample size shall be reduced to make efficient use of network, memory, and power resources. |
| R-123 | MGR: Interface Selection | Interface shall have a policy to dynamically select between available interfaces based on connectivity cost and performance. |
| R-124 | DSR: WAN-IF_WAN_AHD_Device_Class_Capabilities_Visiblity | WAN-IF SHALL enable AHD and WAN Devices to expose their certified device classes and capabilities in resource oriented architecture fashion. |
| R-125 | DSR: WAN-IF_WAN_AHD_Device_Class_Capabilities_Representation | WAN-IF SHALL enable AHD and WAN Devices to use an interoperable representation of the certified device classes and capabilities. |
| R-126 | DSR: WAN-IF_WAN_AHD_Services_Visiblity | WAN-IF SHALL enable AHD and WAN Devices to make the capabilities/services visible. |
| R-127 | DSR: WAN-IF_WAN_AHD_Services_Representation | WAN-IF SHALL enable interoperable representation of the capabilities/services. |
| R-128 | DSR: WAN-IF_WAN_AHD_Identification_Certified_Device_Class | WAN-IF SHALL enable AHD and WAN devices to identify the certified devices classes. |
| R-129 | DSR: E2E_Arch_Data_DataFlow_tracking | Data model shall allow for the data flow tracking |
| R-130 | SER: WAN-IF_Device_Authentication | WAN-IF SHALL enable the authentication of the AHD and WAN Device. |
| R-131 | SER: WAN-IF_Data_Confidentiality_Transit | WAN-IF SHALL enable cryptographic confidentiality protection to mitigate threats of unauthorized data disclosure, for data in transit. Industry standard ciphersuites and methods SHALL be used. |
| R-132 | SER: WAN-IF_Data_Integrity_Transit | WAN-IF SHALL enable a cryptographic data integrty check mechamism to mitigate threats of data payload tampering, for data in transit. Industry standard ciphersuites and methods SHALL be used. |
| R-133 | SER: WAN-IF_Data_Confidentiality_Transit | WAN-IF SHALL enable cryptographic confidentiality protection to mitigate threats of unauthorized data disclosure, for data in transit. Industry standard ciphersuites and methods SHALL be used. |
| R-134 | SER: WAN-IF_Data_Integrity_Transit | WAN-IF SHALL enable a cryptographic data integrty check mechamism to mitigate threats of data payload tampering, for data in transit. Industry standard ciphersuites and methods SHALL be used. |
| R-135 | SER: WAN-IF_Data_Origin_Authenticity | WAN-IF SHALL enable data origin authentication. |
| R-136 | SER: WAN-IF_User_Identity | User identity SHALL be in a single namespace for each instance of a WAN-IF Sender to WAN-IF Receiver connection. User identity SHALL be unique within each WAN-IF defined namespace. |
| R-137 | SER: WAN-IF_End_User_Authentication | WAN-IF SHALL support industry standard two-party user authentication. This is used to enable the in-band provisioning of the token that could be used in the future interaction (e.g. data origin authentication) |
| R-138 | SER: WAN-IF_Device_Authentication | WAN-IF SHALL enable the authentication of the AHD and WAN Device. |
| R-139 | SER: Authentication | SL shall support mutual authentication of communication end points. |
| R-140 | SER: Encryption | On request the SL shall encrypt data that is being exchanged |
| R-141 | SER: Secure Environment | The EAN shall have a secure environment for identification of the patient and possibly secure storage, confidentiality and integrity. |
| R-142 | SER: Security | EAN (Embedded Area Network) shall ensure security through use of the secure environment |
| R-143 | SER: Data Integrity | EAN (Embedded Area Network) shall ensure data integrity |
| R-144 | SER: Consent Management | EAN (Embedded Area Network) interface shall support consent management |
| R-145 | SER: Security | Interface shall ensure data stream can only be accessed by authorized user. |
| R-146 | SER: Data Integrity | Interface shall employ end-to-end integrity protection / checking. |
| R-147 | SER: Security | Video shall be transmitted in secure manner to ensure patient privacy. |
| R-148 | SER: Data Integrity | Interface shall employ end-to-end integrity protection / checking. |
| R-149 | CHG: Form Factor Battery | EAN (Embedded Area Network) device shall be capable of reporting battery status. |
| R-150 | CHG: Battery Life | EAN (Embedded Area Network) shall be designed to minimise the battery draw to lowest possible level to ensure longer battery life |
| R-151 | OPR: e2e_sec_azn_authn_entity2_users+operators | The user identifier should be associated with his measurements as early as possible (on a first user authentication-capable device). |
| R-152 | OPR: e2e_sec_IM_patient_id_cross_referencing | The local user identifier used for authentication purposes shall be mapped into patient ID used by the healthcare service. |
| R-153 | OPR: store and forward_traceability | Store and Forward AHD shall provide traceability of the observations. It is required as service providers care about the quality of the observations and want to be able to trace the history of the observations |
| R-154 | OPR: List of Destinations | The SF function shall be capable to deliver stored data to multiple destinationa as indicated by the requestor (i.e. indicated by the URI or list of URIs). |