| INPUT CONTRIBUTION Requirement |
| --- |
| Group Name:* | REQ |
| Title:* | Health Vertical Requirements |
| Source:* | Michael Kirwan, Continua Health Alliance, <contact info> |
| Contact: |  |
| Date:* | 2013-07-27 |
| Abstract:* | Members of the Continua Health Alliance have identified a number of requirements that may be useful in developing health sensors with embedded cellular modems, yet are outside the scope of the Continua Health Alliance Design Guidelines. These out-of-scope requirements are articulated herein. Furthermore, many of these requirements may also be useful in supporting Smart Building, Devices & Things, and Audio/Video Use Cases currently being defined by oneM2M. |
| Agenda Item:* |  |
| Work item(s): |  |
| Document(s) Impacted* | <A list of the Technical Report(s), Technical Specification(s) or other documents that are impacted by this contribution> |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Identify which requirements are applicable to oneM2M and make recommendations as to which standards organization would best address any remaining requirements. |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

| Requirement ID | Classification | Requirement Text |
| --- | --- | --- |
| R-013 | OSR-019, SWIR-005 (new req. not yet in TS) | The M2M System shall be able to provide the capability of M2M Applications to exchange data with one or more authorized M2M Applications which are not known. |
| R-015 | OSR: WAN-IF_Local_Service_Discovery | The M2M System shall enable discovery of usable M2M Applications on an M2M Gateway or at an M2M Device |
| R-018 | OSR: WAN-IF_Remote_Device_Discovery | The M2M System shall enable discovery of M2M Gateways and M2M Devices available to an M2M Application for data exchange |
| R-021 | Non-functional Section 7 | Continua Health Alliance is incorporating a RESTful approach to its design. To support CHA, oneM2M should consider RESTful styles and approaches while designing the oneM2M architecture. |
| R-022 | Non-functional Section 7 | Continua Health Alliance is incorporating a RESTful approach to its design. To support CHA, oneM2M should consider RESTful styles and approaches while designing the oneM2M architecture. |