| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG1 |
| Title:* | Introduction of underlying notions for access control and authorization |
| Source:* | Gemalto |
| Contact: | Francois Ennesser, francois.ennesser@gemalto.com |
| Date:* | 2013-12-02 |
| Abstract:* | A need was identified at TP7 to clarify terminology around access control and authorization. As a first step in this direction, the present contribution proposes some text to introduce important notions in this domain, which could be introduced either in the Security TR-0008 or in the Roles and Focus Area TR-0005. R01 version adds modification shown in revision mark to the initial text. R02 adds clarification that policy decision takes place partly offline and partly online (yellow highlight). |
| Agenda Item:* |  |
| Work item(s): | WI-ooo7 |
| Document(s) Impacted* | oneM2M-TR-0005 Roles_and_Focus _Areas-V0_0_2 (preferred, to enhance visibility to oneM2M WGs), or TR-0008 Security. Possible impact on oneM2M-TR-0004 Definitions and Acronyms (to decide). |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Include proposed notions into oneM2M-TR-0005. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Rationale:

The intent of the “Roles and Focus Areas” TR was to identify functional roles and topics and derive appropriate terminology that will be useful to further elaborate the oneM2M specification. Since TP7 new notions related to Access Control and Authorization have emerged and a need was identified to introduce a related terminology.

This contribution attempts to describe important notions that could provide a basis to clarify further terminology.

# Proposal:

## Proposed Change:

Insert a new section related to Authorization and access control in TR-0005:

## 6.2.y	Notions related to access control and authorization

Access control and authorization are important aspects of several M2M scenarios, but they can involve a number of M2M roles in different positions depending on use cases. However, a general authorization and access control framework can be extracted that involves a few invariable access control notions which are mapped to M2M roles according to scenarios.

Indeed the general access control framework involves a “resource”, owned by a first actor (“resource owner”), which needs to be accessed by a second actor (“Resource consumer”).

In a real world scenario, the resource could be a bus, the resource owner would be the public transport company, and the resource consumer would be a passenger.

In an M2M scenario, the resource may be information such as the data generated by a first M2M application, the resource owner is the human being or a legal entity on behalf of which this application operates, and the resource consumer will be a data consuming M2M application.

For example, the resource may be the measurement stream generated by a water flow sensor, deployed in a river upstream by public authorities, which is useful to farmer downstream to manage their irrigation system. As another example, the resource may be the configuration parameters of a device deployed on the field.

The resource consumer  needs to request and obtain authorization to access the resource.

In the real world example of the public transport system, the passenger needs to buy a ticket from a ticket office, which often involves a monetary transaction.

In an M2M scenario, such a step implies  a willingful decision of the human being or legal entity on behalf of which the application operates. But human beings or legal entities want to make such decisions once, while they are awake: This process can generally take the form of deciding on a policy that will be used by an  M2M application to derive actual decisions.

In other words, the policy decision is performed partly offline involving humans and partly online involving applications running on beholf of humans, while policy enforcement takes place online i.e. during operation of the M2M applications.

In any case, the resource consumer actually obtains a kind of ticket (“access token”) that can be presented during operation as a proof that proper authorization has been granted by the resource owner. The ticket office that delivers the access token has to be a trusted entity,   which acts as a “policy decisioner” for distributing access tokens and could for example request authentication of the requestor.

In the first example above, the farmers wanting to use the water flow measurement stream could go to a web site, managed by the public authorities to open access to their sensors, and request to subscribe to the corresponding data stream for their irrigation applications. The irrigation applications would then obtain access tokens from the public authorities, acting as a policy decisioner.

Then, with the access token, the resource consumer can access the resource through a “policy enforcer” (the ticket controller in the public transport example), which may connect to the policy decisioner.  The policy enforcer is typically an agent contracted by the resource owner, e.g. an M2M Service Provider, which applies the policies set by the policy decisioner.

In the M2M scenario above, the farmer’s application would present the access token obtained from the public authorities when requesting subscription to the water flow measurement stream, to show that it is properly authorized to access those data.

Editor’s note: The terminology of “resource owner” and “policy decisioner” is FFS.