| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG1 |
| Title:* | Use cases of M2M Application for home automation |
| Source:* | Wan Yuan Sun, Chinese Academy Of Science R&D Center For Internet Of Things,sunwanyuan@ciotc.org |
| Contact: |  |
| Date:* | 2013-12-03 |
| Abstract:* | With the widely use of smart home, the design of the home automation becomes more important than before. Based on the architecture of the internet of things, we design a special architecture for home automation containing three layers (sensor layer, network layer and user service layer) |
| Agenda Item:* |  |
| Work item(s): | <A list of the designation of the relevant work item(s)> |
| Document(s) Impacted* | <A list of the Technical Report(s), Technical Specification(s) or other documents that are impacted by this contribution> |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* |  |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

1 Abbreviations

CPU	Central Processing Unit

MMS	Multimedia Message Service

2 General description of  M2M application for home automation

M2M applications for home automation including:

the remote monitoring of  house

possibly triggering alarms when emergency happens

the automation control of household appliances

In order to acquire the information of  the home, appropriate sensors have to be used. Now we use three-layer structure，which includes front-end sensor layer ,network layer and user service layer.

Figure 1：System Structure

The sensor layer consists of the smart entrance guard, sensor node and control node, etc., all these devices support variety of short distance wireless communication protocol. The network layer consists of a control terminal and public/private network . The user service layer provides human-device interactions.

3 Specific description of M2M application for home automation

3.1 The front-end sensor system

All device nodes communicate with control terminal through the short distance wireless communication protocol. Smart entrance guard contains anti-theft lock and monitoring. When anti-theft lock detects unauthorized key to unlock, anti-theft lock will capture the current monitor screen and send the alarm information to the control terminal.

The sensor node contains humiture detection, combustible gas detection, smoke detection and wireless infrared detection. When detecting anomalies, the sensor nodes will send detailed exception information to the control terminal.

Control node contains light control, air-conditioning control, fresh air system control, doors and window s control. Control terminal can send the command to the control node to realize the remote control. Doors and Windows control contains the opening and closing of the doors , Windows and curtain.

3.2 The interconnection and transmission of the network

Control terminal plays the role of heterogeneous converged network relay. It communicate with front-end device node through the sensor network module; communicate with user communication through cellular network module, so as to realize the interconnection of people and things.

Figure 2: Structure of control terminal

The structure of control terminal is shown in figure 2. The storage device is responsible for saving abnormal information. Keys and LCD forms the human-computer interaction interface.  The sensor network module is responsible for communicate with front-end device node, while the cellular network module is responsible for communicate with the remote user.

3.3  The remote monitoring for user

Users can receive the remote abnormal alarm information at real-time, also can control the household appliances which are realized by the help of cellular network module. When outsiders try to open the door, the terminal will captured monitor images by sending MMS to the user. While other nodes detect abnormalities, it will send short message to the user.

In order to realize the remote control , the user can send contract format of short message to control terminal. Control node contains the four control nodes in figure 1.