| Input contribution Use case |
| --- |
| Use Case Title:* | Remote air-conditioner location monitoring for manufacturer |
| Group Name:* | WG1 |
| Source:* | ChinaUnicom |
| Contact: | Peng Wang (wangpeng@chinaunicom.cn) Junling Mao (maojl11@chinaunicom.cn) Changwei Hu (hucw5@chinaunicom.cn) |
| Date:* | 2014-3-27 |
| Abstract:* | A user case named “remote air-conditioner location monitoring for manufacturer” is described in this document, which involves a new requirement that the M2M systems shall support the capability of reusing the SIM card activation and deactivation capability in underlay network. |
| Agenda Item:* | TBD |
| Work item(s): | TBD |
| Document(s) Impacted* | TBD |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Discussion and initial agreement for potential network API over mcn |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Title

### Remote air-conditioner location monitoring for manufacturer

## Description

### The air conditioner manufacturer intends to utilize the monitoring module installed in the air conditioner to monitor the location of sold air conditioners. If the air conditioners are sold to impermissible places, the manufacturer can know the location and serial number of the air conditioner  and  punish the corresponding sales agent.

### A SIM card will be embedded in the monitoring module to support  the mobile communication.  To reduce the subscription cost of mobile network service, the air conditioner manufacturer intends to only active the mobile network service (i.e. active the embedded SIM card) when the air conditioner is in use. Therefore, the monitoring module should be able to trigger the activation of the SIM card. On the other hand, the manufacturer also has the requirement to remotely trigger the deactivation of the SIM card via M2M platform when he does not need monitoring the air-conditioner.

## Source (as applicable)

## Chinaunicom

## Actors (as applicable)

### Mobile network operator

### Air-conditioner  manufacturer application server

### M2M platform

### Air-conditioner monitoring module

## Pre-conditions (if any)

### The mobile network operator opens the service interface for remotely changing the state (e.g. card information, association relationship with mobile number) of target SIM cards. This interface can support the activation and deactivation of SIM cards.

### The mobile network operator opens the service interface for device locating.

## Triggers (if any)

### The following triggers could initiate exchange of information.

### The air-conditioner monitoring module initiates the activation request (Trigger A). In this case, the air-conditioner is in use, and the monitoring module intends to active the SIM card and report location information to manufacturer.

### The manufacturer application server initiates the deactivation request (Trigger B). In this case, the manufacturer does not need monitoring the air-conditioner for a long time, and intends to terminate the usage of the SIM card in target monitoring module via M2M platform.

### The manufacturer application server initiates the activation request (Trigger C). In this case, the manufacturer needs to confirm the location of the air-conditioner again, and intends to active the SIM card in target monitoring module via M2M platform.

## Normal Flow (as applicable)

### SIM card activation  (Trigger A)

### The air-conditioner monitoring module initiates the activation request to M2M platform.

### The M2M platform uses the SIM card activation capability provided by the mobile network operator to active the SIM card in corresponding monitoring module and feedback the activation information to monitoring module.

### The monitoring module collects the location information using the locating capability provided by underlay network and reports the location information to manufacturer application server.

### SIM card deactivation (Trigger B)

### The manufacturer application server initiates the deactivation request to M2M platform.

### The M2M platform uses the SIM card deactivation capability provided by the mobile network operator to terminate the usage of the SIM card in target monitoring module and feedback the deactivation information to manufacturer application server.

### SIM card activation  (Trigger C)

### The manufacturer application server initiates the activation request to M2M platform.

### The M2M platform use the SIM card activation capability provided by the mobile network operator to active the SIM card in corresponding monitoring module and feedback the activation information to manufacturer application server.

### The manufacturer application server wakes the monitoring module.

### The monitoring module collects the location information using the locating capability provided by underlay network and reports the location information to Manufacturer application server.

## Post-conditions (if any)

## High Level Illustration (as applicable)

## Potential requirements (as applicable)

### The M2M systems shall support the capability of  reusing the SIM card activation and deactivation capability in underlay network.

### The M2M system shall support device addressing mechanism.

### The M2M system shall support the capability of  reusing the locating capability in underlay network.

### The M2M system shall support the devices to report their location and other privacy information .