| Input contribution Use case |
| --- |
| Use Case Title:* | Electric bicycle Anti-theft |
| Group Name:* | WG1 |
| Source:* | Chinaunicom |
| Contact: | Junling Mao (maojl11@chinaunicom.cn) Peng Wang (wangpeng@chinaunicom.cn) Changwei Hu (hucw5@chinaunicom.cn) |
| Date:* | 2014-3-27 |
| Abstract:* | A user case named “electric bicycle anti-theft” is described in this document, which involves a new requirement that the M2M systems shall support the capability of reusing the SIM card activation and deactivation capability in underlay network.. |
| Agenda Item:* | TBD |
| Work item(s): | TBD |
| Document(s) Impacted* | TBD |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Discussion and initial agreement for potential network API over mcn |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Title

### Electric bicycle anti-theft

## Description

### Anti-theft modules are integrated in several types of electric bicycles to monitor the location of electric bicycles. If the users cannot find their electric bicycles, they can use their mobile terminal to send a request to anti-theft application server to get the location of their electric bicycles, or remotely trigger the alarm of anti-theft module.

### A SIM card and 2G celluar module will be embedded in the anti-theft module to support the mobile communication, which is designed to be unreachable for safety considerations. For reducing cost, the SIM card is generally not activated when the electric bicycle leaves factory, When the electric bicycle is sold, the owner can active the SIM card via anti-theft application server if he wants to use the anti-theft function. On the other hand, the owners also have the requirement to deactivation of the SIM card if they do not need the anti-theft function.

## Source (as applicable)

## China Unicom

## Actors (as applicable)

### Mobile network operator

### M2M platform

### Anti-theft module

### Anti-theft application server

### User terminal

## Pre-conditions (if any)

### The mobile network operator opens the service interface for remotely changing the state (e.g. card information, association relationship with mobile number) of target SIM cards. This interface can support the activation and deactivation of SIM cards.

### The mobile network operator opens the service interface for device locating.

### The mobile network operator opens the service interface for device triggering.

## Triggers (if any)

### The following triggers could initiate exchange of information.

### The user terminal initiates the activation request (Trigger A). In this case, the electric bicycle is in use, and the user intends to active the SIM card.

### The user terminal initiates the deactivation request (Trigger B). In this case, the user intends to terminate the anti-theft function of electric bicycle.

### The user terminal initiates the locating request (Trigger C). In this case, the user intends to get the location of the target electric bicycle.

### The user terminal initiates the alarm request (Trigger D). In this case, the user intends to trigger the alarm of the target electric bicycle.

## Normal Flow (as applicable)

### SIM card activation  (Trigger A)

### The user terminal module initiates the activation request to anti-theft application server.

### The anti-theft application server forwards the activation request to M2M platform.

### The M2M platform uses the SIM card activation capability provided by the mobile network operator to active the SIM card in corresponding electric bicycle anti-theft module and feedback the activation information to anti-theft application server.

### The anti-theft application server forwards the activation information to user terminal.

### SIM card deactivation (Trigger B)

### The user terminal initiates the deactivation request to anti-theft application server.

### The anti-theft application server forwards the deactivation request to M2M platform.

### The M2M platform use the SIM card deactivation capability provided by the mobile network operator to terminate the usage of the SIM card in target electric bicycle anti-theft module and feedback the deactivation information to anti-theft application server.

### The anti-theft application server forwards the deactivation information to user terminal.

### Remote locating (Trigger C)

### The user terminal initiates the locating request to anti-theft application server.

### The anti-theft application server forwards the locating request to M2M platform.

### The M2M platform use the locating capability provided by the mobile network operator to locate the target electric bicycle anti-theft module and feedback the location information to anti-theft application server.

### The anti-theft application server forwards the location information to user terminal.

### Remote alarm (Trigger D)

### The user terminal initiates the alarm request to anti-theft application server.

### The anti-theft application server forwards the alarm request to M2M platform.

### The M2M platform uses the device triggering capability provided by the mobile network operator to trigger the device and forwards the alarm request to the target electric bicycle anti-theft module.

### The target electric bicycle anti-theft module starts the alarm function.

## Post-conditions (if any)

## High Level Illustration (as applicable)

## Potential requirements (as applicable)

### The M2M systems shall support the capability of  reusing the SIM card activation and deactivation capability in underlay network.

### The M2M systems shall support the capability of  reusing the locating capability in underlay network.

### The M2M systems shall support the capability of  reusing the device triggering capability in underlay network.

### The M2M system shall support the remote device control mechanism.