| Input contribution Use case |
| --- |
| Use Case Title:* | Underlying network service activation and deactivation |
| Group Name:* | WG1 |
| Source:* | ChinaUnicom |
| Contact: | Junling Mao (maojl11@chinaunicom.cn) Peng Wang (wangpeng@chinaunicom.cn) Changwei Hu (hucw5@chinaunicom.cn) |
| Date:* | 2014-5-26 |
| Abstract:* | A user case named “underlying network service activation and deactivation” is described in this document, which involves a new requirement that the M2M systems shall support the capability of reusing the network service activation and deactivation capability in underlying network. |
| Agenda Item:* | TBD |
| Work item(s): | TBD |
| Document(s) Impacted* | TBD |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Discussion and initial agreement for potential network API over mcn |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Title

### Underlying network service activation and deactivation

## Description

### Background of the use case

### Since the network APIs defined by OMA and GSMA generally focus on the requirements of OTT applications,  these network APIs do not include the network API for underlying network service activation and deactivation. Currently, for flexible M2M service deployments and low network service subscription cost, some underlying network operators have developed their private network service activation and deactivation APIs and opened them to M2M application providers. The M2M systems may need to transform these private network APIs to uniform format and open for M2M applications.

### Overview of  the use case

### In the M2M device, a network service module (e.g. SIM card ) will be embedded to support  the network communication. For some potential requirements, the network service module need be activated or deactivated  by remote or local M2M applications via M2M platform.

### In the context of this use case, an active network service module means that the network service module enables the M2M device to send / receive M2M traffic from the M2M Application server. An inactive network service module does not allow the M2M device to send / receive M2M traffic, however the service module, together with the M2M device, is capable to exchange signaling with the operator’s M2M platform

### The following scenarios are given to show above requirements.

### Factory acceptance test

### During the factory acceptance test of the M2M device, the network service module need be activated for M2M service testing. After the test, the network service module need be deactivated for saving the network subscription cost.

### Starting usage

### When the M2M device are sold and the user starts to use it, the network service module need be activated to support the M2M service. The network service module may be activated via M2M platform by local M2M applications in the case that the local M2M applications detects the M2M device in use or by remote M2M applications in the case that the user requests the M2M application server to active the M2M device.

### Abandon

### When the M2M device is abandoned by user, the network service of the M2M device need to be deactivated for reducing network service subscription cost. In this case, the network service module will be deactivated via M2M platform by remote M2M applications.

### Lost

### When the M2M device is lost or stolen, the network service of the M2M device need be deactivated for reducing network service subscription cost. In this case, the network service module will be deactivated via M2M platform by remote M2M applications.

### Abused

### When the M2M device is misused by user (e.g. used for certain forbidden services), the remote M2M application server intends to stop providing M2M service and deactivate the network service of target M2M device via M2M platform.

### Similarly, if a M2M device is used outside a specific geographic area in which the M2M device is supposed to operate (e.g. a vending machine is removed from its assigned place) then a location enabled M2M device may deactivate the network service module.

## Source (as applicable)

## China Unicom

## Actors (as applicable)

### Underlying network operator

### M2M Application server (operated by a M2M Application Service provider)

### M2M platform (operated by the Underlying network operator)

### M2M device (containing a network service module)

### Network service module (operated by the Underlying network operator)

## Pre-conditions (if any)

### The mobile network operator opens the service interface, i.e. network API, for remote activation and deactivation of underlying network service.

## Triggers (if any)

### The following triggers could initiate exchange of information.

### Trigger A:

### The M2M application on M2M device initiates the activation request. In this case, the M2M device is in use, and the M2M application intends to activate / deactivate the network service of the corresponding M2M device via an M2M platform.

### （Note that even if the network service of the M2M device is deactivated,  the M2M device may still be able to connect to target M2M platform  according to the policy of  network operator. ）

### Trigger B:

### The M2M application server initiates the activation request. In this case, the M2M application intends to activate / deactivate the network service of the target M2M device via M2M platform.

## Normal Flow (as applicable)

### Network service activation  by local M2M application on M2M device (Trigger A)

### The M2M application on M2M device initiates the activation request to M2M platform.

### The M2M platform uses the network service activation capability provided by the underlying network operator to active the network service of the corresponding M2M device and feedback the activation information.

### Network service activation by remote M2M application (Trigger B)

### The M2M application server initiates the activation request to M2M platform.

### The M2M platform uses the network service activation capability provided by the underlying network operator to activate the network service of target M2M device and feedback the activation information to the M2M application server.

### Network service deactivation by remote M2M application(Trigger B)

### The M2M application server initiates the deactivation request to M2M platform.

### The M2M platform uses the network service deactivation capability provided by the underlying network operator to deactivate the network service of target M2M device and feedback the deactivation information to the M2M application server.

## Post-conditions (if any)

## High Level Illustration (as applicable)

## Potential requirements (as applicable)

### The M2M systems shall support the capability of  reusing the network service activation and deactivation capability in underlying network.

### .